## Slide 1: The Role of Wastewater Treatment in Protecting Water Supplies Against Emerging Pathogens
Christopher S. Crockett, Ph.D., P.E.
Manager of Watershed Protection
Office of Watersheds
Philadelphia Water Department

## Slide 2: Past Microbial Understanding
Dilution will reduce receiving water concentrations of pathogens below effect thresholds
Microbes do not survive well in the environment
Meeting regulatory permit limits addresses microbial risks sufficiently to downstream users and water supplies
Removal of microbes by downstream water suppliers is easier and better
Exposure to large doses of microbes is required for infection

## Slide 3: Changing Microbial Reality
Our Knowledge of Microbes Is Changing
  Emerging pathogens are resistant to removal and disinfection by conventional water and wastewater treatment
  Traditionally defined “well treated” wastewater effluents can contain significant amounts of infectious and viable pathogens
World’s Population Changing
  Growing immunosuppressed and immunocompromised populations
Global Environment Changing
  Global climate change/variability (temp, rainfall)
  Watershed land use changes from development
  Water quantity changes – less dilution (effluent dominant)
  Microbial population and behavior changes

## Slide 4: Emerging Diseases Worldwide
Source: C. Haas

## Slide 5: Health Effects of Emerging Pathogens
No longer just stomach illness and diarrhea
Can have severe health effects on the general population and specific subpopulations
Infection can result in a variety of chronic diseases including:
  hepatitis, myocarditis, insulin dependent diabetes, aseptic meningitis, and ocular and respiratory infections
Kidney failure and death can occur for certain pathogens and certain subgroups

## Slide 6: Emerging Pathogens Detected In Raw Sewage or Wastewater Effluents
Type | Organism | Author
bacteria | Helicobacter pylori | Lu, 2002
enterovirus | adenovirus 40 41 | Enriquez, 1995
enterovirus | Calicivirus | Smith, 1998
enterovirus | Calicivirus (astrovirus) | Nadan, 2003
enterovirus | coxsackievirus | Sedmak, 2003
enterovirus | Echovirus | Sedmak, 2003
enterovirus | Hepatitus E | Pina, 1998
enterovirus | Rotavirus | Villena, 2003
protozoa | Cryptosporidium | Crockett, 1995
protozoa | Cyclospora cayetanensis | Sturbaum, 1998
protozoa | Giardia | Crockett, 1995
protozoa | Toxoplasma gondii | Miller, 2002

## Slide 7: Changing Microbial Reality
Regulations & Regulatory Process Changing
  SDWA & CWA connections
  TMDLs
  Emerging contaminants
Technology Changing
  new technologies that allow the ability to detect viable and infectious emerging pathogens
Costs & Consequences of Regulatory Compliance Is Changing
  No silver bullets
  Effective treatment technologies are expensive (residuals, energy)
  Unintended consequences of compliance for one contaminant causes problem with another

## Slide 8: Changing Public Reality
Public Communication & Expectations Changing
  Complex issues
  Greater media coverage
  More public outreach and education
    Consumer Confidence Reports, Public notifications
  Increased public awareness
    People now realize safe water does not mean 100% contaminant free water
  Public expects water to be “safe”
  How can water be “safe” if emerging contaminants are there
  Changing consumer attitudes
    Bottled water, etc.
  Public Recreation in water supply areas

## Slide 9
www.phillyrivercast.org

## Slide 10: New Microbial Strategies
Focus on individual microorganisms as a control strategy is counterproductive
Look for common approach in managing the spectrum of emerging contaminants
  Potentially also suitable for deliberately introduced threats as well

## Slide 11: Role of Multiple Barriers
the lesson of multiple barriers
  the more hurdles we place in between microorganisms and people, the lower the risk
  and these barriers must be reliable
  as “natural” barriers (distance, time, etc.) diminish, “engineered” barriers must increase
Source protection
Particle removal
Disinfection
Distribution management
Source: C. Haas
Wastewater Treatment
Disease in Population

## Slide 12: Drinking Water Treatment Removal of Emerging Pathogens
Physical removal - 0.5 to 2.6 log
  depending on the pathogen
Data suggest that even rigorous conventional water treatment processes will still have difficulty achieving over 2 log removal (>99%) of emerging pathogens on a routine basis

## Slide 13: Wastewater Treatment Removal of Emerging Pathogens
Biological treatment achieved approximately 2 log (99%) reduction of enteric viruses, bacteria, and indicators, but was only able to achieve 1 log reduction of Cryptosporidium

## Slide 14: Wastewater Plant Removal & Inactivation of Pathogens Scenarios
Conventional Plant
Crypto < 2 log
Adenovirus < 2 log
Add Tertiary Treatment and UV Disinfection
Crypto > 6 log
Adenovirus 3.2 log

## Slide 15: Optimization to Remove Emerging Pathogens
Beyond new processes, an operator could
use sequential UV light and chlorine disinfection more effectively
increase MCRTs and MLSS
improve the removal an any filtration processes if they are used to optimize their current processes.

## Slide 16: Pathogen Survival
Using the varying decay rates published for various bacteria, viruses, and protozoa
under specific conditions
it can take more than 3 weeks for 90% of the organisms to die off

## Slide 17: Time for 90% Die-Off of Pathogens in Water
Note: Helicobacter pylori can survive 30 days, Crypto > 100 days

## Slide 18: Downstream Travel Ranges of Pathogens
Conservative estimates using a maximum survival of 5 days
  90% die-off of bacteria and viruses after 32 to 64 km (20 to 40 mi) travel downstream from the wastewater plant.
Wastewater utilities that are within this 32 to 64km (20 to 40 mi) distance should consider
  participating in any water supply early warning or notification systems if they are available so that downstream water suppliers are warned of conditions that could create unusual challenges to the water treatment process.
  Community disease surveillance & tracking

## Slide 19: How Do We Develop Standards & Approaches
Risk based approaches have been and will most likely be the starting point
Microbial risk assessment is a developing field with as many unknowns as cancer risk assessment

## Slide 20: Risk Based Intake Water Thresholds
Organism | Type | Average finished drinking water conc. (#/L) | Average log water treatment removal & inactivation | Estimated average intake water concentration threshold (#/L)
Entamoeba coli | Bacteria | 0.000000625 | 5 (99.999%) | 0.0625
Salmonella | Bacteria | 0.0013 | 5 (99.999%) | 130
Cryptosporidium | Protozoa | 0.003 | 3 (99.9%)** | 0.075*
Giardia | Protozoa | 0.00000675 | 5 (99.999%) | 0.675
Echovirus 12 | Virus | 0.0000685 | 5 (99.999%) | 6.85
Polio I | Virus | 0.0000151 | 5 (99.999%) | 1.51
Polio I | Virus | 0.00191 | 5 (99.999%) | 191
Polio III | Virus | 0.000000265 | 5 (99.999%) | 0.0265
Rotavirus | Virus | 0.000000222 | 5 (99.999%) | 0.0222

## Slide 21: Crypto Case Study
Applies the previous techniques into one example that takes into account
Levels reported in effluent in studies
Removal / inactivation by wastewater treatment
Survival and downstream travel ranges
Intake concentration estimates compared to risk based thresholds for drinking water

## Slide 22: Reported Concentrations of Cryptosporidium in Wastewater Effluent
LT2 Cutoff
Potential Effluent Limit

## Slide 23: Ranges of STP Discharge & Streamflow: LT2ESWTR Thresholds
Intake has Bin 2 Potential
Intake has outbreak Potential
5.2 MGD
52 MGD
0.5 MGD

## Slide 24: Crypto findings
A wastewater discharge to streamflow ratio of 0.82 and 8.2%, respectively could result in a potential for downstream intakes to exceed the regulatory requirement for LT2ESWTR
Very possible in developed and effluent dominant watersheds

## Slide 25: Some take home messages
It’s not just coliforms anymore
Pathogen contamination and control can use tools and techniques modifed from chemical control
Cooperation between researchers, utilities and the public health community is needed -- particularly for informing risk-based decision making

## Slide 26: Conclusions
The current regulatory approaches and traditional industry practices need to be revised to include strategies that mitigate emerging pathogen effects on receiving bodies.
Meeting the traditional regulatory standards based on indicator organisms may not be sufficient to mitigate emerging pathogen effects
Raw and treated wastewater represent a significant source of emerging pathogens that has the potential to adversely affect downstream drinking water supplies.

## Slide 27: Conclusions
Discharges of emerging pathogens from wastewater treatment plants has the potential to…
  reach a water supply intake in a viable state at concentrations that could exceed regulatory limits
  increase endemic risk from drinking water
  require additional drinking water treatment
To mitigate these effects, a variety of wastewater treatment processes can be used and optimized to achieve up to 6 log of combined removal and inactivation of emerging pathogens

## Slide 28: Wastewater Industry Recommendations
Industry must consider new strategies to address the challenges represented by discharging emerging pathogens to downstream water supplies and recreational areas and be provided the regulatory flexibility to implement these strategies.
Consider expanding the treatment process beyond secondary treatment and using multiple processes and techniques to address emerging pathogens while meeting other future regulatory requirements.
  The combination of UV light disinfection and sand or membrane filtration is one example.

## Slide 29: Water/Wastewater Industry Synchronization & Trading
Upstream STP cannot remove all parameters equally and effectively
Downstream WTP cannot remove all parameters equally and effectively
If upstream STP can remove certain X parameters more effectively and the downstream WTP can remove Y parameters more effectively, then a balance can be struck between the two.
However the shifting landscape of parameters and limits requires constant communication/negotiation
Concept works for 1 STP and 1 WTP, gets very complicated for multiple STPs and WTPs in a watershed
The TMDL approach could allow for watershed based permitting and effluent trading to provide incentive for creative approaches but regulatory agencies must be willing to utilize a new approach

## Slide 30: Final Thoughts
Reason for Drinking Water Treatment and Wastewater Treatment is to Protect Public Health
The Microbial challenge is real
Everybody pay’s somehow
Regulatory process as it is, has a tendency to divide the water and wastewater industry instead of unite it
First step is communication

## Slide 31: QUESTIONS ???