## Slide 1: WATER ENVIRONMENT RESEARCH FOUNDATION Wet Weather Effluent Blending Project WERF Project No. 03-CTS-12PP
David R. Williams
Director of Wastewater
East Bay Municipal Utility District
Pathogen Management Panel Discussion
2006 NACWA Summer Conference
Seattle, WA
July 21, 2006

## Slide 2: Presentation Outline
Project Background
Regulatory Perspective
Project Approach
Preliminary Results
Next Steps

## Slide 3: What is Blending?
EBMUD Main WWTP Blending at Peak Flow = 415 MGD
The practice of diverting a part of peak wet weather flows to WWTPs around biological treatment units and combining effluent from all processes prior to discharge from a permitted outfall.

## Slide 4: Project Background
EBMUD awarded $585,000 under research agreement with WERF; $400,000 awarded under original agreement (December 2004)
EBMUD directing work of nine subcontractors and participating as field test site
Pilot project under WERF’s Public Participation program
  Expanded WERF Project Subcommittee
  Stakeholder involvement in project oversight

## Slide 5: WERF Project Subcommittee Members
Mike Sweeney, PSC Chair, Research Council Liaison (EMA)
Karl Boone (ADS Environmental Services)
Tom Brueckner (Narragansett Bay Commission)
Mike Connor (San Francisco Estuary Institute)
Alfred Dufour (US EPA)
Charles Gerba (University of Arizona)
Carol Hufnagel (Tetra Tech)
Michele Pla (Bay Area Clean Water Agencies)
Kellogg Schwab (Johns Hopkins University)
Mic Stewart (Metropolitan Water District of Southern CA)

## Slide 6: Regulatory Perspective
In November 2003, EPA issued draft guidance regarding blending practices at municipal WWTPs serving sanitary sewer systems
EPA received over 98,000 public comments and opposition from Congress; draft guidance shelved in May 2005
In October 2005, the Natural Resources Defense Council (NRDC) and the National Association of Clean Water Agencies (NACWA) submitted joint policy recommendations to EPA
In December 2005, EPA issued draft policy on permit requirements for peak wet weather discharges from WWTPs serving sanitary sewer systems

## Slide 7: Project Approach
Compare final effluent and receiving water quality during blending to baseline conditions—dry weather and wet weather non-blending
  EBMUD Main Wastewater Treatment Plant (MWWTP) – SSO
  City and County of San Francisco (CCSF) Southeast Water Pollution Control Plant (SEWPCP) – CSO
  Public Health Focus: Pathogens and indicator organisms in final effluent; primarily indicator organisms in SF Bay (some limited pathogen testing)
Use 2-D hydrodynamic, water quality transport model to estimate pathogen and indicator organism concentrations in SF Bay under each scenario

## Slide 8: Project Approach (cont’d)
Estimate incremental risk to public health, if any, attributable to blending practices
  Static model using Monte Carlo simulation to conduct comparative screening level risk characterization
Develop alternatives to blending practices and estimate incremental benefits to public health

## Slide 9: Planned Field Sampling Events
EBMUD/CCSF: 7 of 16 field sampling events planned for 2005-06 (Year 1) and 2006-07 (Year 2) wet weather seasons have been completed
 | Year 1 |  | Year 2 |  | Total | 
Condition | EBMUD | CCSF | EBMUD | CCSF | EBMUD | CCSF
Dry Weather | 1 | 1 | 1 | 1 | 2 | 2
Wet Weather Non-blending | 2 | 1 | 4 | 5 | 6 | 6
Wet Weather Blending | 4 | 5 | 4 | 3 | 8 | 8
Total | 7 | 7 | 9 | 9 | 16 | 16

## Slide 10: Field Sampling Locations and Analysis
Primary effluent (prior to disinfection during blending), Final effluent (after disinfection) – single grab samples
  Giardia
    enumeration, characterization (FE only) – estimate of intact cysts
  Cryptosporidium
    enumeration, infectivity (FE only)
  Adenovirus, Enterovirus
  Fecal coliform, E. coli, enterococcus, male specific coliphage
  cBOD5, TSS, VOCs, metals
San Francisco Bay (3 locations)
  Fecal coliform, E. coli, enterococcus, male specific coliphage
  Limited Giardia and Cryptosporidium testing (4 of 16 events)

## Slide 11: SF Bay Field Sampling Locations
CCSF SEWPCP
EBMUD MWWTP
Oakland
Alameda
San Francisco
Treasure Island
San Francisco Bay
Up-current
Outfall
Down-current
Up-current
Down-current
Flood Tide
Outfall
Locations
  Outfall (midpoint of diffuser section)
  One nautical mile “Up-current”
  1/2 nautical mile “Down-current”
Single grab sample at each location during each event
Up- and down-current locations are dependent on tide direction

## Slide 12: Presentation Outline
Project Background
Regulatory Perspective
Project Approach
Preliminary Results
Next Steps

## Slide 13: EBMUD Final Effluent Giardia and Cryptosporidium Results
Giardia
  Higher during WW than DW
  “Intact” cysts at 30–48% of total
Crypto
  Higher during WW non-blending than blending
  All infectivity results below MDL (1 oocyst/L)
Error bars represent maximum and minimum values.

## Slide 14: EBMUD Primary and Final Effluent Adenovirus and Enterovirus Results
Adenovirus
  Final effluent values significantly higher during blending
Enterovirus
  All final effluent values at or below MDL (1 PFU/L)
Error bars represent maximum and minimum values.

## Slide 15: EBMUD In-plant and Receiving Water Fecal Coliform Results
Highest final effluent result during DW
Highest outfall and down-current results measured during blending; still low and higher than FE results
Similar results for E. coli
Error bars represent maximum and minimum values.
Pre-1986 EPA Recommended Limit for Beaches =
200 MPN/100 mL (geo. mean)

## Slide 16: EBMUD In-plant and Receiving Water Enterococcus Results
Final effluent results slightly higher during WW non-blending vs. blending
Highest receiving water results measured during blending; similar to WW non-blending
Error bars represent maximum and minimum values.
EPA Recommended Limit for Beaches = 104 CFU/100 mL
(single sample)

## Slide 17: EBMUD In-plant and Receiving Water Male Specific Coliphage Results
Final effluent results were lower during blending vs. WW non-blending events
Receiving water results were also lower during blending vs. WW non-blending events
Error bars represent maximum and minimum values.
MDL during DW event

## Slide 18: Next Steps
Year 2 Field Sampling (Sep 06–Apr 07)
  Expand in-plant sampling at EBMUD/CCSF to include influent, secondary effluent, and downstream of blending point locations (additional funding provided by US EPA)
  Add Milwaukee Metropolitan Sewerage District Jones Island WWTP and Eugene/Springfield WPCF (Oregon) as field test sites (field sampling only)
Conduct water quality transport and hydrodynamic computer modeling to estimate pathogen and indicator organism concentrations in SF Bay
Conduct risk assessment and develop blending alternatives

## Slide 19: WERF Wet Weather Effluent Blending Project Questions?
David R. Williams
Director of Wastewater
East Bay Municipal Utility District