## Slide 1: Emerging Contaminants: Will they be regulated, and if so, how?
Amy Woodis, Metro Wastewater
Pat Nelson, CH2M Hill
NACWA Summer Conference
July 2006

## Slide 2: What are Considered to be Emerging Contaminants?
Endocrine disrupters (mimic natural hormones)
Pharmaceuticals and Personal Care Products (human & veterinary drugs, fragrances, sunscreens, supplements, etc.)
Industrial and Household Chemicals (flame retardants, plasticizers, etc.)

## Slide 3: Why does Metro care about this?

## Slide 4: Metro & Front Range Considerations
Public perception is: “There may be problems”
Metro is the largest wastewater facility in the state of Colorado
Metro is located on the edge of the plains, at the “bottom” of significant topographic changes
Front Range cities are water-limited
  Water development projects in the South Platte basin are underway
  Water reuse is common (reclaimed water and reuse)

## Slide 5: Possible Regulatory Approaches for Emerging Contaminants
Through Safe Drinking Water Act
  Human health-based considerations
Through Clean Water Act
  Aquatic life-based criteria
  Protection of drinking water supplies

## Slide 6: Establishment of Drinking Water Criteria by EPA (SDWA)
Based on:
  Peer-reviewed epidemiological studies regarding human health
  Occurrence in the environment
  Human exposure
  Risks of adverse health effects in the general population and sensitive subpopulations
  Analytical methods of detection
  Technical feasibility, i.e., can the limits be met
  Impacts of regulation on water systems, the economy, and public health

## Slide 7: Establishment of Water Quality Criteria by EPA (CWA)
Based on:
  Protection of designated uses
  Human health impacts, e.g., bioaccumulation in people and epidemiological studies
  Degree of environmental attenuation of compounds over time
  Degree of removal in wastewater treatment
  Impacts on aquatic species
Can be numeric or narrative

## Slide 8: Development of State Water Quality Standards
Based on EPA criteria (must be as stringent as EPA)
May be based on site specific information or a different interpretation of study data
May use Best Professional Judgment for Permit Limits
  Based on a review of literature
  Based on evaluation of technology
  Other sources
  Specific regulations that apply to development of BPJ

## Slide 9: Are There Plans for Regulation of ECs by EPA?
ECs could show up on the 2008 drinking water Contaminant Candidate List; next one due to come out in 2006
EPA is not actively developing any water quality criteria for ECs
EPA needs additional funding to perform needed research
EPA must develop meaningful biological endpoints

## Slide 10: Why is EPA not Ready to Develop Criteria for ECs in the Near Term?
Too many compounds to study, much less to develop criteria
New compounds are developed that enter the market all the time
EPA needs to develop the methods to measure toxicity of compounds
Not enough money for the need research
No agreed upon detection levels

## Slide 11: How Could the States or EPA be Pushed to Regulate ECs?
Third party law suit
General public demands action
Downstream water provider concerns
Politics
Regulatory agencies out to “save the environment”
Desire to “do something”

## Slide 12: First Step Would be to Apply Existing Standards
Regulations under the SDWA and the CWA already limit some ECs, specifically endocrine disruptors
Examples:
  Pesticides: atrazine, chlordane, DDT, endrin, lindane, methoxychlor, simazine, and toxaphene
  Nonpesticide organics: benzo(a)pyrene, bis(2-ethyhexyl) phthalate, dioxin, and PCBs
  Inorganic chemicals: cadmium, lead, and mercury

## Slide 13: Human Health Standards Exist for Some ECs (SDWA)
Parameter | MCLG ug/L | MCL ug/L | Lifetime Health Advisory, ug/L | 10E-6 Cancer Risk
Atrazine | 3 | 3 | -- | --
Benzo(a)pyrene (PAH) | -- | 0 | -- | 0.005
Chlordane | 0 | 2 | -- | 0.1
DDT | -- | -- | -- | --
Dioxin (2,3,7,8 TCDD) | 0 | 0.00003 | 0.00004 | 0.0000002
Endrin | 2 | 2 | 2 | 
Ethylhexyl phthalate (BIS-2) | 0 | 6 | -- | 3
Lindane | -- | -- | -- | --
Methoxychlor | 40 | 40 | 40 | --
PCBs | 0 | 0.5 |  | 0.1
Simazine | 4 | 4 | 4 | --
Toxaphene | 0 | 3 | -- | 0.03

## Slide 14: Criteria Already Exist for Some ECs (CWA)
Parameter | EPA Water + Fish, ug/L | EPA Fish Ingestion, ug/L
Atrazine | No Standard | No Standard
Benzo(a)pyrene (PAH) | 0.0038 | 0.018
Chlordane | 0.0008 | 0.00081
DDT | 0.00022 | 0.00022
Dioxin (2,3,7,8 TCDD) | 5.00E-09 | 5.10E-09
Endrin | 0.059 | 0.06
Ethylhexyl phthalate (BIS-2) | 1.2 | 2.2
Lindane | 0.98 | 1.8
Methoxychlor | 100 | No Standard
PCBs | 0.000064 | 0.000064
Simazine | No Standard | No Standard
Toxaphene | 0.00028 | 0.00028

## Slide 15: Implementation of existing criteria could present challenges to dischargers
Colorado Wastewater Utility Council initiated a study on organics and wastewater treatment plants.
Out growth of the water quality standards hearing on organics.
Study Elements
  Data gathered from several WWTPs detected several organics
  Determine levels in possible sources to the stream based on existing data
  Evaluate what addition data will be necessary.
Focused on ethylhexyl phthalate (Bis-2)– an endocrine disrupter. All WWTPs had some level.

## Slide 16: Results of Study Industrial Wastewater Discharges - Bis 2
 | No. of Samples | No. of Detects | % Detects | Minimum (ug/l) | Maximum (ug/l) | Mean (ug/l)
Aluminum Forming | 30 | 28 | 93% | <2 | 300,000 | <13,000
Foundries | 53 | 25 | 47% | 2 | 16,000 | 1,100
Coal Mining | 52 | 36 | 69% | 3 | 11,000 | 940
Rubber Processing | 6 | 6 | 100% | <24 | <4,300 | <880
Auto and other laundries | 10 | 7 | 70% | 22 | 1,000 | 310
Nonferrous Metals Manufacturing | 55 | 34 | 62% | ND | 1,200 | 100
Timber Products Processing | 9 | 9 | 100% | 9 | 300 | 60
Textile Mills | 94 | 75 | 80% | 1 | 760 | 56
Ore Mining and Dressing | 28 | 18 | 64% | NA | 12 | 50
Pulp and Paperboard Mills | 163 | 106 | 65% | ND | 2,500 | 36
Paint and Ink Formulation | 19 | 10 | 53% | <5 | 80 | <18
Coil Coating | 16 | 16 | 100% | 0 | 42 | 14
Photographic Equipment/Supplies | 15 | 14 | 93% | 3.7 | 26 | 13
Information represents data from the USEPA verification program, table provided by Metro District. |  |  |  |  |  | 

## Slide 17: Results of Study Bis 2 Storm Water Concentrations
Location | Land Use | Sample 1 | Sample 2 | Sample 3 | Mean *
Sand Creek Tributary at 34th Avenue and Havana | Industrial | 17 | 26 | 11 | 18.0
South Platte River Storm Drain at 7th Avenue | Industrial | 14 | 23 | 8 | 15
South Platte River Storm Drain at 54th and Steele | Industrial | 30 | 10 | 13 | 17.7
Villa Italia Storm Drain at Newland Street | Commercial | ND | 19 | 11 | 10
Cherry Creek Storm Drain at Colfax Avenue | Commercial | 28 | 76 | 10 | 38
Cherry Creek Storm Drain at University Blvd | Commercial | 25 | 54 | 29 | 36
North Sanderson Gulch Tributary | Residential | 7 | 5 | ND | 4
Shop Creek at Parker Road | Residential | 64 | ND | ND | 21
* The mean is of all samples including non-detects. Non-detects were considered zero for calculating the mean. |  |  |  |  | 

## Slide 18: Wastewater Discharge Concentrations of Bis 2
Parameter | No of Detects | No of Samples | Ave of Detectable Results | Max of Detectable Results | Min of Detectable Results
Metro District | 3 | 31 | 15.7 | 21 | 11
Colorado Springs | 3 | 22 | 23.8 | 57 | 1.5
Centennial WSD | 3 | 7 | 1.02 | 1.5 | 0.65
Centennial has not industrial users
Possible Limits
  MCL = 6 ug/L
  Cancer Risk = 3 ug/L
  Water + Fish = 1.2 ug/L
  Fish Ingestion = 2.2 ug/L

## Slide 19: Conclusions of WWUC Study
There are detectable levels of endocrine disrupting compounds in wastewater, stormwater and industrial discharges.
Insufficient data available in Colorado on water quality levels in the stream.
Suggestion is for additional study including data collection.

## Slide 20: CWWUC Study for BIS-2 and Nonylphenol
Goals is to measure the fate and transport of Bis-2 and Nonyphenol in urban semi arid environments including influent, effluent, and receiving stream.
Members of the CWWUC will sample their own effluent and receiving streams.
CREEC to perform interpretation of data.
Identify possible biological, chemical and physical processes controlling the occurrence and distribution of these compounds.
Report on the study results.

## Slide 21: CWWUC Study for BIS-2 and Nonylphenol
Project initiated in 2006
Field and laboratory work in 2007
Final report completed in 2008
Still waiting approval from CWWUC

## Slide 22: City of Omaha CSO Study
Part of the City’s monitoring of CSOs and their impacts
USGS performing study
Study period is from July 2006 to September 2007
Twice monthly sampling – once during dry weather and once during wet weather

## Slide 23: Monitoring Locations
Sampling sites include:
  14 streams locations
    11 on Papillion Creek
    3 on Missouri River
  CSO Points (11)
  Stormwater (2)

## Slide 24: Omaha CSO Monitoring Plan
74 different organic compounds being analyzed
Examples:
  Bis(2-Ethylhexyl) phthalate
  Caffeine
  Cholesterol
  Cotinine
  4-Nonylphenol, diethoxylates
  Nonylphenol, monoethoxylates
City Contact
  Marty Grate
  email: mgrate@ci.omaha.ne.us
USGS Contact
  Jason Vogel, Lincoln, NE
  Phone (402) 328-4130
  email: jrvogel@usgs.gov

## Slide 25: What other ways could ECs be controlled?
Establish limits as “Less than detection”
  “If there is no known safe limit, make sure that it is not detectable.”
Based on literature review
  Make assumptions based on small amount of research
Require a minimum level of treatment
  Tertiary Treatment
  Reverse Osmosis
Require discharger to perform research to establish limit

## Slide 26: What regulatory controls are in place?
Effluent guidelines
  Establish state of the art treatment based limits
Industrial Pretreatment Program
  Require focused influent sampling
Best Management Practices
  Could be treatment related
Biosolids
  Modify to require types of treatment
  Establish new standards

## Slide 27: What You Can Do?
Public education on the issues
Communicate that effective organic removal in WWTPs generally results in effective EC removal.
Participate in monitoring studies to develop more information.
Encourage pollution prevention measures

## Slide 28: Questions?