## Slide 1: INTERSECTION OF THE CLEAN WATER ACT AND THE SAFE DRINKING WATER ACT
Susan H. Richardson
Kilpatrick Stockton, LLP
1100 Peachtree Street, Suite 2800
Atlanta, GA 30319
404-815-6330
surichardson@kilpatrickstockton.com

## Slide 2: Objectives
Clean Water Act: to restore and maintain the chemical, physical and biological integrity of the nation’s waters.
  Fishable and Swimmable Waters

## Slide 3: Objectives
Safe Drinking Water Act: to protect the nation’s drinking water from harmful biological and chemical contaminants.
  Safe Drinking Water at the Tap

## Slide 4: Crossing Paths
Increasing Demands on Surface Waters
Increasing Quantities of Wastewater Discharges
New Pollutants are Emerging
Overlaps of Clean Water Act and Safe Drinking Water Act

## Slide 5: Increased Opportunities for Cooperation and Collaboration!

## Slide 6: Safe Drinking Water Act 101
Enacted in 1974
Applies to Public Water Systems (“PWS”)
  Either publicly or privately owned.
  Provides water for human consumption.
  Has at least 15 service connections or
  Serves at least 25 individuals at least 60 days/year.

## Slide 7: Safe Drinking Water Act 101
National Primary Drinking Water Standards: Requires compliance with Maximum Contaminant Limits (“MCLs”) or treatment techniques; federally enforceable.
EPA first establishes a Maximum Contaminant Limit Goal (“MCLG”) – level at which no adverse health effect from exposure to contaminant expected.
MCL must be set as close as feasible to the MCLG.
Treatment techniques – utilized when not economically or technically feasible to set an MCL.
National Secondary Drinking Water Standards – Address aesthetic concerns such as taste, color and odor; not federally enforceable.

## Slide 8: 1986 SDWA Amendments
Issue MCLGs and MCLs for 83 contaminants within three years and an additional 25 new contaminants every three years thereafter.
Surface Water Treatment Rule – Required all PWSs using surface water to disinfect.
Total Coliform Rule – Enacted to prevent microbial contamination within a distribution system.

## Slide 9: 1996 SDWA Amendments
Four themes that characterize the 1996 Amendments:
  New and stronger approaches to prevent contamination of drinking water;
  Better information for consumers;
  Regulatory improvements (including better science, prioritization of effort and risk assessment); and
  New funding for states and communities through Drinking Water State Revolving Program.

## Slide 10
The 1996 Safe Drinking Water Amendments establish a strong new emphasis on preventing contamination problems through source water protection and enhanced water system management. That emphasis transforms the previous law, with its largely after-the-fact regulatory focus, into a truly environmental statute that can better provide for the sustainable use of water by our nation’s public water systems and their customers.
U.S. Environmental Protection Agency, 1996

## Slide 11: 1996 SDWA Amendments – New Programs
Source Water Assessment Program
Contaminant Monitoring Programs
  Contaminant Candidate List
  Unregulated Contaminant Monitoring Regulation
  National Contaminant Occurrence Database
Microbial Contamination Programs
  Long Term Enhanced Surface Water Treatment Rule
  Stage 2 Disinfection Byproducts Rule

## Slide 12: Source Water Assessment Program
States required to conduct a surface water assessment program to:
  Delineate the boundaries of areas providing source water for public water systems.
  Identify origins of regulated and unregulated contaminants in delineated area to determine susceptibility of PWS to contaminants.
  Required to be completed by 2003.
  Once completed, results to be made public.

## Slide 13: Source Water Assessment Program: Potential Impacts on Clean Water Organizations
February 8, 2003 Memorandum to EPA Regional Administrations – source water as a top priority.
EPA has indicated that the Source Water Assessments should be used in conjunction with CWA programs such as TMDLs and NPDES permitting.
Potential increased scrutiny on wastewater sources that discharge in vicinity of drinking water source.

## Slide 14: Contaminant Monitoring Programs
1996 Amendments revamped requirements for establishing MCLs
  Eliminated requirement for regulating 25 new contaminants every three years.
  Established requirements for standards to be risk-based, focusing on highest priority chemicals.

## Slide 15: Contaminant Monitoring Programs
Starting in 1991, EPA to implement a cyclical process:
  Review of five contaminants every five years;
  Determine whether to regulate based on three criteria:
    Contaminant adversely affects human health;
    Known or substantially likely to occur in PWSs with a frequency and at levels of public health concern;
    Regulation of contaminant presents meaningful opportunity for health risk reduction.
  If EPA determines to regulate, then EPA has two years to establish MCLG and MCL.

## Slide 16: Contaminant Candidate List
Identifies contaminants not subject to treatment standards but known or anticipated to occur in PWSs and may require regulation.
Three categories:
  Priorities for additional research;
  Priorities for additional occurrence data;
  Priorities for consideration for rulemaking.

## Slide 17: Contaminant Candidate List
1998 CCL – 50 chemical and 10 microbial contaminants.
2005 CCL – 42 chemical and 9 microbial contaminants.
Next CCL – Draft in Winter 2006; final in early 2008; may include pharmaceuticals and personal care products.

## Slide 18: Unregulated Contaminant Monitoring
To develop “occurrence data” for the CCL, PWSs required to monitor water supplies for unregulated contaminants.
Every five years, EPA required to establish list of contaminants and monitoring program.
Data is utilized in evaluating contaminant’s occurrence in drinking water and potential population exposed to each.

## Slide 19: National Contaminant Occurrence Database
Stores data on the occurrence of both regulated and unregulated contaminants.
Utilized by EPA to make occurrence determinations on whether or not to regulate a contaminant.
May also be useful for state tailoring of system monitoring and source water protection.
Must be available to the public in readily accessible form.

## Slide 20: Contaminant Monitoring Program: Potential Impact on Clean Water Organizations
New information is being developed on a large body of contaminants, including some that are subject to water quality criteria or sampling requirements under the CWA.
Combination of occurrence information and information from Source Water Assessment Program may influence effluent limitations and other permitting requirements under TMDL program.

## Slide 21: Microbial Contamination Programs
Greatest area for overlap for wastewater and water utilities.
Historically – CWA and SDWA use differing indicators of contamination and different treatment approaches.
Concerns about future increases in microbial contamination prompts need for more unified approach to addressing microbial contamination.

## Slide 22: New Rules Aimed At Microbial Contamination
January 2006 – EPA finalizes two rules:
  Long Term 2 Enhanced Surface Water Treatment Rule – aimed at reducing risk of Cryptosporidium from entering water supplies.
  Stage 2 Disinfection Byproducts Rule – Requires water systems to limit the amount of disinfection byproducts in drinking water.

## Slide 23: Long Term 2 Enhanced Surface Water Treatment Rule – LT2 Rule
Cryptosporidium are resistant to chlorination and may appear in highest quality source waters.
1. Monitoring Phase – requires PWS to conduct two years of monthly sampling for Cryptosporidium.
  2. Treatment Phase – Based on results of monitoring phase, filtered water systems will be assigned to one of the multiple regulatory “bins.”
Systems that fall into bins requiring higher treatment will be required to implement new treatment and management strategies – potentially significant capital expenditures.

## Slide 24: Potential Impacts on Clean Water Organizations – LT2 Rule
Increased information and potential capital expenditures may push for increased removal at the wastewater treatment facility.
Increased information may have impacts on Cryptosporidium water quality criteria being developed under CWA.

## Slide 25: Stage 2 Disinfection Byproducts Rule– DBP Rule
DBPs may form in drinking water when disinfectants interact with naturally occurring materials; potentially associated with increased cancer, reproductive and other human health risks.
1979 – Total Trihalomethane Rule – interim MCL of 0.10 mg/L as annual average; applied to any community water system > 10,000 people.
1998 – Stage 1 DBP – mandated enhanced coagulation to remove natural organic materials from systems and also set MCL for certain DBPs based on system-wide running annual averages.

## Slide 26: Stage 2 Disinfection Byproducts Rule– DBP Rule
2006 – Stage 2 DBP – Requires PWS to identify locations within distribution system likely to have highest DBP concentration. Locations then used as sampling sites for compliance monitoring; compliance calculated for each monitoring location.
Clean water organizations facing own unique challenges for protecting public from DBPs, prompting need for increased collaboration with drinking water agencies.

## Slide 27: Current Controversies and Emerging Issues
Conflicts over Cryptosporidium Treatment Responsibilities – City of Cincinnati v. Sanitation District No. 1 of Northeastern Kentucky.
Blending and Potential Impacts on Drinking Water.
Pharmaceuticals, Personal Care Products and other Emerging Pollutants.
Effluent Limitation Guidelines for Drinking Water Facilities
Reclaimed Water.

## Slide 28
These changes create an opportunity for conflict.
Yet…
These changes present unique opportunities for collaboration and cooperation between clean water organizations, drinking water organizations and state and federal regulatory agencies.

## Slide 29: We want to stay away from this:

## Slide 30: …and create more of this: