## Slide 1: Efficient Operations Using a Knowledge-Based Support System
Sandeep Karkal, PE
Deputy District Manager-Engineer
Novato Sanitary District
Steven S. Line
President
ICOMMM Inc.

## Slide 2: Background on NSD
Special purpose independent district
Established in 1925
Service area: Novato and portions of northern Marin County
Service population: approx. 55,000
Services offered:
  Wastewater collection, treatment, and disposal
  Refuse disposal, recycling, and green-waste collection through a franchise collector entity

## Slide 3: NSD Facilities -Treatment Plants
Novato Treatment Plant (NTP)
4.53 MGD ADWF
  Upgraded 1984
  Activated sludge secondary, nitrifying biofilter
Ignacio Treatment Plant (ITP)
  1.53 MGD ADWF
  Upgraded 1984
  Trickling filter secondary, nitrifying biofilter

## Slide 4: Collection System
Approx. 230 miles
Size:
  “upper system” - 6” to 24”,
  Interceptors 30” to 48”
System age: 1920s to 1970s, some 1990s
Big picture sizing criteria:
  1950s plan buildout population: 350,000
  1990s plan buildout population: 60,000

## Slide 5: Collection System Past Practices
Maintenance:
    Purely reactive (including run to failure mode)
Response Plan:
    Outside entities reported backups, overflows, or other problems
Record-keeping:
    Paper and Memory Based
      Paper maps
      Individuals in Collection Crews remembered problem areas

## Slide 6: ISSUES
Reactive nature of all work
Age and reliability of existing records
Mindset of collections crews
  Wait for problem to be reported
  Clean areas by memory About five years ago…
  Started recording segment cleaned

## Slide 7: Big Picture for Knowledge Acquisition and Integration
Common Knowledge Management System across Enterprise
Work Management System
  Planning, Scheduling, Tracking and Reporting
Program Management
  SSMP
  FOG
  CIP
Asset Inventory
  Collection System, Pump Stations, Treatment Plants, Fleet
Condition and Risk Assessments
  CCTV Inspections, In-situ conditions
Capacity Assessment
  Flow Modeling
Notes: How Novato Sanitary is currently implementing CMOM.

## Slide 8: Completed: 2004 - 2005
First Phase of Video Inventory of Collection System
Cleaning Scheduling and Recording
Spot Repair
Trunk line Flow Model
Wet Weather Tributary Flow Monitoring
Capital Improvement Planning
SSO Reporting

## Slide 9: Currently in progress
CCTV collection system — 20% this year
Deploying Field Computers
Programming continuing objectives:
  CIP planning
  O&M planning
  Hydraulic analysis
  Color Aerial Orthophoto Integration
  Contour Lines
  Manhole and Pipe Elevations

## Slide 10: Future
CCTV remaining Lines ~80% prioritized as required
FOG program Inspection Scheduler and Tracking
Program Generated Spot Repair Work Orders
Identify Backflow Prevention Locations

## Slide 11: Future
Database for Automated Customer Notification of Lateral Damage or for Accessing Easements
Link service Charge Data to Parcel and Address. Commercial & Residential
Link Permit Card Information to Base Map
GPS Tracking and Reporting of District Collection Crews

## Slide 12: Knowledge Management Architecture
ICOMMM
Knowledge Management
Solution
Work
Management
Hydraulic
Modeling
Program
Management
Planner /
Scheduler
Condition
and Risk Evaluation
Records
Management
Tracking
and Reporting
CCTV
PicAx Video
Asset
Inventory
(GIS)
Notes: How Novato Sanitary is currently implementing CMOM.

## Slide 13: Take it away – Steve!

## Slide 14: Key Objectives of the Knowledge Base System
Provide a common information repository for O&M, Engineering, Planning, and Program Management.
Set goals and track performance
Confidence in resource allocation decision making
Fully Support SSMP, SSO, and other regulatory and management programs reporting functions

## Slide 15: CCTV Inspection Program
Consistency of defect Identification is key
Records structural, operational, and configuration issues
All Inspection records are maintained for analysis and reporting
System Incorporates Damage Severity Index for prioritizing CIP and R&R decisions
Notes: PicAx screen shot

## Slide 16: Asset Inventory GIS Knowledge Base
Develop GIS Based Network of all collection system structures
Each pipe segment and manhole is unique for record tracking
GIS is used as the primary interface for all of the System Modules
Change management and configuration management practices are critical
Notes: Computerized map

## Slide 17: Planning / Scheduling
Planner -
  Assigns Asset Plans to infrastructure components – i.e. cleaning and inspection frequencies
  Incorporates Risk Management – looks at condition, capacity, as well as consequence of failure in planning scenarios.
  Establishes Program Goals – inspection, cleaning and R&R objectives
Scheduler –
  Assigns Work based on plan and daily events
  Levels Assignments based on crew performance and resource availability
  Tracks Progress made against plan as well as amount of reactive maintenance

## Slide 18: Work Management System
Assigns routine scheduled and unscheduled Work Orders
Collects and reports facility specific costs for maintenance and repair activities
Track maintenance history for performance benefits

## Slide 19: Program Management
Asset Management Program
  Condition assessment
  Capacity assessment
  CIP planning
  Life Cycle cost analysis
Sanitary Sewer Management Plan
  FOG
  SSO reporting
  CMOM
  GASB 34

## Slide 20: KM as Basis for Solutions
Performance Basis
  Increase performance through proactive planning and scheduling
  Documented history helps crews plan response requirements
Cost Basis
  Implement Repair / Refurbishment decisions
  Age/condition/capacity replacement solutions
Risk Basis
  Reduce SSO’s through proactive / predictive maintenance practices
  Manage risk through shared knowledge
  Helps build consensus for public outreach and future financing

## Slide 21: Thank You ! Questions