## Slide 1
Information Technology in Wastewater Collection
City of San Diego
NACWA Winter Management Conference
February, 2006

## Slide 2
San Diego’s Metropolitan Area Wastewater System

## Slide 3: San Diego’s Municipal Sewer System
2,897miles of trunk sewers and collection lines
  316 miles of sewer lines in Non-ROW
83 Pump Stations
40 Storm Water Diversion Valves/Pump Stations
Area served: 330 square miles
Number of manholes: 55,043
  5400 manholes in Non-ROW

## Slide 4: San Diego Sewer Rate Increases
Sewer Rate Increases Approved by City Council in October 2001
First 7.5% Increase on March 1, 2002
Second 7.5% Increase on March 1, 2003
Third 7.5% Increase on March 1, 2004
Fourth 7.5% Increase on March 1, 2005
  Current average household monthly bill: $35.17

## Slide 5: EPA Administrative Order
Developed with EPA over 12 month period
Issued by EPA in April 2002
City developed and submitted 13 plans during CY2002
In substantial compliance during CY 2003 and CY 2004
Superseded by Partial Consent Decree

## Slide 6: Partial Consent Decree
Lodged with Court
Duration through June 30, 2006
Full system cleaning and maintenance program
Capital Improvement Program
  Complete awarded projects
  30 miles of pipeline replaced/rehabilitated

## Slide 7: CIP Activities Overview Since CY 01:
Contract CCTV Activities
Sewer Main Replacement/ Rehabilitation
Sewer Modeling

## Slide 8: Sewer CIP Televising Program
Actual Actual Actual Actual Planned Planned CY 2001 CY 2002 CY 2003 CY 2004 CY 2005 CY 2006
Televising 198 408 644 88 77 40
(in miles)

## Slide 9: Sewer Pipeline Replacement/Rehabilitation Program
Actual Actual Actual Actual Actual Actual CY 1999 CY 2000 CY 2001 CY 2002 CY 2003 CY 2004
In Miles 17 14 27 49 44 48
Actual Goal CY 2005 CY 2006
In Miles 37 30

## Slide 10: Summary of Pipe Assessments
 | Original Forecasted Percentage | Assessed To Date | Percentage To Date
Maintenance | 40% | 549 miles | 60.2%
Rehabilitation/ Point Repair | 20% | 226 miles | 24.7%
Replacement | 40% | 138 miles | 15.1%
TOTAL |  | 913 miles | 

## Slide 11: Sewer Modeling:

## Slide 14: O&M Activities Overview Since CY 2001:
Main Cleaning Section Improvements
  Created Canyon subsection
  CMMS Implementations
Planning Section Creation/ Implementation
  Serves Main Cleaning, Pumps, Construction
GPS Implementation

## Slide 15: CMMS Implementation:
Main Cleaning: PS Tools (in-house), Spacient
Pump Stations: EMPAC
FOG: Current legacy system, Developing new in-house CMMS
Construction: Current legacy system (SWIM); developing new in-house CMMS

## Slide 16: CMMS: PS Tools: Grouping Tool
Notes: This shows that red pipes that are getting behind schedule, yellow pipes that are scheduled to be cleaned currently, and some pipes that are scheduled to be cleaned in the near future … all might be within a short drive (block or two) of one another. This reduces driving/“window-time” of crews. Basically, if several pipes on one block need cleaning, and several blocks on the next block over are due for cleaning next week, might as well schedule them both. Then, the crew doesn’t have to drive back there next week. This is done for every ROW cleaning crew, every day.
The dialog box is used by the planner scheduler to generate, track, and manage service requests.

## Slide 17: PS Tools Generates Paper Work Order:
Notes: Paper work order made by PSTools. Info is provided to crews in tabular and graphical format. Most info is collected from crews by means of circling the conditions they found … I.e. circle “MR” for medium roots.

## Slide 18: Main Cleaning Progress: 8700 Miles Cleaned Since CY 02

## Slide 19: Grease-Related Spills in San Diego

## Slide 20: Residential Grease Mailer
Bi-lingual mailer
Sent within 10 days of grease-related spill to neighborhood within 1,000 ft. radius of spill
9,000+ mailed in CY2004

## Slide 21: Grease Education Program FY 2005
Grease Brochures
  150,000 to Rental Mgt. Firms
  20,000 distributed at community fairs, conventions, etc.
  5,000 distributed to Community Service Centers
  2,500 to Mayor & Council offices
  5,000 distributed through MWWD Speakers Bureau
Water/Sewer Bill Inserts
  Twice a year mailing
Grease Education Posters
  Community Service Centers
  City Administration Building Elevators

## Slide 22: Grease Education Program CY 2004-05
TELEVISION
  City TV PSAs and Grease Ed Video broadcast
  MWWD Website
  10 copies of video sent to other municipalities Councilmember Scott Peters Annual Holiday Grease Education Press Conference

## Slide 23
GPS Implementation:
  Import GPS Data into ESRI
    Compare with Scheduled PSTools Data
    Compare with Daily Reports

## Slide 24: Sewer Spills vs Rainfall CY 2000 – CY 2005
Number of Sewer Spills
Rainfall in Inches

## Slide 25: CY 2000 Sanitary Sewer Overflows Total Spills: 365

## Slide 26: CY 2005 Sanitary Sewer Overflows Total Spills: 63

## Slide 27
Questions? Comments?
City of San Diego
Metropolitan Wastewater Department
Wastewater Collection Division