## Slide 1: Issues and Problems with EPA’s New Methodology for Developing Stream Nutrient Standards
William T. Hall
Hall & Associates

## Slide 2: NUTRIENT STANDARD DEVELOPMENT
Nutrients (N, P) not toxic in classical sense
  Do not cause toxic effects directly
  Stimulate plant growth  adverse effects
EPA Nutrient Criteria Guidance (2000)
  Define relationship to plants first
  Relate to macroinvertebrates, fish
ASIWPCA (May 2007)
  Unable to demonstrate necessary relationships

## Slide 3: TIMELINE AND BASIS FOR PA NUTRIENT TMDL ACTIONS
Period | Basis | TP Limits
2000 – 2003 | Dissolved Oxygen Christina River Basin; Wissahickon Creek | ~1.0 mg/L
2004 - 2007 | Nuisance Algae Skippack Creek; Neshaminy Creek; Wissahickon Creek | 0.2 mg/L
2008 | Invertebrates Chester Creek; Indian Creek; Paxton Creek; Sawmill Run; Southampton Creek | ≤0.04 mg/L

## Slide 4: EVOLUTION OF NUTRIENT TMDLs
Long-standing approach
  Model effect of nutrients on plant growth
  Assess plant effect on diurnal DO
  Limit nutrients to control plant growth
Nuisance Algae
  Limit nutrient to prevent nuisance algae (but no standard for nuisance algae)
  Regression approach discredited
Weight of Evidence/Conditional Probability
  Latest approach
  Treats TP as a toxic substance to invertebrates
  Yields extremely restrictive endpoints

## Slide 5: 2008 NUTRIENT TMDLs TP Limit/Reduction Requirements
TMDL | WWTP | MS4
Goose Creek | 0.04 mg/L (>98% reduction) | 53.9% Reduction
Indian Creek | ~0.05 mg/L (90-97% reduction) | 62-70% Reduction
Southampton Ck | 0.08 mg/L (92% reduction) | >90% Reduction
Paxton Creek | CSO Long Term Control Plan | 89% Reduction
Sawmill Run | 98% Reduction from CSOs | 55-96% Reduction

## Slide 6: “WEIGHT OF EVIDENCE” CONDITIONAL PROBABILITY
 | Piedmont | Ridge & Valley | Allegheny Plateau
Reference | 16-17 | 10-15 | 19-36
Literature | 13-100 | 13-100 | 13-100
Stressor Total Taxa EPT Taxa Scrapers/Clingers Dominant Taxa | 36-39, 64 | 14-23 | No Strong Response
Final Endpoint | 40 ug/L | 25 ug/L | 35 ug/L

## Slide 7: WEIGHT OF EVIDENCE
Reference
  Based on distribution
  Unrelated to impairment
Literature
  Mostly reference based
  Other
    Algal growth saturation
    Dodds regression
    New Jersey TDI
    Delaware Criteria
Stressor-Response
  Macroinvertebrates
    EPT Taxa < 8, 10.5, 16
    Clingers < 52.5%
    Scrapers < 7.5%
    Urban Intolerant < 31.5%
    Total Taxa < 19
    Dominant Taxa
  Algae
    Diatom TSI > 4.5

## Slide 8: ISSUES WITH NEW APPROACH
Not consistent with Published 304(a) Criteria
Ignores plant growth
Picks new invertebrate impairment levels
Assumes all invertebrate impairments are due to nutrients
Treats TP like a toxic substance
Conditional probability defines standard

## Slide 10: CONDITIONAL PROBABILITY
Basis: Paul and McDonald (2005)
Paul and McDonald: Must Be Strong Stressor For Method To Be Useful
  It is imperative that extensive laboratory data analysis be conducted to confirm that stressor is highly correlated to the impairment
  Must be a clear, scientifically established causal relationship between pollutant and endpoint
SAB said Conditional Probability not good enough

## Slide 11: CONCERNS WITH EPA APPROACH
Used skewed database to draw conclusions
Purposefully ignored site-specific information contrary to conclusion
Violates “Bedrock” National Criteria Principles

## Slide 12: BEDROCK 304(a) PRINCIPLES
  Set at level necessary and sufficient to protect designated uses
  Must be based on documented dose/ response relationships from lab studies
  Confounded data may not be used
  Site-specific data must be considered
  Sufficient well documented data must exist

## Slide 13: SITE-SPECIFIC DATA

## Slide 14: SITE-SPECIFIC DATA

## Slide 15: IGNORED OTHER FACTORS

## Slide 16: EXPANDED DATABASE WITH USGS MONITORING DATA

## Slide 17: CONDITIONAL PROBABILITY WITH USGS MONITORING DATA

## Slide 18: EXPERT OPINIONS
Dominic Di Toro, Ph.D.
  Conditional probability is not a sufficient basis for establishing water quality standards … it represents a retreat from scientifically defensible criteria
Steven Chapra, Ph.D.
  This is such a scientifically indefensible representation of the connection between nutrients and ecosystem health that I believe that its adoption would represent a grave mistake

## Slide 19: PEER REVIEW JUSTIFICATION
New § 304(a) criteria derivation method
Inconsistent with “Bedrock” 304(a) criteria principles
Precedent setting approach impacts other pollutants
Changes prevailing practices
Significant nationwide impact
Independent experts urge peer review