## Slide 1: Managing Decontamination Wastewater A Utility Planning Tool
Sustainable Systems
AMSA’s 2005 Winter Conference
February 3, 2005
Guy Aydlett: Director of Water Quality, HRSD and Chair, AMSA Pretreatment and Hazardous Waste Committee
Linda Warren: Director of Emergency Response Programs and Project Manager, CH2M HILL
Protecting Wastewater Infrastructure Assets...

## Slide 2
What is Decontamination (Decon) Wastewater ?
For the purpose of this tool….
Wastewater generated as a result of decontamination activities performed after a terrorist attack with chemical, biological or radioactive substances
C B R

## Slide 3
Understanding the Threat
Why the issue of Decon Wastewater is important to utilities:
Worker & System protection
Pass-through & interference
Biosolids contamination/disposal options

## Slide 4
History of the Decon Wastewater Project
Why it began:
  Boca Raton, Florida
  Anthrax Protocol

## Slide 5
About the Tool
Alignment with USEPA and related projects
Evolution of the Decontamination Wastewater Tool
Tool Purpose:
Provide guidance to wastewater utilities to plan for, and react to, a malevolent incident involving CBR agents where decontamination activities may result in such agents entering the sewer system.

## Slide 6
What the Tool won’t cover...
This document does not address malevolent attacks directed at the wastewater system or any other asset owned or operated by the wastewater utility.

## Slide 7
Organization of the Decon Wastewater Planning Tool
Six chapters guide the reader from background on the issue through ways to minimize the threat
Checklist is a quick guide for utility action
References will be available on the AMSA website (www.amsa-cleanwater.org)

## Slide 8
What substances are we concerned about ?
Chemical Agents
Nerve agents
  Sarin
  VX
Blistering agents
  Sulfur mustard
  Lewisite
Blood agents
  Hydrogen cyanide
  Arsine
Choking agents
  Phosgene
  Diphosgene
Industrial chemicals
  Arsenic compounds
  Sodium fluoroacetate
  Orthophosphates

## Slide 9
What substances are we concerned about ?
Biological Agents
Bacteria
  Anthrax
  Plague
  Tularemia
Viruses
  Smallpox
  Hemmorhagic fevers
  Encephalitis
Rickettsiae
  Rocky Mountain spotted fever
  Typhus
Toxins
  Ricin
  Botulinum
  Enterotoxin

## Slide 10
What substances are we concerned about ?
Radioactive Substances
Americium-241
Cesium-137
Cobalt-60
Iodine-131
Iridium-192
Molybdenum-99
Plutonium
Radium-226
Strontium-90
Uranium

## Slide 11
How can these substances enter the sewer system ?
Runoff from decontamination wash-down
Inflow around and through manhole covers
Through catch basin inlets of combined systems
Through a floor drain from interior decontamination

## Slide 12
How can these substances enter the sewer system ?
Decontamination Showers
Mobile
Portable
Fixed

## Slide 13
How can these substances enter the sewer system ?
Direct and intentional discharge by emergency personnel
CBR-exposed persons washing and laundering
Excreta from exposed persons
Disposal of contaminated drinking water from distribution systems and storage tanks

## Slide 14
Minimizing the threat thru Planning, Coordination & Communication
Develop an Emergency Response Plan that includes info related to Decontamination Wastewater:
  Decision-making framework for response
  Procedures for preparedness, response and incident management
  Contact info for agencies to assist and agencies to notify
Within the utility...

## Slide 15
Minimizing the threat thru Planning, Coordination & Communication
Maintain and distribute supplies and equipment to contain decon wastewater
Provide Personal Protective Equipment (PPE)
Develop mutual aid agreements (other utilities, haulers)
Within the utility...

## Slide 16
Minimizing the threat thru Planning, Coordination & Communication
Establish protocols and agreements to assure utility notification
Invite representatives to train with utility staff
Assist with developing procedures and identifying labs for rapid determination of CBR substances
Collaborate in designing methods for containing decontamination wastewater on-site
With emergency managers and first responders ...

## Slide 17
Minimizing the threat thru Planning, Coordination & Communication
Provide information for proper deployment of equipment and materials to prevent decon wastewater from entering sewer system
Encourage the use of a safe tracer dye
Prepare brief instructions ready to give to persons involved in a decon event
  include containment procedures and contact info
With emergency managers and first responders ...

## Slide 18
Minimizing the threat thru Planning, Coordination & Communication
Meet with key customers (hospitals, clinics, laboratories and industry)
Incorporate notification requirement into pretreatment permits
Amend pretreatment regulations to require key customers to develop a plan for containing decontamination wastewater
With customers and agencies that may discharge decon wastewater ...

## Slide 19
Minimizing the threat thru Planning, Coordination & Communication
Work with water utilities to establish decon disposal procedures:
  Isolation
  In-situ treatment
  Temporary storage prior to discharge
With customers and agencies that may discharge decon wastewater ...

## Slide 20
      Minimizing the Threat thru Physical Measures
Barriers
  drain seals, manhole shields, pan inserts, berms and drain plugs
Containment
  sumps, pools, or improvised dikes that retain the runoff; storage and treatment of decon shower water
Sorbents
  gels, foams and solids
Preventing decontamination wastewater from entering the sewer system...

## Slide 21: Mitigating Impacts if decon wastewater reaches the sewer
Chemical agents minimized by calcium hypochlorite, sodium hydroxide or the U.S. Military’s Decontamination Solution No. 2
Many, but not all, bacteria, viruses and toxins can be inactivated with a sufficient contact time with chlorine.
Radioactive materials removed only through advanced treatment (ultrafiltration and reverse osmosis)
Control rate of entry to minimize surges that affect bugs at the plant.

## Slide 22: Minimizing the Threat thru Training and Information Updates
Provide periodic training for utility staff in emergency preparedness, response, and recovery
Test and evaluate emergency plans and procedures through tabletop, functional, and full-scale exercises.
Participate with other utilities, local emergency management agencies, regulators and first responders.
Stay abreast of new legislation and regulations, industry research and newly developed guidance and protocols (visit http://www.amsa-cleanwater.org/advocacy/security/).

## Slide 23
What to do to prepare and What to look for
Contacts (First Responders, Utilities, etc.)
Drills/mock-ups
Facility inspection (mobile & fixed)
Require containment/holding
Follow-up (treatment & disposal)
Lessons learned

## Slide 24
On-going Research and Needs
EPA is working with 15 other agencies on:
1. Protecting physical and cyber infrastructure
2. Identifying drinking water contaminants
3. Improving analytical methodologies and monitoring systems for drinking water
4. Containing, treating, decontaminating, and disposing of contaminated water and materials
5. Planning for contingencies and addressing infrastructure interdependencies
6. Targeting impacts on human health and informing the public about risks
7. Protecting wastewater treatment and collection systems

## Slide 25
Checklist
Provides the reader with a quick reference of key actions to take for decontamination wastewater preparation and response

## Slide 26
For more information
Contact...
Will Pettit
Manager, Regulatory Affairs
AMSA
  (202) 833-3280
  wpettit@amsa-cleanwater.org