## Slide 1
AMSA
February 2, 2005
Dianne Mills, CDM
Rate Structures and Regional Systems
Rates on the Rise-An Inside Look at Rate Setting Studies & Strategies

## Slide 2: Regional Authorities/Organizations
Many Regional Systems are Serving only other governmental bodies
These entities will pay the Regional System- a Wholesale Rate
Generally, only include administration and operation of wastewater conveyance and treatment.
Often established for economies of scale
Introduces a new set of complexities to Rate Setting

## Slide 3: Similarity to Retail Rate Setting
Recover sufficient total revenue to ensure proper operation & maintenance (O&M), development and perpetuation of the system, and preservation of the utility’s financial integrity.
$Maintenance
$Operation
$Capital Costs
$Debt Service

## Slide 4: Differences from Retail Rate Setting
Method of cost distribution is often defined in a legal agreement between regional system and participants served.
Much less customer costs for billing, meter reading and customer service staff
Agreement may sometimes stipulate that certain capital costs are reimbursed separate from user rate.
Distribution method often different for capital and operating and sometimes between participants.
Can be much more distinct for each customer than retail rates where necessity make customer “classes” necessary

## Slide 5: Wholesale Rates Should Fit Situation
Benefits each wholesale customer receives especially in area of capital must be analyzed
Do upgrades or expansions benefit each customer the same?
Were transmission lines installed which benefit only one customer?
Variable charge for treatment tends to be more uniform unless,
Strength of sewer to be treated is a factor, this may influence complexity of rate method
What to do about excessive I/I from participants?

## Slide 6: WSACC Rate Method
Serves 4 towns plus Mecklenburg County
Separated Treatment and Interceptor since all customers did not benefit equally in each component
Treatment Component
  Fixed Component-Capacity Allocation defined in agreement
    Upgrade
    Capital-original debt service
    Expansion
  Variable Component-Flow from 2nd year back

## Slide 7: WSACC Rate Method (Continued)
Interceptor Component
  Fixed Component- Capacity Allocation
    Capital
    Expansion
  Variable Component-Flow from 2nd year back
Some capital projects reimbursed separate from rate since they benefit for example, only the County.

## Slide 8: Broward County North District Regional Wastewater System Rate Method
Treatment and Disposal Component
  Fixed Component- Capacity Allocation from agreement
Transmission Component
  Fixed Component-Capacity Allocation from agreement different from treatment since some users don’t participate in transmission system.
Variable Component allocation based on estimated wastewater flows
Difference is after year end when actual flows are known, the total variable payment is adjusted

## Slide 9: Ft. Worth Wholesale Water Rate Method
Adds another rate component
  Excess Max Day Charge
  Excess Max Hour Charge
Obviously requires more sophisticated computerized metering equipment to produce hourly readings.
Probably would not be needed unless control of demand on water production very important.
Probably not as necessary for wastewater.

## Slide 10: Green Bay Metropolitan Sewerage District Wholesale Methodology
City of Green Bay, other cities and two paper mills
  Paper mills served under separate contract with specific loading and flow limitations
District has multiple metering stations and measures flow and loadings from each mill and municipal customer on a continuous sampling basis.
Monthly flows and loadings are then applied to unit costs to determine bills.
Probably the most accurate method but requires more sophisticated equipment and a very much more complicated rate system.

## Slide 11: Expansion and Rehabilitation CIP
When facilities are expanded determination must made as to who benefits from expansion
  Original agreement must be amended to reflect new guaranteed capacities
  Generally only the debt service on expansion will be subject to new capacity limits
  As with WSACC this requires several allocation bases for debt service
    Original debt service
    New debt issues tied to specific projects
Rehabilitation is generally assumed to benefit all participants equally.
Recommended that how these contingencies should be handled be included in original agreement to make future negotiations simpler

## Slide 12: Rate Methodology Determination
Neither too simple or too complicated for your situation
Consider that some methods like the one for Green Bay require a considerable investment in capital for equipment, maintenance on equipment, etc.
Try to anticipate changes in the future that might impact the rate methodology and incorporate some flexibility