## Slide 1: MIAMI-DADE COUNTY SETTLEMENT WITH FLORIDA DEPARTMENT OF ENVIRONMENTAL PROTECTION RE: INJECTION WELLS Developments in Clean Water Law Seminar November 2004 Henry N. Gillman

## Slide 2
MIAMI-DADE WATER AND SEWER
DEPARTMENT (MDWASD)
SOUTH DISTRICT WASTEWATER
TREATMENT PLANT (SDWWTP)
NOVEMBER 2004

## Slide 3: SDWWTP Fact Sheet
Population Served - 596,609
Service Area - From Flagler to Homestead
Plant - Construction: 1983 - Capacity: 50 MGD
Expansions: 1984 - Capacity: 75 MGD
1994 - Capacity: 112.5 MGD
Current FDEP Rating: 97 MGD
Current Plant Flows: 93 MGD
Wells - No. Constructed: 17
No. Permitted to Operate: 13
No. Monitoring Wells Constructed: 17 Dual Zones
Value of Unusable County Investment: Approx. $32M
SDWWTP to be Expanded to 131 MGD in 2013
  Will meet growth needs through 2020

## Slide 4: MIAMI-DADE WATER AND SEWER DEPARTMENT SOUTH DISTRICT WASTEWATER TREATMENT PLANT
Effluent Treated to Secondary Standards (20/20)
Seventeen Injection Wells Installed (13 in operation)
    Well diameter: 24” (one is 20”)
    Cased depth: 2400-2746 ft
    Total depth: 3054-3193 ft
Seventeen Monitoring Wells Installed
    Well diameter: 6, 12, and 20”
    Monitoring Zones: Upper Floridan at various zones
    (900, 1500, 1800 ft)
Physical Description

## Slide 5
Settling
Tank
Aeration
Tank
Chlorine
Contact
Tanks*
Digester
Grit Chamber
RAS
WAS
Farm
Wells
Waste
Schematic – How Does SDWWTP Work?
Effluent
Pump Station
Drying
*Chlorination only applied for emergency discharge to ponds
O2 Plant

## Slide 6: Wastewater Treatment Levels Achieved
Monitoring Parameter | 2002 Incoming (MG/L) | 2002 Outgoing (MG/L) | Regulatory Requirement
CBOD (MG/L) | 149 | 5 | 20 MG/L Annual Average
TSS (MG/L) | 142 | 10 | 20 MG/L Annual Average

## Slide 7
Drinking Water Parameters | Water Standards Achieved
Inorganic Compounds | 
Disinfection ByProducts | 
Volatile Organic Contaminants | 
Synthetic Organic Contaminants | 
Secondary Drinking Water Standards |  (Except Color & Iron)
Radionuclides | 
Microbiological | Not met – Disinfection not required
Drinking Water Standards Achieved

## Slide 8
Federal SDWA “State underground injection programs shall contain minimum requirements for effective programs to prevent underground injection which endangers drinking water sources…” “…if the presence of such contaminant may result in such system's not complying with any national primary drinking water regulation or may otherwise adversely affect the health of persons.”
Deep Injection Wells Rules & Regulations
Congress
USEPA Rule “…if the presence of such contaminant may result in such system's not complying with any national primary drinking water regulation or may otherwise adversely affect the health of persons…” “…movement of any contaminant…”

## Slide 9
FDEP Rule “No underground injection activity shall be authorized where a Class I or III well causes or allows movement of fluid into underground sources of drinking water, if such fluid movement may cause a violation of any primary drinking water standard under 40 C.F.R. pt. 141 (1994), or may otherwise adversely affect the health of persons…” “…if any water quality monitoring of an underground source of drinking water indicates the movement of injection or formation fluids into underground sources of drinking water, the Department shall prescribe such additional requirements for construction, corrective action (including closure of the injection well), operation, monitoring, or reporting as are necessary to prevent such movement…”
WASD FDEP Issues Permits to Operate WWTP
Deep Injection Wells Rules & Regulations (Continued)
Florida Legislature

## Slide 10: What is the Problem?
In 1994, Ammonia was discovered at 1500 foot depth
At 1500 feet, Ammonia is considered an indicator of the movement of treated wastewater
Treated wastewater is intended to remain in the Boulder Zone, not at 1500 feet
According to USEPA definition, the aquifer at 1500 feet is a potential future water supply source requiring protection
Underground Injection Control rules prohibit movement of fluids into a USDW
Important Facts:
    SDWWTP effluent complies with Primary Drinking Water Standards except for disinfection
    Groundwater at 1500 feet is salty and undrinkable. It contains high Total Dissolved Solids (TDS), Chlorides, and Sulfates

## Slide 11
Lower Floridan
Boulder Zone
Depth
Feet
0
200
400
600
800
1000
1200
1400
1600
1800
2000
2200
2400
2600
2800
3000
3200
3400
Dual Zone
Monitor Well
Injection
Well
Upper
Monitor
Zone
Lower
Monitor
Zone
Biscayne Aquifer
Hawthorn Formation
Floridan Aquifer
USDW 10,000 mg/l
Hydrogeology of SDWWTP

## Slide 12
Injection Well Video

## Slide 13: ELEVATED AMMONIA IN THE 1,500 FOOT MONITORING WELLS SOUTH DISTRICT INJECTION WELL SYSTEM
Scale in Feet
0
300
600
Black Creek Canal
Black Creek Canal
S.W . 97th Avenue
N
LEGEND
Property Border
Existing Pipeline
I-13
I-15
S.W . 232nd Street
I-16
I-14
I-7
I-17
I-8
I-12
I-3
I-2
I-1
I-9
I-10
I-11
I-4
I-5
BZ-1
I-6
WWTP
Effluent Pumping Station
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: AMMONIA AND TKN DETECTED IN 1,500 FOOT MONITOR WELLS ON NORTH SIDE OF SITE
500
1,000
1,500
2,000
2,500
3,000
Injection Well
Monitor Wells
Depth (feet)
Injection Zone
10,000 mg/L TDS
Ammonia and TKN
1,500’ Zone
Sand, Shell, Limestone
Avon Park and Lake City Limestone and Dolomite
Oldsmar Limestone
Suwannee Limestone
Tampa Limestone and Clay
Hawthorn Group
Notes: <number>
<footer>
<header>
<date/time>
4

## Slide 15: ELEVATED AMMONIA IN THE 1,800 FOOT MONITORING WELLS SOUTH DISTRICT INJECTION WELL SYSTEM
Scale in Feet
0
300
600
I-13
I-15
S.W . 232nd Street
I-16
I-14
I-7
I-17
I-8
I-12
I-3
I-2
I-1
I-9
I-10
I-11
I-4
I-5
BZ-1
I-6
Black Creek Canal
WWTP
Black Creek Canal
LEGEND
Property Border
Existing Pipeline
N
Effluent Pumping Station
S.W . 97th Avenue
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: AMMONIA AND TKN DETECTED IN 1,800 FT MONITOR WELLS ON SOUTHEAST SIDE OF SITE
500
1,000
1,500
2,000
2,500
3,000
Injection Well
Depth (feet)
Injection Zone
10,000 mg/L TDS
Monitor Wells
1,800’ Zone
Ammonia and TKN
Sand, Shell, Limestone
Avon Park and Lake City Limestone and Dolomite
Oldsmar Limestone
Suwannee Limestone
Tampa Limestone and Clay
Hawthorn Group
Notes: <number>
<footer>
<header>
<date/time>
4

## Slide 17: Actions Since Ammonia Discovery
1994 - MDWASD Reported Findings. Began negotiations with FDEP and USEPA
1996 - MDWASD Participated in FDEP/USEPA Working Group
1997 - BCC Approved Consent Decree with USEPA
      - Perform Science Based Studies to Determine the Cause of Fluid Movement
      - Total Estimated Cost: $2M
1997 - 2002 - MDWASD Complied with All Requirements of Consent Order (CO)
July 2000 - Draft USEPA Rule Revision Published
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18: Actions Since Ammonia Discovery (Continued)
April 2002 - USEPA Notified MDWASD of Intent to Unilaterally Terminate CO on August 2002
May 2002 - MDWASD Appealed USEPA’s Decision
May 2002 - MDWASD Negotiates with FDEP
July 2002 - BCC Approves MDWASD Draft CO.
August 2002 - CO Terminated by USEPA in August 2002
September 2002 - MDWASD Agrees to Mediation
Oct. 2002 – Feb. 2003 - Mediation Sessions
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: Actions Since Ammonia Discovery (Continued)
January 2003 - USEPA Required to Issue Rule Revision by March 2003
March 2003 - Draft Tentative Agreement
May 2003 - Workshop
May 2003 - GOE Review
May 2003 - USEPA published Relative Risk Assessment of Management Options for Treated Wastewater in South Florida
June 2003 - BCC Review
Summer 2003 - Signed by Parties
April 2004 - Effective Date
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20: New Consent Order Provisions
MDWASD to Perform Pilot Studies, Worse Case Requires Additional Treatment Facilities within 5 Years. Capital Cost Estimated to be $150M
Next Treatment Plant Expansion (to 131 MGD) to Include Wastewater Reuse. Capital Cost Estimated to be Less Than $50M over Approximately 10 Years
County to be the Local Sponsor for the Everglades Restoration Reuse Project to be Further Defined in Approximately 2011
County to Update Wastewater Master Plan
Requirements of Miami-Dade County
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: New Consent Order Provisions (Continued)
15 MGD ( 10 years of growth) of Building Permit Capacity Becomes Immediately Available
USEPA and FDEP Lawsuits Against Miami-Dade County are Averted
Protection of County’s Investment ($32M) in Deep Wells and plant capacity is Assured (continued use of 17 existing wells, and potential upgrade of well capacity)
Peak Flow Issues Including System Storage, Sidestream Treatment, and New Well Construction, are Resolved
No Penalty to be Paid by Miami-Dade County
State to Assist MDWASD Capital Funding with Low Interest Loan
Benefits to Miami-Dade County
Notes: <number>
<footer>
<header>
<date/time>