## Slide 1: Colorado Surface Water Quality Standards for Organics, or: The Potential Consequences of Regulation Without Adequate Information?
AMSA Developments in Clean Water Law Seminar
Amy Woodis, Metro Wastewater
November 2004

## Slide 2: Organics Regulatory Framework
Includes numeric water quality criteria for 154 organic parameters
Are applicable to all surface waters of the state, unless site-specific standards have been adopted

## Slide 3: Organics Regulatory Framework, continued
Aquatic life numeric criteria (acute and/or chronic) have been adopted for 59 of the 154 chemicals
Human health-based criteria (chronic only) have been adopted for 151 of the 154 chemicals

## Slide 4: Organics Regulatory Framework, continued
Human health-based criteria set for:
(1) Water supply-only classification (is unique to this region)
(2) Fish ingestion without water supply classification
(3) “Water + Fish,” e.g., aquatic life segments which also have a water supply classification

## Slide 5: Human Health-Based Organics Criteria
All are based on EPA’s IRIS database and/or EPA lifetime health advisories for drinking water (using 10-6 risk factor)
“Water + fish” and fish ingestion criteria based on revised fish consumption rate of 17.5 grams/day

## Slide 6: September 2004 Rulemaking Hearing
Organic standards were revised to reflect new EPA risk assessment data
A “hybrid” approach was adopted by the Water Quality Control Commission for segments with water supply classification after dischargers questioned why POTWs needed to meet more stringent standards that drinking water treatment plants

## Slide 7: Example: “Hybrid” Approach
Ethylhexyl phthalate (BIS-2)
New water supply standard: 2.5 to 6 ug/L
First number (2.5 ug/L) is risk-based
Second number (6 ug/L) is Maximum Contaminant Level under the Safe Drinking Water Act

## Slide 8: “Hybrid” Approach, continued
Discharge permit limitations set as follows:
Ambient water quality target is set using first number in the range
No effluent limitation shall require an “end-of-pipe” discharge level more restrictive than the second number in the range

## Slide 9: “Hybrid” Approach, continued
Water bodies are in attainment for 303(d) purposes so long as the ambient water quality does not exceed second number in the range
EPA not expected to object, e.g., see “EPA Likely to Approve Novel Colorado Plan for Effluent ‘Range,’” (Vol. 13, No. 21, Inside EPA’s Water Policy Report)

## Slide 10: Metro & CO Wastewater Utility Council Concerns
Organics sampled by Metro to comply with pretreatment requirements did not include all of the regulated chemicals
There was a lack of data from other POTWs around the state
State regulators had virtually no data
Monitoring and analysis of organics involve high costs

## Slide 11: Preparation for Hearing
Metro contracted with CH2M Hill to provide summary analysis of (limited) effluent organics data from 6 Colorado POTWs (all WWUC members)
Treatment costs were to be estimated for these POTWs
No in-stream sampling was involved

## Slide 12: 5 “Candidate” Chemicals Chosen for Review
Trichlorophenol 2,4,5 (newly regulated, but no monitoring data obtained)
Methylene chloride
Chloroform
BIS-2 ethylhexyl phthalate
Vinyl chloride

## Slide 13: 5 “Candidate” Chemicals Chosen for Review, con’t
The selected chemicals were based on a review of available data by CH2M Hill indicating they were likely to be present
Other organics were noted to be present in POTW discharges at levels that could be of concern
Trichlorophenol 2,4,5 was chosen because it was newly regulated

## Slide 14: 6 WWUC Members Volunteered
POTW | Designated Use(s) | Max. Plant Flow (cfs) | Stream Flow (cfs)
A | WS | 309 | 0
B | WS | 116 | 15
C | FI | 19.3 | 850
D (no pre- treatment) | WS | 3.1 | 2.9
E | W+F | 7.5 | 0.5
F | W+F | 56 | 34

## Slide 15: Results – Methylene Chloride
POTW | Use(s) | WQ Std (ug/L) | Effluent Limit | Max Value Found
A | WS | --- | --- | 3.8
B | WS | --- | --- | 5.2
C | FI | 180 | 8,107 | no data
D | WS | --- | --- | no data
E | W+F | 5.6 | 6.0 | no data
F | W+F | 5.6 | 9.0 | 0

## Slide 16: Results - Chloroform
POTW | Use(s) | WQ Std (ug/L) | Effluent Limit | Max Value Found
A | WS | --- | --- | 0.9
B | WS | --- | --- | 2.7
C | FI | 110 | 4,955 | 3
D | WS | --- | --- | 19
E | W+F | 3.4 | 3.6 | no data
F | W+F | 3.4 | 5.5 | no data

## Slide 17: Results – BIS 2
POTW | Use(s) | WQ Std (ug/L) | Effluent Limit | Max Value Found
A | WS | 6 | 6 | 27
B | WS | 6 | 6.8 | 13
C | FI | 2.2 | 99 | 27
D | WS | 6 | 11.6 | 14
E | W+F | 1.2 | 1.3 | no data
F | W+F | 1.2 | 1.9 | 11

## Slide 18: Results – Vinyl Chloride
POTW | Use(s) | WQ Std (ug/L) | Effluent Limit | Max Value Found
A | WS | 2 | 2 | 0
B | WS | 2 | 2.3 | 0
C | FI | 2.3 | 104 | 0
D | WS | 2 | 3.9 | 19
E | W+F | 0.023 | 0.025 | no data
F | W+F | 0.023 | 0.037 | 0

## Slide 19: Est. Treatment Costs - Oxidation
POTW | Construction | Annual Operations
A | $60,000,000 | $11,700,000
B | $22,500,000 | $4,400,000
C | $3,700,000 | $730,000
D | $600,000 | $117,000
E | $1,450,000 | $280,000
F | $10,900,000 | $2,120,000

## Slide 20: Est. Treatment Costs – Packed Tower
POTW | Construction | Annual Operations
A | $10,000,000 | $730,000
B | $3,750,000 | $275,000
C | $625,000 | $45,000
D | $100,000 | $7,000
E | $240,000 | $18,000
F | $1,800,000 | $133,000

## Slide 21: Est. Treatment Costs – GAC
POTW | Construction | Annual Operations
A | $120,000,000 | $18,250,000
B | $45,000,000 | $6,800,000
C | $7,500,000 | $1,100,000
D | $1,200,000 | 180,000
E | $2,900,000 | $440,000
F | $21,800,000 | $3,300,000

## Slide 22: Rulemaking Hearing Strategy
Neither Metro nor WWUC included data in prehearing statements
Determined it was too risky
However, because no data were presented, the WWUC proposal to extend the “hybrid” approach to W+F segments failed

## Slide 23: Where Do We Go From Here?
Two externalities also come into play:
      Public perception
      Political reality

## Slide 24
Public Perception on Organic Chemicals

## Slide 25: Political Reality in Colorado

## Slide 26: Next Steps… (or not)?
Work cooperatively with the state to obtain more data?
Will that lead to enforcement actions or 303(d) listing?
Risk of third-party lawsuits?
Does it make sense to begin to consider costly, advanced treatment technologies?