## Slide 1: “XENOBIOTICS” Compounds, Sources, & Characteristics AMSA – 2004 National Pretreatment Conference
Jerry Ongerth, PhD, PE,
EBMUD Water Quality Office
October 28, 2004
W:\nab\esd\bkh\presentations\amsa2004.ppt

## Slide 2: OVERVIEW
Contaminants -- What, where, & why
Pharmaceutical Residuals
  Origins
  Behavior
  Fate and distribution
Next Steps
  What can we expect?
  What can we do about it?
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3: Xenobiotics--Emerging Contaminants
Hormonally Active Agents (HAA’s) or “Endocrine Disrupters”
Pharmaceutically Active Compounds (PhAC’s) or Pharmaceutical Residuals
Personal Care Products PCP’s (or w/PhAC’s = PPC’s)

## Slide 4: Hormonally Active Agents
Human, animal, & plant hormones
  Estrogens
  Phytoestrogens
Detergent residues
  Nonylphenol
Low volatility solvents/plasticizers
  phthalates

## Slide 5: Pharmaceutical Residuals
Prescription drugs
  Antidepressants; antibiotics; vasoregulators; lipid regulators; antiepileptics
Nonprescription drugs (over-the-counter)
  Analgesics; cold remedies; dietary supplements;
Illicit drugs:
  Opiates; amphetamines; cocaine derivatives; designer drugs

## Slide 6: Personal Care Products
Disinfectants
Deodorants
Fragrances
Flavoring agents
Insect repellants
Sun screens

## Slide 7
What have you been drinking???

## Slide 8: EVENTS & FINDINGS
Reports of trace organics presence in surface & groundwater--Europe, 1990’s
“Our Stolen Future”--Colburn, T., 1996
USGS Surveys--139 streams, 30 states, 1999-2000

## Slide 9: PHARMACEUTICAL RESIDUALS
Prescription drugs
  Antidepressants; antibiotics; vasoregulators; lipid regulators; antiepileptics
Nonprescription drugs (over-the-counter)
  Analgesics; cold remedies; dietary supplements;
Illicit drugs:
  Opiates; amphetamines; cocaine derivatives; designer drugs
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: WHY PHARMACEUTICALS?
Many compounds
Widely distributed
Produced to affect humans & animals
Active at (relatively) low concentration
Produced to be:
  Soluble
  Poorly degradable
  Relatively stable
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: EUROPEAN FINDINGS
  Analgesic (aspirin)
  Anti-inflamatory (diclofenac)
  Beta-blocker (propanolol)
  Lipid regulator (clofibrate)
  Antiepileptic (carbamazepine)
  Sedatives (diazepam)
  Antineoplastic (ifosfamide)
  X-ray contrast (iopromide)
Sewage  surface & groundwater & marine
Widespread & increasing
More than 40 Compounds reported:
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12
Pharmaceuticals, hormones, and other organic wastewater contaminants measured in 139 streams during 1999 & 2000
USGS SURVEY--1999 & 2000
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13
USGS--1999 & 2000
Most commonly detected groups :
Steroids
Nonprescription drugs
Insect repellent
Highest concentration compounds:
Detergent metabolites
Steroids
Plasticizers
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: WHAT DOES THE DATA SUGGEST
Reported detections are scattered & at low concentrations (typically < 1g/L)
Analytical procedures are designed to find only compounds of selected types
Sampling & analysis schemes limit both what and how much we can find
Data on production, use, and characteristics are available
Prediction can help to show what we need to know
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: ACADEMIC ESTIMATE
100,000 kg/yr /(19,000,000 p x 365 days/yr)  15 mg/cap-day
15 mg/cap-day / 100 L/cap-day = 0.15 mg/L
150 ug/L @ 100,000 kg/yr 1.5 ug/L @ 1000 kg/yr

## Slide 16: APPROACH
Comprehensive--All compounds in use
  Highest 50 (by total mass prescribed)
    No 1 = Acetaminophen--300,000 kg/yr (45 mg/cap/day)
    No 50 = Doxycycline--2000 kg/yr (0.3 mg/cap/day)
  Population @ 1999: 19,000,000
Mass balance
  UseExcretion SewageTreatment
  100 L per capita per day
  Biological secondary treatment
Measure residuals in samples from 7 STP’s
  Australia (2), Germany (3), and USA (2)
  20 mgd to 200 mgd

## Slide 18
Schematic of a STP with chemical (g.h-1) mass balance (Clark et al., 1995)

## Slide 19
Rank
Name
Annual dispensed mass (kg)
1
ACETAMINOPHEN
295882 (45 mg/cap/day)
2
METFORMIN (hydrochloride)
90878 (12 mg/cap/day)
3
LACTULOSE
88099
4
AMOXYCILLIN
46204
5
RANITIDINE (hydrochloride)
33724 (5 mg/cap/day)
6
CEPHALEXIN
25408 (4 mg/cap/day)
7
NAPROXEN
22850
8
VALPROATE (sodium)
20889
9
ASPIRIN
20389
9b
SALICYLIC ACID (ex-aspirin)
20389
10
GEMFIBROZIL
20042 (3 mg/cap/day)

## Slide 22
Per capita to sewage mg/cap/day
Approximate limit of detection--0.01 to 1 ug/L

## Slide 24: CONTROLLING FACTORS
Quantity of use
Excretion quantity and form
Fugacity, Log P (range is 7 logs)
Biodegradability (range is 6-8 logs)
Acid-base chemistry
Reactivity

## Slide 25: VERIFICATION
Sewage treatment plant data
  Good agreement
  Consistent: Australia-Germany-USA
Environmental data
  USGS data
  European data

## Slide 26: APPLICATION
Planning for sampling & analysis
Guide--what to look for
Estimate quantities of use from raw sewage data

## Slide 27: SIGNIFICANCE
Based on quantities--very low
Toxicology--???

## Slide 28: Source Control Activities
Pharmaceutical disposal
Product bans
Any value???

## Slide 29: CONCLUSIONS
Compounds in significant use are likely to be
detectable
Compound presence & fate in the environment
  depends on physical/chemical properties
Sampling & analysis procedures control what
is detectable
Knowing what is there permits rational planning
Source control activities may serve limited educational function – at this point