## Slide 1
Drinking Water Supply and Treatment
Effluent Guidelines Rulemaking –
Overview & Status
Presented to: AMSA 2004 Pretreatment Conf. Norfolk, VA October 29, 2004 | Presented by: Carey A. Johnston, P.E. U.S. EPA, Office of Water Washington, DC

## Slide 2: Outline of Presentation
Briefly review effluent guidelines & CWA effluent guidelines planning requirements.
Summarize EPA’s review of the drinking water supply and treatment and its identification for an effluent guidelines rulemaking.
Next Steps…
Questions?

## Slide 3
<number>
<footer>
<date/time>
Pretreatment
Treatment
Sewage Treatment Plant
ELGs regulate indirect and direct dischargers
Surface Waters
Indirect Discharger
Direct Discharger
What are Effluent Guidelines?

## Slide 4: Clean Water Act (CWA) §304(b) and §304(m) Planning Requirements
CWA §304(b) requires EPA to develop effluent guidelines for industrial wastewater dischargers. EPA must annually review and, if appropriate, revise these regulations.
The effluent guidelines program has had its schedules set by the judicial branch for most of its three decade history. Last decree ended in August 2004.
Congress amended the CWA in 1987 and established a formal planning process for the effluent guidelines program (§304(m)).

## Slide 5
<number>
<footer>
<date/time>
START
Solicit stakeholder recommendations and data on revising existing effluent guidelines and on identifying industries for new effluent guidelines
Publish Preliminary Plan Identifying Industry Sectors for Possible Inclusion in Final Plan
Perform Detailed Investigations
of Industry Sectors Identified in Preliminary Plan
Conduct Additional Outreach Meetings
Publish Final Plan
Decide Which Industry Categories to Identify for Guideline Revision or a New Guideline
Screening Level Analyses
Effluent Guidelines Biennial Planning

## Slide 6: CWA §304(m) Requirements
For industry categories without a guideline:
  EPA must identify new categories of point sources discharging toxic or non-conventional pollutants and establish a schedule for promulgating guidelines within 3 years, and
  Legislative history says EPA must address “significant” or “nontrivial” discharges.

## Slide 7: Drinking Water – Comments on Preliminary Plan
Public comments suggested EPA develop effluent guidelines for this industrial sector due to the potential of facilities in this industrial sector to discharge nontrivial amounts of non-conventional and toxic pollutants (e.g., metals and salts).
These commenters noted that the source of these pollutants can include drinking water treatment sludges and reverse osmosis reject wastewaters.
Consequently, EPA collected additional information and re-evaluated the information for the 2004 Final Plan.

## Slide 8: Drinking Water Supply and Treatment – Source of Residues
Drinking water supply and treatment residuals come from: (1) source water; and (2) treatment chemicals.
Treatment Process | Residue Form
Intake Screening | Trash
Pre-sedimentation | Solids
Coagulation, Flocculation, Sedimentation | Slurry
Filtration | Liquid/Slurry
Ion Exchange/Inorganic Adsorption Processes | Liquid/Brine
Softening | Slurry
Membrane Processes | Liquid/Brine
Adsorption Processes for Organic Processes | Slurry/Solid

## Slide 9: Drinking Water Supply and Treatment – Likely Residues
Characteristics of drinking water supply and treatment residuals are location- and season-specific.
Parameter/Chemical | Likely Source
Suspended Solids | Source Water
Organic Matters | Source Water
Radionuclides | Source Water
Aluminum Salts | Chemical Coagulation
Iron Salts | Chemical Coagulation
Polymer | Chemical Treatment
Lime | Chemical Treatment & pH Correction
Powdered Activated Carbon | Taste & Odor Control

## Slide 10: Drinking Water Supply and Treatment – Residual Production
Large water treatment facilities can generate significant quantities of residuals.
For example, a large utility treating 130 MGD of average-quality river water can produce 16 tons of dry solids per day.
Source Water | Ave. Range of Residue Production (lbs. Dry Solids/MG Treated)
Good-Quality Reservoir Water | 100 – 150
Fair-Quality Reservoir Water | 150 – 250
Average-Quality River Water | 200 – 300
Poor-Quality Reservoir Water | 250 – 350
Poor-Quality River Water | 350 – 450
Source: AWWA, Water Quality & Treatment, 4th Edition

## Slide 11: Drinking Water Supply and Treatment – Discharge Data
EPA's primary source of wastewater data for this industrial sector is EPA's Permit Compliance System (PCS).
This database contains information required by the NPDES Permit Program for major dischargers across the country, including discharge flows and pollutant concentrations.
EPA was therefore able to analyze this information for the 16 drinking water supply and treatment facilities with major permits for the year 2000.

## Slide 12: Drinking Water Supply and Treatment – Discharge Data
However, EPA does not require states to include such data for other dischargers (e.g., minor and indirect dischargers) in PCS.
PCS lists approximately 900 drinking water supply and treatment facilities as having minor permits for the year 2000, but does not include data on discharge flows or pollutant concentrations.
Consequently, EPA was unable to quantify discharges from these minor and indirect discharging facilities.

## Slide 13: Drinking Water Supply and Treatment – Discharge Data
EPA noted that the largest dischargers had recent significant reductions:
  Washington, DC (500,000 toxic-weighted pounds in 2000) now has a BPJ permit requiring 85% reduction
  Phoenix, AZ (100,000 toxic-weighted pounds in 2000) is now not a direct discharger
The breakdown of the remaining facilities was:
  Two facilities greater than 4,000 toxic-weighted pounds,
  Three between 1,000 – 4,000,
  Four between between 5 – 1,000, and
  Seven facilities less than 5.
Total direct discharges for this industrial sector in 2000 as reported to PCS: 20,560 toxic weighted pounds.

## Slide 14: Drinking Water Supply and Treatment
The PCS data suggests that some drinking water supply and treatment facilities with direct discharging permits are not discharging pollutants in significant concentrations.
However, the data also supports commenters' statements that other drinking water treatment and supply facilities may discharge nontrivial amounts of toxic and non-conventional pollutants.
Consequently, EPA identified the drinking water supply and treatment industry for an effluent guidelines rulemaking.

## Slide 15: Control and Management Options
Source reduction
  Selection of raw water source intake (Fairfax, VA, estimated 50% reduction of residuals by moving intake to mid-river location);
  Choice of chemicals for coagulation & softening;
  Re-circulation and reuse of filter backwash waters; and
  Treatment chemical recovery (alum, quick-lime).
Concentration/Treatment
  Physical: Lagoons, Drying Beds, Gravity Thickening, Vacuum Filtration, Belt Filters, Filter Presses.
Disposal
  Land application (landfill, roadbed construction);
  POTW; and
  Surface water discharge.

## Slide 16: Issues Related to Surface Discharge
Character of receiving waters determines acceptability of discharges.
Considerations in determining WQBELs
  Adequate dilution to meet water quality standards;
  Benthic deposition; and
  Aesthetics (no precipitation of treatment chemicals).
Controlled discharges
  Storage and release basins; and
  Monitoring requirements.

## Slide 17: Issues Related to POTW acceptance
POTW hydraulic & solids handling capacity.
Residuals may be abrasive to POTW centrifuges and other sludge thickening equipment.
Residuals may contain free alum which may aid POTW operations.

## Slide 18: States and Regions Have Taken a Wide Range of Permitting Approaches
General permit
  Many states regulated these facilities through general permits.
Individual permit with numerical limitations and/or BMP requirements
  A review of 400 NPDES permits for drinking water facilities in EPA Region 3 identified that most facilities have a TSS limit of 30 mg/l.
  In addition, other states such as Michigan use 30 mg/l monthly average as a treatment-based BPJ limit for filter backwash discharges.

## Slide 19: Next Steps
EPA published the 2004 Effluent Guidelines Program Plan on September 2, 2004 (69 FR 53705).
EPA will gather information and data on this industry to assist in evaluating technology options.
EPA intends to propose effluent guidelines for the this industrial sector by September 2006 and take final action by September 2007.

## Slide 20: Questions?

## Slide 21: For Further Information
www.epa.gov/guide/plan.html
Most record documents, including all public comments, can be viewed online at: www.epa.gov/edocket (Docket #OW-2003-0074)
Contact:
  Tom Born, Project Lead: Drinking Water, 202-566-1001, born.tom@epa.gov
  Carey Johnston, Project Lead: Effluent Guidelines Planning, 202-566-1014, johnston.carey@epa.gov