## Slide 1: TBT: Issues and Challenges
James J. Pletl, Ph.D.
Hampton Roads Sanitation District
Virginia Beach, VA

## Slide 2: TBT: What Is It?
Tributyltin
Classified as a pesticide
Suspected endocrine disruptor, may induce imposex in molluscs
Half-life in days-months in water and sediment, biodegradation important

## Slide 3: TBT: Use And Source
Antifouling biocide most commonly used in :
  ship paints and coatings
  sonar domes
  domestic stains/paints
Sources of TBT in Elizabeth River:
  leaching from ship hulls, possibly 102-103 g/day
  secondary is ship hull blasting
  sediment probably another significant NPS

## Slide 4: TBT: Regulatory Implications
Current VA saltwater chronic water quality standard is 1 ppt
EPA draft chronic criterion was 1 ppt, based partly on field data
HRSD provided extensive comments on draft
EPA recently finalized chronic saltwater criterion at 7.4 ppt

## Slide 5: TBT: Regulatory Implications
Use of TBT restricted in 1988 to only coating vessels > 25m
Ambient monitoring shows concentrations in the 5-15 ppt range
VA lists Elizabeth River for TBT in 305(b)/303(d) report, TMDL required
Two HRSD plants on Elizabeth River

## Slide 7: TBT: Political Implications
Hampton Roads harbor one of busiest in US
Competition high between shipyards
Stringent WQS’s in HR harbor puts shipyards there at a disadvantage:
  foreign business is critical to success
  well over 50% foreign ships have TBT, Navy ships not the problem

## Slide 8: TBT: Political Implications
No standard more stringent in US than VA
DEQ and industry continue to pressure HRSD to accept TBT wastes
VA has had to back-peddle when implementing WQS’s with shipyards
DEQ using mass-based limit of 5 g/yr rather than concentration-based
International phase out planned for 2008

## Slide 9: HRSD Initiatives
Address industrial discharges
Research analytical methods, develop capabilities
Document domestic/commercial contribution
TMDL listing - data review
Negotiate NPDES permit language

## Slide 10: Pretreatment Approach
Stringent WQS’s combined with known sources require a unique approach
HRSD concerned that it would receive limits and require additional treatment
Pretreatment program implemented a “zero discharge” policy

## Slide 11: Pretreatment History
Sonar dome discharge prohibited first, domes impregnated with TBT
CWT’s, which receive sonar dome water contaminated with TBT, regulated next
Recent HRSD activities focus on hull-blasting activities of shipyards.

## Slide 12: Examples: Industrial Discharge Concentrations
Discharger | Mean (ng/l) | Range (ng/l)
A | 593 | 373-878
B | 175 | 28-305
C | 2843 | 228-7930
D | 3482 | 426-10,900

## Slide 13: Industrial Wastewater Permit Language
No detectable level (10 ppt) can be discharged
Discharges believed to contain any level of TBT must be reported, sampled and analyzed by HRSD protocols
No waste-mixing allowed

## Slide 14: Pretreatment Program Impacts
One ship repair facility has
  eliminated blasting waste from sanitary sewer
  cleaned and recoated/replaced discharge lines previously contaminated
  sealed manholes to address air deposition
All but two repair facilities have eliminated work involving TBT coatings

## Slide 15: TBT: Analytical Approach
No 40 CFR Part 136 method available
Split samples within and between labs significantly vary
DEQ advocates use of method developed by VA Institute Marine Sciences for research
GC-FPD followed by confirmation with MS

## Slide 16: TBT: Analytical Approach
HRSD reviewed and adopted VIMS method with numerous QC additions:
  field, container and equipment blanks
  blank acceptance ranges
  MS and MSD acceptance ranges
  confirmation maximum RPD
  surrogate acceptance ranges
  internal standard acceptance criteria
  40 CFR Part 136-based MDL

## Slide 17: TBT: Analytical Approach
Method very tedious, multiple clean-up steps
10-15 sample batch requires 3-4 people
Instrumentation costs over $65,000
$700/sample with all QC
Holding time is 12 weeks

## Slide 18: Domestic/Commercial Sources
DEQ alleged that TBT found in:
  toilet bowl cleaners
  disinfectants
  carpet/upholstery shampoos
  PVC products
Nearly 70 compounds registered in VA for sale containing TBT
DEQ assumed products are available and purchased if registered

## Slide 19: Product Survey
Approximately 35 companies associated with registered products surveyed
76% of products are paints/stains/coatings
16% products used in cooling towers
6% products no longer available
1 product used in commercial cleaning and has since been substituted
Conclusion: alleged products not reaching HRSD’s facilities

## Slide 21: TMDL Listing: Ambient TBT Data Quality And Reliability
HRSD reviewed data quality, found significant deficiencies:
  lack of sampling SOP
  preservation not addressed
  CRMs, equipment blanks, MQOs, MS and MSD not used
  poor or non-existent analytical and sampling documentation

## Slide 22: Ambient TBT Data
Data quality deficiencies cont.:
  blank contamination, field and lab
  ignored EPA QC recommendations
  failure to address saltwater matrix effect
  chain of custody not implemented

## Slide 23: Ambient TBT Data
DEQ now funds VIMS to conduct all Elizabeth River TBT data
VIMS agreed to incorporate QA/QC promoted by HRSD
Data now much less variable and more reliable

## Slide 24: NPDES Language
DEQ proposed 2 analyses/yr and QL of 10 ppt in draft permits
HRSD presented TBT control efforts (domestic/commercial/industrial)
HRSD documented analytical issues
Negotiated 2 samples/permit term and QL of 30 ppt

## Slide 25: Status and Conclusions
Ambient monitoring of receiving waters continues
Receiving waters for 2 HRSD plants still 303(d) listed, awaiting TMDL
No quantifiable concentrations reported in effluent
Comments will be provided in current standards review to adopt final EPA chronic criterion