## Slide 1
Airport Deicing Operations
Effluent Guidelines Rulemaking –
Overview & Status
Presented to: AMSA 2004 Pretreatment Conf. Norfolk, VA October 28, 2004 | Presented by: Carey A. Johnston, P.E. U.S. EPA, Office of Water Washington, DC

## Slide 2: Outline of Presentation
Briefly review effluent guidelines & CWA effluent guidelines planning requirements.
Summarize EPA’s review of the airport industrial sector and its identification for an effluent guidelines rulemaking.
Next Steps…
Questions?

## Slide 3
<number>
<footer>
<date/time>
Pretreatment
Treatment
Sewage Treatment Plant
ELGs regulate indirect and direct dischargers
Surface Waters
Indirect Discharger
Direct Discharger
What are Effluent Guidelines?

## Slide 4: Clean Water Act (CWA) §304(b) and §304(m) Planning Requirements
CWA §304(b) requires EPA to develop effluent guidelines for industrial wastewater dischargers. EPA must annually review and, if appropriate, revise these regulations.
The effluent guidelines program has had its schedules set by the judicial branch for most of its three decade history. Last decree ended in August 2004.
Congress amended the CWA in 1987 and established a formal planning process for the effluent guidelines program (§304(m)).

## Slide 5
<number>
<footer>
<date/time>
START
Solicit stakeholder recommendations and data on revising existing effluent guidelines and on identifying industries for new effluent guidelines
Publish Preliminary Plan Identifying Industry Sectors for Possible Inclusion in Final Plan
Perform Detailed Investigations
of Industry Sectors Identified in Preliminary Plan
Conduct Additional Outreach Meetings
Publish Final Plan
Decide Which Industry Categories to Identify for Guideline Revision or a New Guideline
Screening Level Analyses
Effluent Guidelines Biennial Planning

## Slide 6: CWA §304(m) Requirements
For industry categories without a guideline:
  EPA must identify new categories of point sources discharging toxic or non-conventional pollutants and establish a schedule for promulgating guidelines within 3 years, and
  Legislative history says EPA must address “significant” or “nontrivial” discharges.

## Slide 7: Airport Deicing Operations
Commentors identified airport deicing as new category
EPA reevaluated 2000 study:
  Discharges estimated at 21 million gallons of aircraft deicing fluid annually
  Estimated that the 2000 storm water permit regulations would reduce discharges to 17 million gallons annually
  Estimated that an effluent guideline could reduce discharges to 4 million gallons annually
Toxicity of aircraft deicing fluids mainly due to glycols and additives
  Glycols are fairly non-toxic in the aquatic environment. For mammals, main concern is ingestion of ethylene glycol
  The limited data on toxicity of additives indicate deicing fluids containing additives are more toxic than pure glycols

## Slide 8: Challenges in Controlling and Regulating Deicing Runoff
Materials strictly regulated by FAA for operational and safety requirements.
All approved materials have environmental implications.
Deicing materials can be widely dispersed.
Deicing runoff is winter-time (cold) storm water event
  Variable flows and concentrations
  Large volumes
  Technically difficult to develop water-quality-based effluent limitations

## Slide 9
<number>
<footer>
<date/time>
Geographic Distribution of 212 Airports With Annual Operations >10,000 & Mean Annual Snowfall Greater than 1”
Source: EPA Preliminary Data Summary, 2000 (EPA-821-R-00-016)
Alaska Airports Include:
Anchorage (2), Juneau, Kodiak, Kenai, Fairbanks, Bethel, King Salmon

## Slide 10: All FAA-Approved Deicing Materials have Environmental Implications
Glycols (aircraft)
  Biochemical oxygen demand
  Toxicity
  Odors
Urea (pavement)
  Ammonia toxicity
  Biochemical oxygen demand
Acetates and formates (pavement)
  Biochemical oxygen demand
Additives (both)
  Toxicity
  Foaming

## Slide 11
<number>
<footer>
<date/time>
Example Deicing Fluid Runoff Pathways

## Slide 12
<number>
<footer>
<date/time>
Aircraft Deicing and Anti-icing Fluids are
Dispersed During and After Application

## Slide 13: Winter Storm Water Complexities
Deicing activities are weather-driven
Complex transport mechanisms
  Aircraft adhesion
  Airborne spray
  Overland flow
  Snowmelt processes
  Snow plowing and disposal
Design Conditions
  Precipitation types
  Temperature

## Slide 14: Control and Management Options
Source reduction
  Combine hot air and low-flow glycol (70% reduction)
Containment/Collection
  Designated deicing areas (e.g., central deicing pads)
  Isolation techniques (e.g., glycol recovery vehicles)
  In-sewer diversions, gates, dams
Storage & Treatment/Disposal

## Slide 15
<number>
<footer>
<date/time>
Example Central Deicing Pad

## Slide 16: Issues Related to Surface Discharge
Character of receiving waters determines acceptability of discharges
  BPJ approach in setting BMPs or numerical limits
  WQBEL approach
Considerations in determining WQBELs
  Wet weather
  Winter temperatures
  Melt-off discharges integrate multi-day events
Controlled discharges
  Storage and release basins
  Monitoring requirements

## Slide 17: Issues Related to POTW acceptance
POTW BOD and/or hydraulic capacity
Discharges occur during wet, cold weather events
Unless equalized, discharges are slug loads
Acclimation to new food source
Potential toxicity to process “bugs”
Potential pass through of additives/contaminants
Aggravation of existing plant problems

## Slide 18: States and Regions Have Taken a Wide Range of Permitting Approaches
General storm water permit
Individual permit with numerical limitations
Individual permit with BMP requirements in lieu of numerical limitations

## Slide 19: Future Developments May Reduce Environmental Impacts
Pavement Deicing
  New product formulations
  Absorbent epoxy coatings to provide prolonged anti-icing
Aircraft Deicing
  Improved additive packages
  Non-glycol deicers
  Lower BOD
  Lower degradation rates
  New recycling and treatment technologies

## Slide 20: Other Airport Industrial Discharges
EPA will also gather data on other airport industrial operations that are currently unregulated by other effluent guidelines (e.g., MP&M, Metal Finishing).
AFFF Training Exercise

## Slide 21: Next Steps
EPA published the 2004 Effluent Guidelines Program Plan on September 2, 2004 (69 FR 53705).
EPA will gather information and data on this industry to assist in evaluating technology options.
EPA intends to propose effluent guidelines for the airport industrial sector by September 2006 and take final action by September 2007.

## Slide 22: Questions?

## Slide 23: For Further Information
www.epa.gov/guide/plan.html
Most record documents, including all public comments, can be viewed online at: www.epa.gov/edocket (Docket #OW-2003-0074)
Contact:
  Eric Strassler, Project Lead: Airports, 202-566-1026, strassler.eric@epa.gov
  Carey Johnston, Project Lead: Effluent Guidelines Planning, 202-566-1014, johnston.carey@epa.gov