## Slide 1: The 2004 Effluent Guidelines Program Plan
2004 National Pretreatment
Coordinators Workshop
October 27, 2004

## Slide 2
The effluent guidelines program has had its schedules set by the judicial branch for most of its history: Green (70’s), Flannery (80’s), & Lamberth (90’s)
Section 304(b) of the Clean Water Act requires EPA to annually review its existing effluent guidelines for possible revision.
Congress amended the CWA in 1987 and established a formal planning process for the effluent guidelines program. Section 304(m) applies only to industries with direct discharging facilities and requires EPA to publish a plan every even year after taking public comment.
304(b) and 304(m) Requirements

## Slide 3
For industry categories with an existing guideline:
  EPA must establish a schedule for the annual review and, if appropriate, revision of these guidelines based on factors such as cost, nonwater quality environmental impacts and other factors the Administrator deems appropriate
For industry categories without a guideline:
  EPA must identify new categories of point sources discharging toxic or nonconventional pollutants and establish a schedule for promulgating guidelines within 3 years
The 2004 Effluent Guidelines Program Plan is EPA’s first attempt since 1990 to establish an effluent guidelines plan outside the context of a consent decree
More on Requirements

## Slide 4
In November 2002, EPA published and requested comment on a Draft Strategy for implementing 304(m) using four decision factors:
  - Does an industry category discharge pollutants that pose a risk to human health or the environment?
  - Will any control technologies, process changes or pollution prevention approaches reduce these risks?
  - If so, what will the technology, process change or pollution prevention approach cost, how well will it perform, and is it affordable?
  - Are there implementation or efficiency issues to consider?
    Have industry changes made existing guidelines inappropriate (e.g., a barrier to the use of new technologies)?
    Would revising a guideline allow more pollutant control at lower cost?
    Could other approaches (e.g., permit support, voluntary reductions) achieve the same or greater reductions more efficiently?
Draft 304(m) Strategy

## Slide 5: Preliminary 2004 Plan
Published December 31, 2003 (68 FR 75515)
  Comment period closed March 18, 2004
Described analytical framework and methodology for conducting the 304(b) review and developing the 304(m) plan
- Similar to draft strategy, some modifications
Presented results of EPA’s 2003 annual review of promulgated guidelines
Presented preliminary decisions on potential new guidelines

## Slide 6: Preliminary 2004 Plan
No categories w/out ELGs identified for development of new guidelines
Two previously-regulated categories identified for detailed study in the 2004 annual review and possible ELG revision: organic chemicals, plastics and synthetic fibers; and petroleum refining
  Review to address two unregulated subcategories: chemical formulators, packagers and reformulators; and petroleum bulk stations and terminals
Identified potentially high hazards or risks from two other industrial categories: inorganic chemicals and nonferrous metals
  Said we would resolve data gaps prior to the 2006 final plan
Identified seven other categories with potentially high hazards or risk
  Said we would continue investigating data gaps for future plans
Regions and stakeholders suggested nine other categories
  Hazard/risk scores do not appear to warrant revision

## Slide 7: 2004 Effluent Guidelines Program Plan -- Overview
Contains results of 2004 annual review
Identifies for effluent guideline rulemaking guidelines for potential revision and develoment, including rulemaking schedules
Discusses 2005 annual review and timeline for next Program Plan

## Slide 8: 2004 Program Plan – Organic and Inorganic Chemicals
Revise ELGs for Organic Chemicals, Plastics and Synthetic Fiber and Inorganic Chemicals industrial categories, focusing on dioxin discharges:
In the Organics Category, dioxin is primarily discharged by vinyl chloride manufacturers. Many of the facilities also manufacture chlorine using the chlor alkali process (regulated under the Inorganic Chemicals guidelines), another source of dioxins
While investigating the role of chlor alkali plants in generating dioxins at large integrated organic chemical plants, we learned that dioxin discharges from stand-alone chlor alkali plants are also significant

## Slide 9: 2004 Program Plan – Drinking Water Facilities
Identified for ELG rulemaking – Drinking water faciliites
Commentors identified drinking water facilities as new category
Discharge data:
  In 2000, PCS had quantitative data for 16 major facilities. 900 minor facilities discharge unquantified amounts
  Largest discharger in 2000 (DC -- 500,000 toxic-weighted pounds) now has a BPJ permit requiring 85% reduction; second largest discharger in 2000 (Phoenix --100,000 toxic-weighted pounds) no longer discharges
  2003 PCS discharges: two facilities greater than 4,000 toxic-weighted pounds, three between 1,000 – 4,000, four between between five – 1,000, seven facilities less than 5, total discharges of 20,560 toxic weighted pounds

## Slide 10: 2004 Program Plan – Airport Deicing
Identified for ELG rulemaking – Airport Deicing
Commentors identified airport deicing as new category
Reevaluated 2000 study:
  Discharges estimated at 21 million gallons of aircraft deicing fluid annually
  Estimated that the 2000 storm water permit regulations would reduce discharges to 17 million gallons annually
  Estimated that an effluent guideline could reduce discharges to 4 million gallons annually
Toxicity of aircraft deicing fluids mainly due to glycols and additives
  Glycols are fairly non-toxic in the aquatic environment. For mammals, main concern is ingestion of ethylene glycol
  The limited data on toxicity of additives indicate deicing fluids containing additives are more toxic than pure glycols

## Slide 11: 2004 Program Plan – Petroleum Refining
No further action on Petroleum Refining -- Identified in Preliminary Plan for further investigation because dioxins and polycyclic aromatic compounds appeared to be present in final effluents in significant amounts
Further investigation indicated little or no dioxin has been detected in final effluent or in refinery refinery wastewater discharges
Data indicate little or no polycyclic aromatic compounds (PACS) are present in discharges from petroleum refiners.
Data indicate that metals and organics are being discharged at or near the detection level.
Data suggest non-conventional pollutants such as ammonia are being discharged at concentrations below which EPA has established recent limitations.
Petroleum bulk stations and terminals -- Process water discharges appear minimal, w/ possible exception of PBSTs that accept ballast water

## Slide 12: 2004 Program Plan -- Schedule
New categories – propose and take final action in 3 years, i.e., August 2007
Revision of Organic and Inorganic Chemicals categories will begin in March 2005; propose rule by March 2008

## Slide 13: 2004 Program Plan -- 2005 Annual Review
Conduct a screening analysis of all 56 industrial categories. Compare with results of previous reviews. 2004 Preliminary Plan identifies other categories with high risk.
More detailed analysis of those that rank high for toxic and non-conventional discharges.
Publish the 2006 Preliminary Plan in 2005 and take public comment.
2006 Final Plan issued by August 26, 2006.

## Slide 14: Litigation on 304(m) Our Children’s Earth Foundation and the Ecological Rights Foundation
Our Children’s Earth Foundation and the Ecological Rights Foundation filed suit in the Northern District of CA asserting EPA failed to carry out its nondiscretionary duty to:
  Adopt a final 304(m) plan for 2004 within statutory deadline
  Annually review existing effluent guidelines in accordance with sections 304(b) and 304(m)
  Failure to comply with 301(d) (5 year ELG review)

## Slide 15: More on 304(m) Litigation
Plaintiffs later filed motion for summary judgment asserting EPA failed to comply with statutory deadline. Court ruled in EPA’s favor given the representation that Plan would be issued by late August.
Plaintiff’s have filed a writ of mandamus to resolve issue of jurisdiction – District Court vs. Circuit Court
Recently Plaintiffs filed a motion to amend their complaint, asking the Court to review Final 2004 Program Plan.

## Slide 16: More Information
Federal Register notice at
Also at www.epa.gov/guide/plan.html
Carey Johnston
  202-566-1014
  Johnston.carey@epa.gov