## Slide 1
Airport Discharge Issues
One POTW’s Perspective
  Lou Kollias, P.E., DEE
  Asst. Chief Engineer
  R&D Dept. – MWRDGC
  2004 Pretreatment Coordinators Workshop
  Norfolk, Virginia
  October 28, 2004

## Slide 2
MAJOR AIRPORTS WITHIN MWRDGC
JURISDICTION
• City of Chicago - O’Hare Airport
• City of Chicago - Midway Airport

## Slide 3
O’HARE AIRPORT
• Approximately 7,700 acres
• Lake O’Hare/South Airfield
• North Airfield

## Slide 4
LAKE O’HARE/SOUTH AIRFIELD
• Storm drainage reservoir
• Approximately 100 acres
• Capacity - 400,000,000 gallons
• Stormwater runoff from ramps, runways, and taxiways
• Deicing runoff from terminals, aprons, runways, taxiways, and holding pads

## Slide 5
LAKE O’HARE/SOUTH AIRFIELD
• Treatment - Three oil/water separators/ clarifiers
• Discharge directed to MWRDGC Inter-ceptor or TARP
November 1 through April 30
• Discharge directed to waterway
May 1 through October 31
• Discharge to occur during low flows and dry weather periods

## Slide 6
LAKE O’HARE/SOUTH AIRFIELD
• Continuous flow measurement
• Continuous automatic sampler
• Discharge (1999 - 2003)
Volume - 817 to 1407 million gallons
BOD - 393 to 687 mg/l
SS - 26 to 41 mg/l

## Slide 7
LAKE O’HARE/SOUTH AIRFIELD
• User Charges (1999 - 2003)
$861,402 - $2,107,210
• Consistently meet Local Limits

## Slide 8
MWRDGC SEWAGE AND WASTE CONTROL ORDINANCE (LOCAL LIMITS)
Cadmium 2.0 mg/l
Chromium (Total) 25.0 mg/l
Chromium (Hexavalent) 10.0 mg/l
Copper 3.0 mg/l
Cyanide (Total) 5.0 mg/l
Fats, oils and greases (Total) 250.0 mg/l
Iron 250.0 mg/l
Lead 0.5 mg/l
Mercury 0.0005 mg/l
Nickel 10.0 mg/l
Zinc 15.0 mg/l
pH range - not lower than 5.0 or greater than 10.0

## Slide 9
NORTH AIRFIELD
• Three-cell reservoir storm drainage facility
• Approximately 30 acres
• Capacity - 105,000,000 gallons
• Stormwater runoff from runways and taxiways
• Deicing runoff from runways, taxiways, and holding pads

## Slide 10
NORTH AIRFIELD
• No treatment
• Discharge directed to MWRDGC Inter-ceptor November 1 through April 30
• Discharge directed to waterway
May 1 through October 31
• Discharge to occur during low flows and dry weather periods

## Slide 11
NORTH AIRFIELD
• Continuous flow measurement
• Continuous automatic sampler
• Discharge (2000 - 2003)
Volume - 52.5 to 611 million gallons
BOD - 172 to 529 mg/l
SS - 27 to 52 mg/l

## Slide 12
NORTH AIRFIELD
• User Charges (2000 - 2003)
$52,860 - $712,702
• Consistently meet Local Limits

## Slide 13
CONCLUSION
• Airport deicing discharges to MWRDGC have resulted in no problems
• Substantial User Charges have been recovered
• Airport and MWRDGC have a good working relationship