## Slide 1: BMPs: Successful Alternatives to Numerical Control
2004 National Pretreatment Coordinators Workshop
October 27, 2004
W:\nab\esd\presentations\\pretreat coord\pretreat Coord. Wrkshp-BMPs 10.04.ppt

## Slide 2: Presentation Overview
Definition
Industrial User BMPs
Zero Dischargers
Commercial Program BMPs
Other agency BMPs
Benefits of BMP Approach
Next Steps

## Slide 3: Best Management Practices
Scheduled activities
Prohibitions of practices
Maintenance procedures
Other management practices
To prevent or reduce pollution
Also includes treatment requirements, sludge or waste disposal

## Slide 4: Industrial User BMPs
BMPs incorporated into permits
Permit conditions:
  Practice pollution prevention techniques to reduce or eliminate pollutants and recycle wastes
  Identify P2 opportunities:
    Improved operating practices
    Material/product substitution
    Technology and process modification
Document P2 opportunities and update to reflect actions implemented

## Slide 5: Industrial User BMPs
Some federal categories have BMP option to meet prescribed categorical requirements:
  Transportation Equipment Cleaning Pollutant Management Plan
  Inspection checklist to confirm implementation
Must comply with local limits

## Slide 6: Industrial User BMPs
BMP Compliance
  Inspections include BMP compliance review
  Cannot assess “remotely”
  Not always occurring during inspection
  “Best behavior” during inspection
BMP Enforcement
  Not analogous to numerical limits SNC

## Slide 8: Zero Dischargers
CIUs/SIUs that discontinue regulated process discharge
Fee/monitoring incentives
EBMUD: 24 ZDs, 13 Discharging CIUs
BMPs
  Closed-loop/recycled rinses
  Evaporators
Complex relationship to local limits calculations
  40,000 gpd to zero discharge

## Slide 10: Commercial Facilities BMPs
MAIL = MAHL (1-SF) – (LUNC +HW +GA)
LUNC = (CUNC)(QUNC)(8.34)
BMPs: uncontrolled becomes controlled

## Slide 11: Commercial Facility BMPs
EBMUD permits ~3800 commercial facilities in 12 business types
Blanket permits
  All businesses in each category have same requirements
  Options for variances where appropriate
Effective non-sampling controls essential
  Seal floor drain
  Install/maintain appropriate equipment

## Slide 12: Commercial Facility BMPs

## Slide 15: Other Agency BMPs
Metropolitan Wastewater, San Diego
  Sector-specific BMP Discharge authorization
    Film Processing
    Dry Cleaners
    Boatyards (customized BMPs in permit)
    Food Establishments
    Auto Repair/steam cleaning

## Slide 16: Other Agency BMPs
Seattle Metropolitan/King County, WA
  Dental mercury BMPs

## Slide 17: Other Agency BMPs
Connecticut Dept of Env. Protection
  General Permits 18 sectors, each with BMPs:
    Vehicle Service Floor Drain and Car Wash
    Minor Photographic Processing
    Minor Printing and Publishing
    Food Processing

## Slide 18: Benefits of BMPs
Includes more dischargers as “controlled” flow for local limits calculations
Efficient use of resources
Decreased discharge of pollutants to treatment plant

## Slide 20: Next Steps
Expand BMP outreach to institutions
Track success of new commercial BMPs
Address emerging pollutants (PBDEs, EDCs, etc.)