## Slide 1: Technical Training Session
2004 National Pretreatment Coordinators Workshop
Association of Metropolitan Sewerage Agencies
Jan Marie Pickrel
U.S. EPA Headquarters
October 29, 2004

## Slide 2: Why Focus on Training Needs?
OIG Recommendation 3.4:
“Promote training opportunities to all POTWs by determining:
a) the POTWs’ ability to access information on EPA’s website and
b) the types of training POTWs need.”
Evaluation Form Questions

## Slide 3: More Reasons “Why?”
Aging Workforce /
New Workforce
Old Issues –
New Solutions
New Issues –
Old and New Solutions

## Slide 4: Training Strategy
Reason for Training
Topic
Target Audience
Training Method
Sources / Resources
  Developers/Trainers
  Venue
  Materials
Communications

## Slide 5
Topics
Regulations
Permit Writing
Inspections / Audits
Local Limits
Particular Sectors
  Regulations
  Case Studies
Security Issues
Performance Measures
Laboratory Methods
Methods
Live Humans/Videos
CD-Roms
Books/Brochures/Bulletins
Sources/Resources
U.S. EPA
States
AMSA
WEF
Trade Organizations

## Slide 6: “Water Environment Federation and U.S. Environmental Protection Agency Pretreatment Training”
2004 Locations:
Nashville, Tennessee (May)
Tampa, Florida (August)
Reno, Nevada (November)
2005 Locations: ?

## Slide 7: General Training Format
4 Overlapping Days:
Day 1: “Introduction to Pretreatment”
  Regulation Overview + Program Development
Days 2-3: “Intermediate Topics”
  Control of Industrial Discharges – Permit Writing
Day 4: “Advanced Topics”
  “Development & Application of Pretreatment Standards with Focus on Local Limits”
Notes: Introduction to Pretreatment is a REGULATION OVERVIEW
- We discuss the PROGRAM OBJECTIVES
REQUIREMENTS for PROGRAM DEVELOPMENT
IDENTIFYING INDUSTRIAL USERS – definition of SIU
What are CATEGORICAL STANDARDS and HOW ARE THEY DEVELOPED
MINIMUM REQUIREMENTS FOR IU AND POTW REPORTING, MONITORING
BASICS OF ENFORCEMENT ACTION, ENFORCEMENT RESPONSE PLANS
Days 2 & 3 are essentially devoted to PERMIT DEVELOPMENT, IDENTIFYING WHAT CONDITIONS TO PUT INTO PERMITS
We actually spend some grueling hours on the Categorical Standards – introducing the names of the categories, going into depth on some, particularly Metal Finishing, Chemical Industry.
We also have some round-table, networking discussion times.
Day 4 Local Limits – Verified with the new 2004 Local Limits Guidance Manual, and some “real world” examples

## Slide 8: “Development & Application of Pretreatment Standards with Focus on Local Limits”
Determining Pollutants of Concern
Developing Sampling Plan
  Collecting and Analyzing Data
Calculating MAHL, Reff, MAIL; Allocating IL
Developing Permit Limits
Notes: Modules named within

## Slide 9: Determining Pollutants of Concern
Review of Local Limits Goal
Discuss Types and Basis for Local Limits
Review Differences between Basis
Importance of Data Stressed and Stressed and..
  Example Removal Efficiency
Notes: In this section, we:
Review why you’d be developing Local Limits
-- to incorporate local protections that the National Standards cannot possibly fully incorporate locally – specific NPDES Permit limits that you may have because of Chesapeake Bay goals or trout streams, POTW Treatment Efficiencies at your specific POTW or POTWs – like flows that may be routed between or shared between 2 or more POTWs, etc.
Types : Chemical Specific, Collection System, BMPs, Case by Case limits
Basis: National POCs, NPDES Permit POCs, Biosolids Regulated POCs, Site Specific POCs
-- Review again the differences between Cat. Stds. And Local Limits – where your options are and how much flexibility you may have and where that flexibility is available.
How to Determine Pollutants of Concern – general basis of prioritizing the pollutants to sample for
Importance of “Good Data” – showing an example that 1% changes in the Removal Efficiency can make a difference in the MAHL

## Slide 10: Data Example: Removal Efficiency
Same POTW: 15.0 mg/l NPDES BOD Limit
5.0 MGD Flow
RR | MAHL [lbs]
92.4% | 8,230
93.4% | 9,477
94.4% | 11,170
95.4% | 13,598
RR | MAHL [lbs]
96.4% | 17,375
97.4% | 24,058
98.4% | 39,094
99.4% | 104,250
Notes: We just calculated the removal rate….now let’s see why this number is so important and why we want to make sure we have sampled, analyzed and interpreted the data to our best advantage….
This chart summarizes the BOD Maximum Allowable Headworks Loading for a typical small POTW….5.0 MGD and a 15 mg/l NPDES permit limit for BOD
The chart starts with 92.4% removal and increases in 1% increments...
The MAHL increase between 92.4% and 93.4% is modest….The MAHL increase between 98.4% and 99.4% is phenomenal….
Oh what a difference 1% can make………of even 0.1 % when you get up above 95%

## Slide 11: Developing Sampling Plan
General Considerations
Sampling Locations
Pollutants to be Sampled
Sampling Frequencies – Initial & Ongoing
Sampling Methods
Analytical Methods

## Slide 12: Developing Sampling Plan (cont.)
Examples:
Calculating Detention Time
Pairing Samples for Accurate Reff
Clean Sampling, Trace Metals Analysis

## Slide 13: Developing Sampling Plan (cont.) Effect of Analytical Method Selection 5.0 MGD Flow POTW, 0.050 mg/l Effluent Limit
Source/ Type of Metals Analysis | Removal Rate % | Allowable Influent Chromium | Chromium MAHL (pounds)
“Regular Level” | 54.5% | 0.11 mg/l | 4.6
Median Literature | 82% | 0.28 mg/l | 11.7
“Low Level” | 93.6% | 0.78 mg/l | 32.5
Notes: Combining the examples just talked about, we show

## Slide 14: Developing Sampling Plan (cont.)
POTW Flow = 3.5 MGD NPDES NH3-N Limit = 2.0 mg/l
INF | EFF | RR %
12.5 | <0.5 | 96.0
14.0 | <0.5 | 96.4
10.8 | <0.5 | 95.4
15.5 | <0.5 | 96.8
 | ADRE | 96.15
INF | EFF | RR %
12.5 | <0.1 | 99.2
14.0 | <0.1 | 99.3
10.8 | <0.1 | 99.1
15.5 | <0.1 | 99.4
 | ADRE | 99.25
MAHL = 7784 pounds NH3N
MAHL = 1516 pounds NH3N
Notes: Detection limits issues aren’t just limited to metals and just in case you thought they were…take a look at this ammonia-nitrogen data.
The only difference in these two MAHLs is the ammonia nitrogen detection limit used by the laboratory.
CLICK CLICK
Just as an aside, I don’t know of many industries who would be happy to learn that they had an ammonia limit in their SIU permit or were having to pretreatment for ammonia just because the POTW was not using the lowest detection limit possible for a particular parameter….
Just another one of the tricks of the trade…..a trick to prevent pretreatment and allow your POTW to best utilize its resources…your POTW was designed to treat ammonia…

## Slide 15: Calculating MAHL, Reff , MAIL Allocating Industrial Loadings
Statistical Methods
Method Detection Level Concerns
Negative Removal Efficiencies
Different Bases (WQ, Inhib., Biosolids, Air)
Safety Factors
“Uncontrolled” and Commercial Loadings
Notes:   Average Daily . . .
  Mean . . .
  Decile . . .
Mean removal efficiency does not indicate how often the derived removal efficiency was achieved.
The decile method requires at least nine daily removal efficiency values based on paired sets of influent and effluent data. However, instead of averaging the daily removal efficiency values, the decile method sorts daily removal efficiency data from lowest to highest and calculates the percentage of the daily removal efficiency above or below a specified removal efficiency. The methodology is similar to a data set median.
A median divides an ordered data set into two equal parts: half the data set is above the median, and the other half is below. The decile method is similar except it divides the ordered data set into 10 equal parts. Therefore, 10 percent of the data set is below the first decile, 20 percent of the data set is below the second decile, etc. The fifth decile is equivalent to the data set median.
MRE recommended over the ADRE by EPA
Decile approach allows for comprehensive view, and considers daily removal efficiency variation.
Individual decile estimates, depending on how conservative the POTW wants to be, can be less precise than the ADRE and MRE estimates.

## Slide 16: Developing Permit Limits
Once the MAIL is determined. . .
Limit Duration
Allocation Methods
  Advantages
  Disadvantages
Reassessments & Updating Local Limits
Notes: Limit Duration – Daily Maximums, Monthly Averages, Instantaneous Maximums
STRESS that EPA does NOT dictate allocation method
Reassessments –
Discussion of when and why to Reassess limits
Common Sense – laugh test
Process Changes
Compliance History

## Slide 17: Summary
WE NEED YOUR FEEDBACK!!
Submit Your Evaluation Forms!!
Email Us
Call Us