## Slide 1: The Mess in Missouri A Recreational Use Attainment Case Study
AMSA Summer Conference
July 21, 2004
Dorris Bender
Water Pollution Control
City of Independence, MO

## Slide 2: The Mess in Missouri
Background
  Clean Water Act (CWA) use designation requirements
  Missouri designated recreational uses and standards
Missouri Whole Body Contact Story
POTW Concerns and Actions

## Slide 3: CWA Section 101(a)(2)
National goal, wherever attainable, of “water quality which provides for . . . recreation in and on the water . . . .”
Commonly referred to as the “fishable/swimmable” goal

## Slide 4: 40 CFR 131.10 Designation of Uses
(a) Each State must specify appropriate water uses to be achieved and protected
(g) States may remove a designated use which is not an existing use or establish sub-categories of a use if the State can demonstrate that attaining the designated use is not feasible
  At least one of six listed factors must be satisfied to justify removal of designated use

## Slide 5: 40 CFR 131.10 Designation of Uses
(j) A State must conduct a use attainability analysis (UAA) whenever it:
  Designates uses that do not include “fishable/swimmable” uses
  Removes a designated “fishable/swimmable” use
  Adopts subcategories of “fishable/swimmable” uses which require less stringent criteria

## Slide 6: Missouri Designated Recreational Uses
Whole-body-contact recreation
Human health protection (Fish consumption and secondary contact recreation)
Boating and canoeing

## Slide 7: Whole Body Contact Recreation
“Activities in which there is direct human contact with the raw surface water to the point of complete body submergence. . . . Water so designated is intended to be used for swimming,water skiing or skin diving.”

## Slide 8: Classified Waters Designated for Whole Body Contact Recreation
Designated Use | Segments |  | Acres/Miles |  | 
 | Total | Percentage | Total |  | Percentage
All lakes | 455 |  | 293,257.8 | ac | 
WBCR lakes | 147 | 32.3% | 262,517.0 | ac | 89.5%
Other lakes | 308 | 67.7% | 30,740.8 | ac | 10.5%
All streams | 3751 |  | 22,217.8 | mi | 
WBCR streams | 285 | 7.6% | 5,531.5 | mi | 24.9%
Other streams | 3466 | 92.4% | 16,686.3 | mi | 75.1%

## Slide 9: Missouri Bacteria Criteria
Limited to classified waters designated for WBC recreation
Exemption for periods when the stream or lake is affected by stormwater runoff
Fecal coliform shall not exceed 200/100 ml
Seasonal from April to October
Year-round for losing streams and scenic waterways

## Slide 10: MO Disinfection Requirements POTWs and Other Domestic WWTF
Discharges within two miles upstream of WBC areas
Discharges to streams with 7-day Q10 flow of zero in metropolitan areas where stream is readily accessible to the public
Fecal coliform limits
  Monthly average – 400/100 mL
  Daily maximum – 1000/100 mL.

## Slide 11: Disinfection Waivers
Missouri Dept of Natural Resources (MDNR) May Waive Disinfection
  WWTF demonstrates that neither health nor water quality will be endangered by failure to disinfect
  NA to losing streams or scenic waterways.

## Slide 12: Other Designated Recreational Uses
Human Health Protection
  Fish consumption
  Secondary contact recreation
  Assumes limited physical contact with the water without likelihood of ingestion
  Not clear
  Numerical bacteria standard NA

## Slide 13: Other Designated Recreational Uses
Boating and Canoeing
  Limited contact with the water assumed
  58% of classified lakes designated
  7% of classified stream segments
  Numerical bacteria standard NA

## Slide 14: Missouri WBC Story
EPA review of Missouri Water Quality Standards (WQS)
State and environmental activist group responses

## Slide 15: EPA Review of Missouri WQS
EPA Region 7 letter of Sept 8, 2000, responded to 1994 and 1996 Missouri WQS changes
  Disapproved items (8)
  Existing provisions identified to be inconsistent with the Clean Water Act (2)
  Items for attention for next triennial review (12)

## Slide 16: EPA Region 7 Sept 2000 Letter
Region 7 intent to request the EPA Administrator to make a finding of inconsistency under the CWA for two existing standards provisions

## Slide 17: EPA Region 7 Sept 2000 Letter
Existing standards provisions identified:
  Outstanding National Resource Waters
  “Missouri’s failure to adequately justify a use designation lower than a ‘fishable/swimmable’ for all classified waters of the State that currently lack a whole body contact use designation. . .”

## Slide 18: EPA Region 7 Sept 2000 Letter
Referenced MDNR’s 1984 “A Whole Body Contact Recreation Use Attainability Analysis”
Directed the State to:
  Revise use classifications to protect fishable/swimmable uses for all classified waters, or
  Conduct a more thorough UAA

## Slide 19: State Response
3/8/01 – MDNR letter to EPA with a three year phased WQS revision plan
Phase 1, High Priority:
  New/revised provisions disapproved by EPA
  Existing provisions Region 7 identified as inconsistent with CWA
  High flow exemption
  Other items of State concern

## Slide 20: State Response
3/21/01 Missouri Clean Water Commission (MCWC) meeting – MDNR briefing on WQS revision plan
6 stakeholder meetings April – June 2001
WQS Phase 1 proposed rulemaking delayed

## Slide 21: Missouri Coalition for the Environment Notice of Intent
7/7/03 – Missouri Coalition for the Environment (MCE) Notice of Intent to sue EPA
Cited EPA’s failure to fulfill its duty under CWA to establish WQS for Missouri

## Slide 22: State Reactions
7/30/03 MCWC meeting – MDNR briefing on proposed WQS changes
  Draft Memorandum of Understanding (MOU) for WBC use assessment
  Phased approach
  Unevaluated waters to be designated for WBC effective July 1, 2008

## Slide 23: MCE v. Leavitt
Complaint filed Oct 7, 2003
16 claims for relief based on Region 7 Sept 2000 letter
Seeks EPA promulgation of revised WQS for Missouri, including:
  WBC recreation use designation for all waters
  Unclassified waters

## Slide 24: State Reactions
10/24 and 11/4/03 – Stakeholder meetings on draft MOU; no consensus reached with MCE and Sierra Club
1/7/04 – MCWC voted to designate classified lakes and streams as WBC upon effective date of WQS rule to be proposed July 2004; directed staff to determine compliance procedures and timeliness

## Slide 25: State Reactions
1/9/04 – MDNR Water Protection Program Director indicated that MDNR does not have the resources to conduct UAAs; UAAs will have to be performed by permitted facilities*
3/10/04 MCWC meeting – MCWC directed staff to research Kansas UAA procedures and report back 4/28/04

## Slide 26: State Reactions
4/28/04 MCWC meeting
  Proposed WQS rule to be published July 2004
  Final rule July 2005
  Staff report on Kansas UAA protocol
  Staff to adapt Kansas UAA protocol and work with stakeholders

## Slide 27: Draft UAA Guidance
MDNR distributed draft UAA guidance June 7, 2004
Stakeholder meeting June 15, 2004
Written comments by July 16, 2004
MDNR intends promulgation by rule

## Slide 28: POTW Concerns
WBC unrealistic use for many waters
  Low flow, restricted access, steep banks, channelization, etc.
  Current velocity, barge traffic
  Bacterial contamination not controllable
Inappropriate WBC designation may mislead the public

## Slide 29: POTW Cost Concerns
WWTF effluent disinfection
CSOs
SSOs
Urban storm water

## Slide 30: Disinfection Concerns
Safety issues (chlorine)
Water quality issues
  Total residual chlorine WQS = 10 µg/L
  Trihalomethanes SDWA MCL = 80 mg/L
Feasibility of disinfection alternatives

## Slide 31: POTW UAA Concerns
Draft UAA Guidance excludes urban areas
Implementation issues
  Workable procedures
  Timely approval process

## Slide 32: UAA Questions
Who – MDNR or stakeholders?
What documentation needed?
Where – how much of stream segment?
When to collect data?
How will UAAs be evaluated? How much evidence = “existing use”?

## Slide 33: POTW Options
Regulatory
Legislative
Legal

## Slide 34: Regulatory Arena
Urban Areas Coalition (UAC); other organizations
Meetings and informal contacts
Written comments
Public statements

## Slide 35: Legal Arena
AMSA/UAC Intervention – MCE v. Leavitt

## Slide 36: Legislative Arena
Monitor legislative activity
Draft proposed legislation?
  (e.g., Kansas Senate Bill 204)

## Slide 37: Missouri WBC Story
To be continued. . .