## Slide 1: City of New York Department of Environmental Protection
October 18-19, 2004
New York City’s Workplan for
CSO Water Quality Assessments and UAA
AMSA / CSOP / EPA Workshop
Chicago, Illinois

## Slide 2: New York City’s Approach to CSO Water Quality Assessments
Beginning in 1983, Efforts Focused on Priority CSO Tributaries with Significant Water Use Problems:
  Anoxia, bacteria, odors, floatables
Perform Detailed Data Collection, Modeling and Engineering To Define Knee-of-the-Curve Facility Plans
Resulting Issues
  Designated Water Quality Standards (WQS) may or would not be attained
  Not all designated uses are “fishable / swimmable”
  Concern that additional investment may be required
  Questions on permitting
Approach – Conduct Use and Standards Attainment (USA) Project and Long Term Control Plan (LTCP) Project

## Slide 3: Features of NYC’s USA and LTCP Projects
Demonstration Approach for LTCP
Waterbody / Watershed Assessments
  17 urban tributaries
  9 open water areas
Project Goals
  Identify current and desired water-based and shoreline uses
  Identify appropriate attainable uses with public/community involvement
  Reconcile water quality standards to highest reasonably attainable uses
  Provide basis for potential UAA
  Develop Long Term Control Plans

## Slide 4: USA / LTCP Project Waterbody/Watershed Assessments
Waterbody/Watershed Assessments
Obtain waterbody-specific information and historical data.
Review WQS, policies, local concerns/interests/issues, goals.
Identify, prioritize and rank all issues.
Develop and execute waterbody/watershed-specific data analysis.
Develop approaches to attain goals.
Evaluate alternatives to achieve goals.
Recommend uses and Water Quality Standards.
Develop waterbody/watershed plan.
Conduct preliminary environmental review.
Waterbody and Watershed Analyses
Computer Modeling and GIS
Facility Plan Assessment
Ecosystem Analyses
Land Use Analyses
Data Collection
Receiving Water Quality
Biology and Habitat
Shoreline Characterization
Engineering Analyses
Engineering Technologies
Innovative Approaches
Best Management Practices
Watershed Controls
Technology Ranking
Government Steering Committee
Waterbody/Watershed Stakeholder Teams
CSO Long Term Control Plan
WQSRR / UAA
26 Waterbody / Watersheds

## Slide 5: Agency and Public Participation
Government Steering Committee
  Provides program oversight with periodic meetings
  Represents EPA regional office, NYSDEC, and other federal, interstate and City agencies
Waterbody / Watershed Stakeholder Teams
  Includes community representation, local riparian and waterbody users, non-governmental organizations, and civic leaders
  Identify local uses and impairments
  Identify and prioritize local water use goals
  Comment on plans

## Slide 6: Ecosystem and Recreational Use Assessments
Ecosystem Use Evaluations
  Characterize current conditions
  Identify potential improvement in benthic diversity (TOC reduction)
  Identify potential improvement in fish diversity / abundance
  Assess habitat for spawning (suitability and significance)
  Compare to reference stations
Recreational Use Evaluations
  Identify stakeholders’ current and desired uses
  Evaluate potential suitability for primary contact
    - Physical nature (bulkheads, access)
    - Compliance with city / state regulations (e.g. beaches)
    - Safety (conflicts with recreational and commercial marine traffic)

## Slide 7: USA / LTCP Data Program (Historical and Current)
Goal: Characterize Current Conditions
  Watershed / Waterbody
  Dry and wet weather, short- and long-term
Methodology
  Compile past CSO facility planning projects’ and others’ data
  Supplement as necessary for USA / LTCP
Watershed Investigations:
  Sewer system configuration and performance
  Discharge volumes and pollutant loads (BOD, TSS, bacteria, others)
Receiving Water Investigations:
  Physical (dye, geometry, surficial geology, floatables)
  Chemical (DO, BOD, nutrients, Chl-a, TSS, SOD, bacteria, toxics, others)
  Biological (fish, icthyo, benthic infauna/epifauna, habitat)

## Slide 8: Historical / USA / LTCP Sampling Locations
Receiving Water Quality
Receiving Water Biology

## Slide 9: Waterbody/Watershed Mathematical Modeling Analysis
Modeling Methodology
  Open-Waters for regional and harbor-wide planning
  Tributaries for priority CSO planning
Watershed Models of Combined and Separate Sewer Systems
  Thirty-year effort
  Simple runoff to complex hydraulics (rational method, SWMM, InfoWorks)
  Detailed calibration to data
Receiving Water Models of Open Waters and Urban Tributaries
  Three-dimensional and time varying
  Hydrodynamics, eutrophication, DO balance, solids deposition, bacteria
  Detailed calibration to data
  Annual and multi-year simulations
Projection Conditions
  Baseline
  Alternative Facility Plans (up to 100% CSO abatement)
  Sewer Separation

## Slide 10: NYC Receiving Water Model Systems
Paerdegat Basin
Receiving Water Model
System-Wide Eutrophication Model
Jamaica Bay Eutrophication Model

## Slide 11: Comprehensive Engineering Evaluations for Long Term Control Planning
Nine Minimum Controls
  Maximize flow to WPCPs, etc.
Additional CSO Controls
  Storage / retention - inline, interceptors, tanks, conduits, tunnels
  Alternative Treatment - disinfection, high rate physical-chemical
  SCADA / Real Time Control
Receiving Water Controls
  Instream aeration / destratification
  Dredging / re-contouring
  End-of-Pipe floatables netting/booming and skimmer boats
Other Best Management Practices
  Water conservation
  Minimize runoff
  Green solutions

## Slide 12: Urban Tributary Example: Paerdegat Basin Waterbody/Watershed
Waterbody/Watershed:
  6,600 feet long, 500 feet wide
  No freshwater flow
  5,500 combined sewer acres
  375 separately sewered acres
  Approximately 70% impervious
  Population = 470,000
Combined
Separate
Paerdegat Basin
CSO
storm sewer
Observed Waterbody Uses:
  Recreational Boating
  Canoeing & Kayaking
  Fishing
Shoreline Activities:
  Bird watching
  Walking trails
  Marinas

## Slide 13: Paerdegat Basin CSO Control Plan
The Plan:
  20 MG in-line storage
  30 MG off-line facility
  Dredging as needed
  Riparian park designation
  Shoreline mitigation
  Community facilities
  $357,000,000 total cost
Plan Developed Using Knee-of-the-Curve Procedure Consistent with EPA Guidance
  Paerdegat Basin was presented by EPA as a CSO Control Policy case study
The Results
  Improved dissolved oxygen
  Reduced indicator bacteria
  Reduced sediment deposition
  Permanent floatables control

## Slide 14: Uses Projected After CSO Control Plan Implementation
Facility Plan Also Reduces:
  Floatable Materials by 91%
  Settleable Solids by 80%
Remaining Issue:
  Criteria for selecting use attainment level??
Paerdegat Basin (Head End) for an Average Precipitation Year
(2) 100% Compliance at Mouth
Standards Compliance
(1) Draft Proposed NYSDEC Chronic (Propagation) Criteria
(2)
Criteria Compliance
(2)
(1)
Base Case
Facility Plan
Sewer Separation
(2)
(2)
Base Case
Facility Plan
Sewer Separation
Standards Compliance
(2)
(2)
Base Case
Facility Plan
Sewer Separation

## Slide 15: Use Attainability in Paerdegat Basin
Factor 3 – Human-caused conditions …
  Impervious pavement, sewering and stormwater
    - Result in non-attainment of aquatic life protection, primary contact and aesthetic uses
    - Appear to cause adverse and irreversible impacts on benthic habitat/biota and affect aquatic life protection
Factor 4 - Dams, diversions and … hydrologic modifications …
  Hydrologic modification to Paerdegat Basin
    - Eliminated natural runoff which dilutes and transports pollutants
    - Altered the natural geometry and depth which impacts tidal flushing
    - Altered the natural contiguous wetlands/habitat
    - Resulted in significant impervious drainage area

## Slide 16: Physical Factors
Human-Caused Conditions …to the Watershed
Urbanization Has Increased:
  Drainage area imperviousness
  Watershed loads
  Magnitude and intensity of discharges
Paerdegat Basin Watershed

## Slide 17: Physical Factors (continued)
Hydrologic Modifications … to Paerdegat Basin
Physical Changes:
  Urbanization altered base freshwater flow
  Waterbody channelized and dredged
  Transformed from tidal creek to dredged drainage channel
  Altered shorelines
  Eliminated wetlands
Caused:
  Reduction of natural flushing
  Alteration of estuarine exchange
  Siltation and formation of sand bars
  Elimination of original habitat
Circa 1900
Today

## Slide 18: Paerdegat Basin Water Use / WQS Recommendations
Approve UAA
Establish a Mixing Zone at the Head End for “Benthic Organism Survival”
Classify Upper Basin for “Fish Survival”
Classify Lower Basin for “Fish and Aquatic Life Propagation”
Classify Entire Basin for “Modified Primary Contact Recreation”
  No bathing
  Restrict other primary contact uses during wet weather events
  Require advisory indicating use limitations
Upper Basin
Lower Basin
CSO Storage
Facility
Mixing Zone
4,250 feet
Recommended Aquatic Life Use Classifications

## Slide 19: Recommended Modifications to State Waterbody Classifications and Standards
Create “Urban Tributary” Classification
  Recognize wet weather conditions when designating uses and applying water quality standards
  Applicable to waterbodies that satisfy any UAA criterion
  - Consider developing generic procedure for testing with UAA criteria
  Baseline water uses:
  - Fish and aquatic life survival
  - Secondary contact recreation
  Other attainable higher uses to be dependent upon effectiveness of CSO Plans
  Facility Plan requirements
  - Based on knee-of-the-curve
  - Technically feasible and implementable
Modify Narrative Standards for Floating Materials and Settleable Solids To Limit “Amounts Which Impair Waters For Their Best Uses”

## Slide 20: Regulatory Reaction to USA Project / Paerdegat Basin UAA
NYSDEC
  Received waterbody/watershed facility plan (LTCP)
  Reviewing draft UAA but has not commented
USEPA Region 2 (Letter to NYSDEC)
  USA Project
  Considers USA Project very valuable for WQSRR
  Urges NYSDEC to complete revisions to WQS as applicable for harbor-wide TMDLs
  Considers completion of Paerdegat Basin Plan significant with possible application to other tributaries
  Paerdegat Basin
  Urges NYSDEC to adopt modified aquatic life use designations with application to other modified and altered urban systems
  Recommends NYSDEC to consider one of four primary contact recreational categories with possible suspension for specified wet event
  Recommends NYSDEC revise narrative criteria to protect best uses rather than require “none, in any amount”