## Slide 1: NPEs and the Pretreatment Program
David Dunlap
Uniform & Textile Service Assoc.
Dir. Government & Environmental Affairs
2005 Pretreatment & Pollution Prevention Workshop
Kansas City, MO
November, 18, 2005

## Slide 2: Today’s Questions
What are NPs, NPEs and APEs?
What is the state of NP science?
What is the regulatory status of NP?
What should one consider with regard to local NP pretreatment issues?

## Slide 3: What are NP, NPEs and APEs?

## Slide 4: Definitions
NP = Nonylphenol
NPE = Nonylphenol Ethoxylate
APE = Alkylphenol Ethoxylate
NPE is a subset of APE

## Slide 5: Nonylphenol
One of the major isomers
C
CH
CH2
CH3
CH2
CH3
CH2
CH3
CH3
OH

## Slide 6: What is NP?
Raw material used in the synthesis of NPE
Intermediate in the anaerobic biodegradation of NPE

## Slide 7: Nonylphenol Ethoxylates
One of the major isomers
C
CH
CH2
CH3
CH2
CH3
CH2
CH3
CH3
O
(CH2CH2O)n H
n = 1 - 100

## Slide 8: What are NPEs?
High performance, cost-effective, “workhorse” surfactants
Excellent wetting agents, emulsifiers and dispersants

## Slide 9: What Does the Science Say about NP/NPEs ?

## Slide 10: State of the Science Human Health
NP exhibits weak estrogenic activity
  10,000 to 1,000,000 times less potent than human estrogens
NPEs used in laundry detergents are not estrogenic
Hormones from human waste are the primary source of estrogenic activity in wastewater and the environment

## Slide 11: State of the Science Human Health
US, EU and Canadian Risk Assessments - conclusions concur
  Normal exposure to NP and NPE does not pose a significant risk to human health.
No link between NP exposure and endocrine disruption in humans

## Slide 12: State of the Science Aquatic Impact
Numerous aquatic NP/NPE studies with dozens of species
Endocrine issue is well understood
Effect levels for chronic toxicity are lower than those for endocrine related effects
Aquatic toxicity, not endocrine issues, drive risk assessment conclusions

## Slide 13: State of the Science Biodegradation
NP is a minor product of NPE biodegradation
NP/NPE are inherently biodegradable
The aromatic ring breaks down during biodegradation

## Slide 15: State of the Science Bioaccumulation
NP/NPEs are not considered bioaccumulative in accordance with established national and international criteria
NP/NPEs are rapidly metabolized and excreted by fish and humans

## Slide 16
Commercial NPEs are not estrogenic
NP is a minor degradation product of NPE - anaerobic degradation intermediate
Aquatic toxicity of NP not endocrine issues drive risk assessment conclusions
NP/NPEs are not PBT chemicals
Governmental risk assessments have concluded that environmental exposure to NP/NPEs does not present a risk to humans
Scientific Summary …

## Slide 17: What Is The Regulatory Status of NP/NPEs in the US?

## Slide 18: Proposed EPA Water Quality Criteria for NP
Chronic Freshwater: 5.9 µg/L
Acute Freshwater: 27.9 µg/L
Chronic Saltwater: 1.4 µg/L
Acute Saltwater: 6.7 µg/L

## Slide 19: Aquatic Levels of NP/NPE in the United States
US 30 Rivers Study (Weeks et al., 1996)
  In coordination with US EPA
  NP median = 0.1 µg/L
National Reconnaissance Survey (Kolpin et al., 2002)
  Sponsored by the USGS
  NP median = 0.8 µg/L
Very few values exceed the WQC

## Slide 20: NP/NPE Pretreatment Considerations

## Slide 21: Pretreatment Know the Facts
There is a difference between NP and NPE
NP is not the predominant degradation product of NPE
NP/NPE are both effectively (95%) removed from effluent in well-functioning secondary sewage treatment plants

## Slide 22
EPA has created a clear bright line with the NP WQC
The aquatic environment is protected by the WQC
Pretreatment WQC Established

## Slide 23
The majority of POTWs will not have an issue with NP
POC – weigh relative risk - e.g. NPEs vs. Pharmaceuticals
Source - domestic vs. industrial / uncontrollable vs. controllable
Impact of alternatives (toxicity, BOD load, biodegradability, pass through)
Pretreatment Do Your Due Diligence

## Slide 24
Identification vs. Impact - Does the POTW or receiving stream have a problem?
Safety factors
MAHL allocation
Reality check
Sound science not emotion or politics
Pretreatment Local Limit Development

## Slide 25
THANKS
David Dunlap
Uniform & Textile Service Association
ddunlap@utsa.com
www.utsa.com
Barbara Losey
Alkylphenols & Ethoxylates Research Council
blosey@regnet.com
www.aperc.org