## Slide 1: Effluent Guidelines: An Update
Presented to: NACWA 2005 National Pretreatment & Pollution Prevention Workshop Kansas City, MO | Presented by: Carey A. Johnston, P.E. U.S. EPA, Office of Water Washington, DC
16 November 2005

## Slide 2
Presentation Overview
Update on Current Effluent Guidelines
  Airport Deicing Operations
  Drinking Water Treatment
  Chlorine and Chlorinated Hydrocarbons Manufacturing
  (e.g., vinyl chloride, chlor-alkali manufacturing)
Update on preliminary 2006 Effluent Guidelines Program Plan
POTW Study Update
Future Directions

## Slide 3
Airport Deicing Operations
Identified for ELG rulemaking in 2004 Effluent Guidelines Program Plan (9/2/04; 69 FR 53705). Currently no ELGs.
Discharges from deicing operations have the potential to cause fish kills, algae blooms, and contamination to surface or ground waters. Current annual discharge estimate: 21 million gallons of deicing fluids.
In the last year EPA worked with industry and NACWA and has conducted 20 site visits and sampling (w/ more this winter).
EPA is also developing three surveys –one for airports and two for airlines to assist in data collection for its engineering and economic, and environmental analyses.

## Slide 4
Drinking Water Treatment
Identified for ELG rulemaking in 2004 Plan (9/2/04; 69 FR 53705). Currently no ELGs.
Discharge from drinking water facilities have the potential to discharge significant quantities of conventional and toxic pollutants, including metals, chlorine, and salts.
In the last year EPA has worked with industry and NACWA and conducted numerous site visits.
EPA has focused its rulemaking on utilities serving more than 10,000 people and is developing two surveys (screener, detailed) to assist in data collection for its engineering and economic, and environmental analyses.

## Slide 5
Chlorine and Chlorinated Hydrocarbons Manufacturing
Identified for ELG rulemaking in 2004 Effluent Guidelines Program Plan (9/2/04; 69 FR 53705). Currently regulated by Parts 414 & 415.
Discharges from vinyl chloride and chlor-alkali manufacturing might contain significant quantities of toxic pollutants, including dioxin.
EPA delayed start until March 2005 and has since started work with industry and has conducted site visits.
EPA is planning to send a questionnaire to all facilities in the scope of the rulemaking in 2006. EPA is also planning to conduct multiple-day sampling episodes in 2006.

## Slide 6
Effluent Guidelines Planning: Direct Dischargers
The 1987 Clean Water Act Amendments added Section 304(m), which re-enforced Congress’ intent that effluent guidelines keep pace with pollution prevention and treatment technology
EPA must review all promulgated effluent guidelines annually
Every other year: after proposal and public comment, EPA must publish a two-year plan for the guidelines program which:
  Identifies and establishes a schedule for any effluent guidelines revisions
  Identifies any industries not currently subject to effluent guidelines that discharge nontrivial amounts of toxics and establishes a schedule to take final action within three years

## Slide 7: Effluent Guideline Planning: Indirect Dischargers
For indirect dischargers, Clean Water Act requires:
  Promulgation of pretreatment standards if there is pass through or interference at POTWs
  Annual review of existing categorical pretreatment standards to identify candidates for revision
      No publication requirement
  As good government practice, we include findings in the Preliminary and Final Effluent Guidelines Program Plans
      Previous plans included review of existing pretreatment standards
      2006 Preliminary Plan also includes findings for potential new categories

## Slide 8
Involve stakeholders from the start of the Plan
Assure transparent decision-making
Evaluate sound information against broad and balanced decision criteria
Effluent Guidelines Planning: Goals

## Slide 9
Pollutant discharges by industrial category
Current and potential technology and pollution prevention options by industrial category
Economic considerations – growth, affordability
Implementation/efficiency considerations of revising existing effluent guidelines or publishing new effluent guidelines
Review of Existing Effluent Guidelines: Factors

## Slide 10
Screening level review to identify categories needing further investigation
Prioritizing candidates using selection criteria
In-depth review to characterize industry categories
Decide on course of action
Present decisions in final Plan
Review of Existing Effluent Guidelines: Phased Process
Notes: Developing an effluent guidelines biennial plan is a two year process consisting of:
  Two annual reviews (odd and even year)
  Preliminary Plan (odd year)
  Describes the methodology and data used in the odd year review
  Identifies and prioritizes categories for detailed studies or additional study but does not propose categories for rulemaking
  Solicits public comment on annual review and preliminary plan.
  Final Plan (even year)
  Describes the methodology and data used in the even year review
  Selects categories for revision, if appropriate
  Identifies industrial categories without existing guidelines discharging non-trivial toxic or non-conventional pollution
  Identifies schedules for any identified effluent guidelines rulemakings
  Solicits public comment on annual review

## Slide 11
Data from TRI, PCS, and the U.S. Census were the major sources of data used in the 2005 annual review
These data sources have sufficient data to support a national comparison and prioritization of the 56 existing industry categories.
Industry-supplied information
Literature
Permitting authorities
Regulated Facility
Sampling or Pollutant
Discharge Estimation
EPA reviews
PCS/TRI data
Data Compiled in PCS &
TRI Databases
Screening Level Review for 2005

## Slide 12
Facilities
  No central database for indirect dischargers
  Primary industry SIC classifications do not directly correspond to an ELG category or wastewater generating operations
Pollutants:
  PCS only contains information for regulated pollutants for ~10% of direct discharging industrial facilities
  TRI reporters often estimate pollutant discharges (e.g., using method detection level) or report releases as ranges
  Lack of toxic weighting factors for some reported pollutants
  Nutrients not fully addressed through toxic weighting factors
  Non-process events (e.g., oil spills) included in environmental release estimates
  All data is reviewed for quality and accuracy - significant effort!
Data/Methodology Challenges

## Slide 13
Technology:
  No central database for technology for each industrial category
  Current treatment-in-place and technology performance data is not readily available
Environmental Impacts
  Lack of data prevents the assessment of potential environmental impacts from industrial discharges
  Some preliminary screening analyses can be done with nutrient modeling for industries undergoing detailed review
Data/Methodology Challenges (cont.)

## Slide 14: Identifying and Prioritizing Categories for Detailed Studies or Additional Study
Calculate two measures of loadings (or toxic weighted pound equivalents) for a category using data in PCS and TRI
  TRI loadings reflect direct and indirect dischargers
Develop a single loading for each category by adding the toxic weighted pound equivalents (TWPE) calculated with PCS data and TRI data
  May double count some pollutants at some facilities
  However, this approach focuses our resources on categories that rank high using both data sources or which have high TWPE in only one source
Prioritized the 13 categories cumulatively discharging 95% of total TWPE for further review
Prioritized the Top 2 categories for detailed studies:
  Pulp, Paper, and Paperboard
  Steam Electric Power Generation
Prioritized the remaining 11 categories for additional study

## Slide 15: New Effluent Guidelines Evaluation: Possible Identification of New Categories of Direct Dischargers
EPA must identify potential new categories of point sources directly discharging toxic or non-conventional pollutants :
  Legislative history says EPA must address “significant” or “nontrivial” discharges.
  If identified, EPA must establish a schedule for taking final action within 3 years
Our evaluation includes the following questions:
  Is this a new category or is this a new subcategory of an existing ELG?
  Are facilities in this category direct dischargers?
  Does this category, as a whole, discharge non-trivial amounts of toxic or non-conventional pollutants?

## Slide 16: Findings of New Effluent Guidelines Evaluation
Tobacco Products Processing (SIC 21)
  Identified in comments to the preliminary 2004 plan
  Sparse data in PCS and TRI
EPA will complete a detailed study for this industrial sector for the final Plan
This detailed study will include site visit and sampling data recently collected by EPA

## Slide 17: New Pretreatment Standards Evaluation: Possible Identification of New Categories of Indirect Dischargers
EPA stakeholders identified the following indirect dischargers for this review:
  Food Service Establishments
  Industrial Laundries
  Photoprocessing
  Printing and Publishing
  Hospitals
  Independent and Stand Alone Laboratories
  Offices and Clinics of Dentists
  Industrial Container and Drum Cleaning (ICDC)
  Veterinary Care Services
  Health Care Services

## Slide 18: New Pretreatment Standards Evaluation: Possible Identification of New Categories of Indirect Dischargers
Is there pass-through?
  For most industries, we did not calculate the actual amount of pass through. Instead, we looked at one or more of the following:
    Potential pass through based on the total annual TWPE per facility
    Potential pass through at national level based on total annual TWPE for all indirect dischargers in an industrial category
Is there interference?
  Evaluated anecdotal and qualitative information
If potential pass through/interference: then look at “appropriate factors”:
  Amount of wastewater pollution discharged and relative toxicity
  Whether other regulatory tools (e.g., local limits set by POTWs, voluntary initiatives) would be more appropriate
  Cost effectiveness ($/TWPE) of potentially available technology options

## Slide 19
Pass through potential (measured as total annual TWPE discharged per facility) represents few toxics per facility – therefore, national regulation is not warranted at this time
Food Service Establishments
Industrial Laundries
Photoprocessing
Printing and Publishing
Interference from conventional-type pollutants can be adequately addressed by Part 403 requirements and enforcement
Food Service Establishments
Findings of New Pretreatment Standard Evaluation: National Categorical Pretreatment Standards May Not Be Necessary

## Slide 20: Findings of New Pretreatment Standard Evaluation: Additional Data Collection or Analysis May Be Necessary
Recommend grouping the following industrial sectors into a possible “Health Services Industry” category:
  Independent and Stand Alone Medical and Dental Laboratories
  Offices and Clinics of Doctors of Medicine
  Offices and Clinics of Dentists
  Nursing and Personal Care Facilities
  Veterinary Care Services
  Hospitals (existing ELG for hospitals – no pretreatment standards)
Limited data in PCS and TRI
  - All or nearly all of these facilities discharge to POTWs
  - Pollutants of concern can include silver, phenols, barium, acetone, and mercury
  - Hospital industry current subject to 1998 EPA/Industry MOU and recent Regional enforcement initiatives to promote EMS
Industrial Container Drum Cleaning (ICDC)
  Conducting formal pass through analysis using information from a 2002 detailed study

## Slide 21
Website: http://www.epa.gov/guide/plan.html
Docket: Most record documents, including all public comments, can be viewed online at:
http://www.epa.gov/edockets
(Docket #OW-2004-0032)
Comment Period Closes: 28 November 2005
Contact:
  Carey Johnston, Project Lead, 202-566-1014, johnston.carey@epa.gov
For Further Information…

## Slide 22
EPA last evaluated POTW performance in late 1970s/early 1980s:
  Characterized occurrence and fate of the 129 priority pollutants in POTW influent, effluent, and sludge
  Collected data from 50 POTWs that met the criteria for secondary treatment
  (Effluent BOD5 & TSS <30 mg/l)
Document in report titled, “Fate of Priority Pollutants in Publicly Owned Treatment Works,” EPA 440/1-82/303, September 1982.
New EPA POTW Study: Background

## Slide 23: New EPA POTW Study: Changes Since 1982
Level of treatment at POTWs more likely to be meeting or exceeding secondary treatment
Increased installation of advanced treatment technologies
  Nutrient removal technologies
  Advanced oxidation
Increasing pressure based on local water quality concerns
Increased concern regarding emerging contaminants in the environment:
  Endocrine disruptor compounds (EDCs), including hormones
  Pharmaceuticals and personal care products (PPCPs)
  Surfactants
  Brominated flame retardants

## Slide 24
Characterize treatment performance for conventional, non-conventional & priority pollutants (well-designed, well-operated POTWs)
Establish current baseline for POTW raw waste characteristics
Expand number of pollutants analyzed over the 1982 “50-POTW Study,” especially for “emerging pollutants of interest”
For POTWs with “advanced” treatment unit operations or treatment configurations, characterize the performance for selected pollutants
Determine the types of standard secondary and advanced treatment equipment and operating conditions that remove selected “emerging pollutants of interest”
New EPA POTW Study: Study Objectives

## Slide 25
Conduct “Screen Sampling” visits to collect 24-hr composite influent & effluent wastewater samples & 1 sludge grab sample
Conduct one four-day “performance sampling”
Facilitate analytical methods development for more sensitive methods (lower MDLs) and for emerging pollutants of interest
Will measure 670 analytes including 110 emerging pollutants of interest
New EPA POTW Study: Current Work (2006)

## Slide 26
In September 2005, provided EPA’s lists of
  670 analytes & related analytical methods
  53 candidate POTWs for screen sampling
Requested NACWA’s comments as well as other good sampling candidates
Welcome well-documented historical data
New EPA POTW Study: NACWA Coordination

## Slide 27
Well-designed & well-operated during the period of record
Meet criteria for secondary biological or advanced treatment
Document analytical methods & changes in design &/or operating conditions during the period of record
New EPA POTW Study: Historical Data Acceptance Criteria

## Slide 28
Future Directions
Some of the benefits of electronic data reporting include:
  - Better data for answering questions on the potential impacts (or lack thereof) of industrial wastewater discharges;
  - Improved public access to environmental release data;
  - Better tracking of environmental releases to help operators improve their pollution prevention programs; and
  - Potential reductions in paperwork transaction costs from existing reporting efforts (currently these transactions are mostly done with paper).
Working on guidance documents & FAQs for Aquaculture, Pharmaceuticals, & CWT.
Improving Effluent Guidelines Website
Evaluating opportunities of the Cross-Media Electronic Reporting Rule (CROMERR)
(October 13, 2005; 70 FR 59847) which provides the legal framework for electronic reporting under all of EPA's environmental regulations.

## Slide 29
Questions/Thoughts?

## Slide 30
For More Information…
Further updates on the EPA’s effluent guidelines program including electronic copies of EPA supporting analyses and Federal Register notices can be found at:
http://www.epa.gov/guide/
EPA ELGs contacts are:
Name | Effluent Guideline | Phone | E-mail
Jan Pickrel | Pretreatment Program | (202) 564 7904 | pickrel.jan@epa,gov
Greg Schaner | Pretreatment Streamlining | (202) 564 0721 | schaner.greg@epa.gov
Carey Johnston | 304(m) Planning | (202) 566 1014 | johnston.carey@epa.gov
Eric Strassler | Airport Deicing | (202) 566 1026 | strassler.eric@epa.gov
Tom Born | Drinking Water Treatment | (202) 566 1001 | born.tom@epa.gov
Samantha Lewis | Vinyl Chloride & Chlor-Alkali Manufacturing | (202) 566 1058 | lewis.samantha@epa.gov
Woody Forsht | POTW Study | (202) 566 1025 | forsht.elwood@epa.gpv