## Slide 1: Controlling Emerging Pollutants Through Pretreatment and Pollution Prevention
Paul Martyn, Industrial Waste Section Head
Sanitation Districts of Los Angeles County
1955 Workman Mill Road, Whittier CA 90601
562/699-7411, x2902
pmartyn@lacsd.org
SANITATION DISTRICTS OF LOS ANGELES COUNTY

## Slide 2: LA County Sanitation Districts
11 wastewater treatment plants
Serve 5.5 million residents
1240 SIUs
Extensive water reuse
  including groundwater recharge
Receiving waters include effluent-dominated water bodies

## Slide 3: Pressures to Address Emerging Pollutants
CA Department of Health Services
  Guidance on indirect potable reuse of wastewater
  Push for source control
NPDES requirements
Minimize public perception problems with existing reuse projects
Existing and potential drinking water standards

## Slide 4: Long Beach WRP Barrier Project
Injection of recycled water into groundwater basin
  Water Replenishment District of Southern California
  2.7 MGD into Alamitos Seawater Barrier
  Microfiltration/RO/UV treatment
Requirements
  Operate pretreatment program and other source control programs in a manner to minimize the likelihood of contamination with toxic chemicals
  State may designate contaminants for inclusion in the pretreatment program
  Develop a “proactive” program for maintaining an inventory of compounds discharged to the sewer system

## Slide 5: General Action - Inventory
Worked with local fire department to gain access to their databases of hazardous chemicals
Prepared fact sheets on chemicals of concern
  Chemical classification
  Synonyms
  Water quality standards
  Uses
  Wastewater sources

## Slide 6: Are Pharmaceuticals Really a Pretreatment Issue?
Widely present in surface water bodies
Known impacts on aquatic life
Concern about potential human health impacts
Disposal may represent a sizable portion of drugs entering sewers
Reasonable and prudent to act now to minimize discharges

## Slide 7: Excretion Percentages – Top 10 US Pharmaceuticals in 2003
Lipitor - cholesterol reduction – < 2% excreted
Zocor – cholesterol reduction – < 0.5% excreted
Prevacid – ulcers - < 1% excreted
Procrit – anemia – < 5% excreted
Zyprexa – antipsychotic – 7% excreted
Epogen – anemia – < 5% excreted
Nexium – acid reflux - < 1% excreted
Zoloft – antidepressant – 14% excreted
Celebrex – anti-imflammatory - < 3% excreted
Neurontin – antiseizure – 100% excreted
Leading OTC drug: Ibuprofen – 10% excreted

## Slide 8: Lindane Leaving LACSD Water Reclamation Plants
CTR
Limit, MUN
Lindane Source Control
19 ppt

## Slide 9: Dischargers of Pharmaceuticals
Hospitals
Long Term Care Facilities
Other Medical Facilities
Homes

## Slide 10: Hospitals/Medical Facilities
Multiagency effort to prepare guidance
CA Department of Health Services, CA Healthcare Association, Kaiser Permanente, CA legislature
DHS and Tri-TAC issued guidance memos
Publicized via widespread distribution and talks at workshops
Facilities encouraged to reduce pharmaceutical discharges to the “extent feasible”

## Slide 11: Recommended Disposal Strategy
RCRA Hazardous Waste
Sewer
Medical Waste
RCRA Hazardous
IV bags with salts/nutrients
Everything else

## Slide 12: Proposed Policy
“No user shall discharge pharmaceutical waste directly or indirectly to sewerage facilities except liquids containing only saline solution, lactate, nutrients such as glucose (e.g., D5W), vitamins, and added salts such as potassium and/or other electrolytes. The term “pharmaceutical” refers to both prescription and over-the-counter drugs.”

## Slide 13: Proposed Policy
May 2004 meeting with hospitals, hospital trade associations
  Serious resistance
  Mostly a cost issue
  Agreed to return with a counterproposal
Needs further follow up
Will address hospices, medical clinics, dentists, veterinarians, etc. once policy is established

## Slide 14: Residential Outreach
Partnership
  CPhA, LACSD, City of LA, OCSD, other POTWs
  Millions of cards to be distributed with prescriptions at pharmacies
  Web site for more info
  Launch expected early 2006
Hurdles overcome – disposal
  Strategy is HHW roundup or solid waste
  Not applicable in all areas

## Slide 15: Residential Outreach
Hurdles overcome - DEA
  No controlled substances at collection events without law enforcement present
  Solved by not accepting controlled substances
  Need national policy changes
National effort
  Product Stewardship Institute
  National dialogue
  Funding issues being resolved

## Slide 16: Are Pesticides a Pretreatment Issue?
They should NOT have to be one
EPA has a statutory obligation to ensure pesticide use doesn’t cause environmental harm
EPA systematically reregistering pesticides and needs to adequately address wastewater impacts
Strategy is to submit comments on registrations, so we don’t have to do extensive source control later
Working with NACWA on comments

## Slide 17: Permethrin
Broad spectrum pesticide
Widespread conversion to pyrethroid pesticide family with chlorpyrifos and diazinon ban for urban areas
Used in permethrin-impregnated clothing, pet shampoos, head lice shampoo, scabies cream
EPA did consider sewer pathway when doing risk assessments for reregistration
  Only second time done
  First was with lindane

## Slide 18: Permethrin
Didn’t consider effluent-dominated waterbodies or POTWs with no mixing zones or dilution
Found that potential environmental concentrations from the sewer pathway were up to 100 times the level of concern
Did not propose any mitigation measures for sewer pathway
NACWA requested that EPA not allow registration of permethrin products with sewer pathways

## Slide 19: Other Pesticides
Pyrethrin
  Natural version of permethrin
  Uses include head lice shampoo and pet shampoos
  EPA didn’t consider sewer pathway
Malathion
  Uses include head lice shampoo
  EPA didn’t consider sewer pathway
Metam sodium
  Inert ingredients in sewer root killer contains excessive NDMA, not considered by EPA
  Fumigant, safety of downstream sewer workers not adequately considered

## Slide 20: General Pesticide Issues
EPA is revising data needed to register pesticides
  Currently, pesticide manufacturers don’t run aquatic toxicity tests on same species as POTWs
  Asked for the tests to match
EPA is evaluating new pesticide registration review procedures
  Asked for assessment of sewer pathways where appropriate
  Asked for adequate opportunities and time for public comment
  Asked them to be consistent with Office of Water on water quality standards
  Office of Pesticide Programs runs its own analysis to determine acceptable water quality amounts