## Slide 1
http://www.ce.ncsu.edu/research/frog/

## Slide 2: Pretreatment Streamlining Rule
Overview of Changes to the
National Pretreatment Regulations
Jan Pickrel – EPA Office of Water, Water Permits Division
November 16, 2005
NACWA 2005 National Pretreatment & P2 Workshop, Kansas City, MO

## Slide 3: Pretreatment Streamlining Rule
Published in Federal Register on October 14, 2005
Effective November 14, 2005
70 FR 60134-60198

## Slide 4: Active Stakeholders
NACWA, WEF and Other POTWs
Industrial Users
  Metal Finishers
  Synthetic Organic Chemical Manufacturers Assoc. (SOCMA)
  Small Business Administration
Approval Authorities (Regions/States)
Natural Resources Defense Council

## Slide 5: Pretreatment Streamlining Overview
Regulation Revised -- 11 Major Topic Areas
Sampling for Pollutants Not Present
General Control Mechanisms
Best Management Practices (“BMPs”) as Local Limits
Slug Control Plans
Equivalent Concentration Limits for Flow-Based Standards
Use of Grab and Composite Sampling
Significant Noncompliance Criteria (“SNC”)
Removal Credits
Equivalent Mass Limits for Concentration Limits
Oversight of Categorical Industrial Users
Miscellaneous Changes

## Slide 6: Summary of Final Rule Changes
Issue | Rule Change
Pollutants not present | CAs can grant sampling waivers where CIU demonstrates that a regulated pollutant is neither present nor expected to be present
General control mechanisms | CAs may issue general control mechanisms to groups of SIUs that are substantially similar
BMPs as local limits | BMPs may be used in lieu of numeric local limits
Slug control plans | POTWs may determine how often they evaluate SIUs for the need for slug control plans or other requirements Any requirements must be reflected in control mech.
Equivalent Conc. Limits | CAs can use existing concentration-based standards instead of converting to flow-based mass limits for CIUs in OCPSF, Petroleum Refining, Pesticide Chemicals
Grab and Composite Sampling | Clarifies and updates application of sampling requirements; Provides flexibility to CA in certain sampling protocols
SNC – Publication | POTW can publish SNC violations in any paper of general circulation

## Slide 7: Summary of Final Rule Changes (cont’d)
Issue | Rule Change
SNC – Applicability | SNC criteria apply only to SIUs and to those IUs that have adversely affected pretreatment program
SNC – Daily Max. or Avge. Limits | Broadens scope of violations covered by chronic, TRC, and other violations
SNC – Late Reports | SNC violation occurs when reports submitted more than 45 days after deadline
SNC – TRC, Rolling Quarters, pH | No changes made to Pre-Streamlining rules
Removal Credits - Overflows | Retains and updates Pre-Streamlining formula to adjust removal credits by number of hours of sewer overflows per year
Removal Credits – Sewage Sludge | ANPRM asks for comment on adding pollutants to list of chemicals eligible for removal credits, and on potential ways to streamline consistent removal requirements
Miscellaneous Changes | Updates or corrects provisions re: to signatory requirements, net/gross calculations, requirement to report all monitoring data, and notification of changes

## Slide 8: Summary of Final Rule Changes (cont’d)
Issue | Rule Change
Equivalent Mass Limits | CIUs can request, and Control Authorities have discretion to approve, the conversion of concentration-based categorical standards to equivalent mass limits
CIU Oversight | Establishes Non-Significant CIU (NSCIU) category (discharges < 100 gpd) CIU reporting can be reduced to yearly compliance certification CA oversight can be reduced to annual evaluation of the CIU’s certification Establishes “Middle Tier” CIU category (discharges don’t exceed (a) the smaller of 5,000 gpd or 0.01 % of POTW design dry weather hydraulic capacity; (b) 0.01 % of POTW design organic treatment capacity; and (c) 0.01 % of the MAHL CIU reporting can be reduced to once annually CA oversight can be reduced to one inspection and sampling event every other year

## Slide 9: Pollutants Not Present
Pre-Streamlining Rules
CIUs must sample for all pollutants covered by the categorical standard, regardless of whether pollutant is present
Final Rule
If CIU can demonstrate a pollutant is not present in its process waste stream or is present only in background levels in intake water, the CA may authorize a sampling waiver for the pollutant
At least one representative process wastewater sample must be taken prior to treatment
Waiver valid for one term of control mechanism (like NPDES provision)
Where to find rule changes?
40 CFR 403.8(f)(2)(v)
40 CFR 403.12(e)(2)
Notes:   Authorization is subject to conditions: 403.12(e)(2) –
  CA may authorizae a waiver where a pollutant is determined to be present solely due to sanitary wastewater discharged from the facility provided that the sanitary wastewater is not regulated by an applicable cat. Std and otherwise includes no process wastewater;
  monitoring waiver is valid only for permit effective period, no case longer than 5 years. New waiver request must be submitted for each permit term
  IU must provide data from at least 1 representative sampling of the process wastewater prior to any treatment. Request must be signed & certified. Non-detectable results may only be used as demo that pollutant not present if lowest min. det. Level method approved by EPA was used in the analysis
  Any waiver must be cited as condition in the IU permit; supporting reasons/info must be maintained by the CA for 3 years after expiration of permit
  IU must certify on each report (special statement) that there has been no increase in the pollutant in the wastewater due to activities
  If waived pollutant is found present or expected present based on changes, IU must immediately comply with more frequent monitoring requirements and notify CA
  Provision does not supersede cat std requirements
Must this rule change be adopted by the CA?
No – this provision is optional

## Slide 10: General Control Mechanism (Permits)
Pre-Streamlining Rules
SIUs must be controlled through permits or equivalent mechanisms
EPA emphasizes the importance of evaluating each SIU individually
Final Rule
Allows POTWs to control SIUs through general permits where the necessary legal authority exists and the SIUs meet the criteria for being substantially similar
  Coverage not allowed for CIUs subject to production-based mass limits, mass limits/day, or limits based on Combined Wastestream Formula or Net/Gross calc.
  CA may choose to make coverage optional or required
Where to find rule changes?
40 CFR 403.8(f)(1)(iii)
Notes: Same or substantially similar types of operations;
Discharge the same types of wastes
Require the same effluent limits
Require same or similar monitoring
In the opinion of the PAOTW, are more appropriately controlled under a general control mechanism than under individual control mechanism
SIU ;must file a written request for coverage that identify contact info; production processes, types of wastes generated, monitoring location, all requests for monitoring waivers ( pollut not present)
Available for mass local limits
Must this rule change be adopted by the CA?
No – this provision is optional

## Slide 11: BMPs as Local Limits
Pre-Streamlining Rules
Pretreatment rules are silent on whether POTWs can use BMPs (rather than numeric limits) to satisfy their requirement to develop local limits
Final Rule
Clarifies that BMPs developed by POTWs may serve as local limits
POTWs must document the supporting rationale for specific BMPs
Where to find rule changes?
40 CFR 403.3(e) - Definition
40 CFR 403.5(c)(4)
40 CFR 403.8(f)
40 CFR 403.12(b), (e), (h)
Notes: BMPs includes:
Schedules of activities
Prohibitions of practices
Maintenance procedures,
Treatment requirements
Operating procedures
Practices to control plant site runoff, spillage or leaks, sludge or waste disposal, raw materials storage
403.8(f)(2)(vii)(H) – allows violations of BMPs to qualify for SNC
Must this rule change be adopted by the CA?
No – this provision is optional

## Slide 12: Slug Control Plans
Pre-Streamlining Rules
Slug discharges are prohibited
  POTWs must evaluate, at least once every two years, whether each SIU needs a plan to control slug discharges
  EPA has historically emphasized that a plan is not required
Final Rule
Provides POTWs the flexibility to review the need for a slug control plan or other requirements as necessary
Requirements must be included in control mechanism
Where to find rule changes?
40 CFR 403.8(f)(1)(iii)(B)(6)
40 CFR 403.8(f)(2)(vi)
Notes: 40 CFR 403.8(f)(1)(iii)(B)(6) – that requirements for a slug plan (if necessary) need to be in the permit
40 CFR 403.8(f)(2)(vi) – includes dates such that the time starts “from this date forward” – must be evaluated within 1 year of being designated an SIU; SIU must immediately report to CA any facility changes that could affect potential for a slug discharge
Must this rule change be adopted by the CA?
Yes – the provision requiring that slug discharge requirements be incorporated into the SIU’s control mechanism must be adopted
(40 CFR 403.8(f)(1)(iii)(B)(6))

## Slide 13: Equivalent Concentration Limits
Pre-Streamlining Rules
No allowance for equivalent concentration limits where categorical standard requires a mass limit to be calculated based on the facility’s flow
Affected CIUs
OCPSF - 40 CFR 414
Petroleum Refining (Cr and Zn) – 40 CFR 419
Pesticide Chemicals – 40 CFR 455
Final Rule
For CIUs subject to OCPSF, Petroleum Refining, and Pesticide Chemicals allows POTW to use concentration limit in categorical standard
Requires CA to document that dilution is not being substituted for treatment
Where to find rule changes?
40 CFR 403.6(c)(6)
Notes: Must this rule change be adopted by the CA?
No – this provision is optional

## Slide 14: Use of Grab/Composite Samples
Pre-Streamlining Rules
Pretreatment regulations specify:
  Type of sampling method for baseline monitoring reports and 90-day compliance reports, but not for periodic compliance reports
  Minimum of 4 grab samples for pH, cyanide, total phenols, oil & grease, sulfides, and volatile organic compounds
  Composite samples must be flow-proportional unless the Industrial User demonstrates that this is “infeasible”
Final Rule
Clarifies when different types of sampling methods may be used:
  Extends sampling requirements to periodic reports
  Gives POTWs flexibility to determine appropriate number of grab samples to measure pH, Cn, total phenols, oil and grease, sulfides and VOCs
  Clarifies composite samples for Cn and VOCs may be done prior to analysis
  Removes requirement that flow-composite sampling must be “infeasible” in order to allow time-composite sampling (sampling must be “representative”)
Where to find rule changes?
40 CFR 403.12(b), (d), (e), (g), (h)
Notes: Must this rule change be adopted by the CA?
Yes – changes relating to the extension of sampling requirements to periodic compliance reports must be incorporated

## Slide 15: SNC – 4 Primary Changes
Publication (403.8(f)(2)(viiii)
Allow publication in any paper of general circulation within the jurisdiction
Application to SIUs (403.8(f)(2)(viii)
Apply SNC to Significant Industrial Users only
  And to other IUs if they cause pass through, interference, imminent endangerment
Daily Max or Ave. Limits (403.8(f)(2)(viii)(A-C)
Include broader array of numeric or narrative violations
Late Reports (403.8(f)(2)(viii)(F)
Extended 30-day deadline to 45 days
Notes: Must this rule change be adopted by the CA?
Yes – The portion that incorporates the numeric or narrative violations is required because the definition of SNC is expanded

## Slide 16: pH
No change.
IUs are prohibited from discharging at pH < 5.0 without exception

## Slide 17: Equivalent Mass Limits
Pre-Streamlining Rules
For CIUs, 40 CFR 403.6(d) allows CA to impose equivalent mass limits in addition to concentration-based standards where the IU is using dilution to meet standards or where the imposition of mass limits is appropriate
For CIUs, Pre-Streamlining rules do not allow the equivalent mass limit to replace the concentration-based standard
Some POTWs and CIUs argue that using concentration-based standards discourages the adoption of water conservation measures
No federal restrictions on using mass limits for local limits

## Slide 18: Equivalent Mass Limits
Final Rule
Emphasizes that CIU may request equiv. mass limits
Allows POTW to set equivalent mass limits as an alternative to concentration limits
To be eligible for use of equiv. mass limits, CIU must:
  Implements water conservation measures that substantially reduce water use,
  Uses control and treatment technologies adequate to achieve compliance with categorical standards, and demonstrate that dilution not used,
  Provides monitoring data to establish its actual average daily flow rate through the use of a continuous effluent flow monitoring device and its baseline long-term average production rate,
  Demonstrates that it doesn’t have daily flow rates, production rates, or pollutant levels that fluctuate so significantly that establishing equiv. mass limits would not be appropriate, and
  Has consistently complied with applicable categorical standards

## Slide 19: Equivalent Mass Limits
Final Rule (cont’d)
If CA approves eligible CIU’s request, CA then calculates the equiv. mass limits:
  Concentration-based categorical standard × CIU’s actual average daily flow rate × unit conversion factor
Once equiv. mass limit is effective in the CIU’s control mechanism, CIU must do the following to retain coverage:
  Maintain and effectively operate control and treatment technologies adequate to achieve compliance with the equiv. mass limits,
  Record the facility’s flow rates through use of a continuous effluent flow monitoring device,
  Continue to record facility’s production rates and notify CA if rates vary by more than 20 percent from production rates used as basis for equiv. mass limits
  Employ same or comparable water conservation measures used in setting the equiv. mass limits

## Slide 20: Equivalent Mass Limits
Final Rule (cont’d)
After calculating equiv. mass limit, CA must reassess the limit and recalculate as necessary to reflect changed conditions, where the CIU notifies it of a revised production rate
CA may retain the initial equiv. mass limits in subsequent control mechanism terms if:
  CIU’s actual average daily flow rate reduced solely as a result of water conservation methods and technologies,
  Actual average daily flows used for calculating limit weren’t based on use of dilution as substitute for treatment, and
  CIU doesn’t bypass treatment control and treatment technologies
Equiv. mass limits are not authorized for pollutants which cannot be appropriately expressed as mass
(examples: pH, temperature, radiation, etc.)
Where to find rule changes?
40 CFR 403.6(c)(5)
Notes: Must this rule change be adopted by the CA?
No – this provision is optional

## Slide 21: Oversight of Categorical Industrial Users (CIUs)
Pre-Streamlining Rule
All CIUs are considered SIUs
POTW may exclude a non-categorical IU from SIU designation if demonstrates that it has no reasonable potential to adversely affect the plant or violate a standard (SIU based on flow alone)
No flexibility to exclude CIUs from SIU status
Final Rule
3 Oversight Scenarios for CIUs:
  CIUs that are considered SIUs
  Non-Significant Categorical Industrial User (NSCIU)
  Middle Tier CIU

## Slide 22: Comparison of CIU Oversight Requirements
 | Control Mechanism Required? | Minimum CIU Reporting Requirements | Minimum POTW Inspection / Sampling Requirements
Categorical SIUs | Yes | 2 times per year (at a minimum) | 1 time per year
NSCIUs | No | Certification only (no reporting), one time per year | Not required
Middle Tier CIUs | Yes | 1 time per year (if representative of operating conditions) | 1 time every other year

## Slide 23: Oversight of Categorical Industrial Users (CIUs) Non-Significant CIU – Final Rule
To be eligible, the CIU must:
  100 gpd or less daily max. categorical wastewater discharge (cannot be averaged flow)
  Have consistently complied w/ all applicable standards and requirements
  Annually submit certification statement indicating that it continues to meet the NSCIU definitional criteria and that it complied w/ applicable standards and requirements
Requires annual certification statement to be signed in accordance w/ 403.12 requirements
CA required to annually list out which CIUs are considered NSCIUs
CA required to annually evaluate whether each NSCIU has submitted its certification statement and continues to meet the definitional criteria
CA establishes inspection and sampling frequencies
Notes: 100 gpd of total categorical wastewater
Never discharges any untreated concentrated wastewater

## Slide 24: Oversight of Categorical Industrial Users (CIUs) Middle Tier CIU – Final Rule
“Middle Tier” CIU Designation:
  CIU can reduce reporting to one time per year
  (instead of minimum twice per year as SIU)
  POTW can reduce its inspections/samplings to one time every other year (instead of minimum one time per year as SIU)
To be eligible as a “Middle Tier” CIU, the CIU discharges can be no greater than:
  0.01% of POTW’s design dry weather hydraulic capacity, or
  5,000 gpd, whichever is smaller (measured by continuous effluent flow monitor unless CIU is batch discharger)
  0.01% of POTW’s design dry weather treatment capacity
  0.01% of MAHL for any pollutant for which CIU regulated
  CIU has not been in SNC for any time in past 2 years
  CIU does not have daily flow rates, production levels, or pollutant levels that vary significantly that reduced reporting would be non-representative of operating conditions
Notes: Proposed Rule
In section discussing NSCIUs, EPA requested comment on “alternative criteria for determining non-significant status … [such as] the percentage of POTW’s total flow discharged by a particular CIU.”
18 POTW commenters suggested adoption of 3-tier system for CIUs
1st tier – categorical SIUs
2nd tier – non-significant CIUs: discharge less than a percentage of POTW’s design dry weather treatment capacity, design dry weather organic treatment capacity, and MAHL for any pollutant detected at headworks for which CIU is regulated
3rd tier – de minimis CIUs: discharge less than 100 gpd
EPA approved Metropolitan Water Reclamation District of Greater Chicago’s pilot project for the 3-tier system (no longer active)
State comments –
WA – delete word “other”; could be used as a loophole; cutoff should be different for different ELG categories
MN – doesn’t oppose, but would rather see us use “SIU” def. to allow exemptions for categorical SIUs with no potential to harm POTW
MI – supports, but proposes 1000 gpd or any higher cutoff
TX – supports
NJ – supports
WI – raise the cutoff to 500 gpd

## Slide 25: Oversight of Categorical Industrial Users (CIUs)
Final Rule
Where to find rule changes?
40 CFR 403.3(v)(2) – Definition NS CIU
40 CFR 403.8(f)(2)(v)(B) and (C)
40 CFR 403.12(e)(3)
40 CFR 403.12(i) – Annual POTW report

## Slide 26: Questions?
Contact Information:
Jan Pickrel
(202) 564-7904
pickrel.jan@epa.gov
Greg Schaner
(202) 564-0721 or schaner.greg@epa.gov