## Slide 1: This presentation is the Intellectual Property of Wade Research, Inc. This presentation is intended for the use of the meeting attendees only. No part of this presentation may be reproduced or transmitted in any form or by any means, electronic or mechanical, including photocopying, recording, or any information storage and retrieval system, without written permission from Wade Research, Inc. Copyright 2005 by Wade Research, Inc.

## Slide 2: Endocrine Disrupters and Other Emerging Pollutants . . . What’s All the Hype About? The Role of MtBE as an Emerging Pollutant - a Forensic Geochemist’s Viewpoint.
Michael J. Wade, Ph.D.

## Slide 3: MtBE as an Emerging Pollutant
Methyl tert-butylether:
[CH3]3C-O-CH3

## Slide 4: MtBE as an Emerging Pollutant
Why is MtBE considered at this conference to be an emerging pollutant? After all, it has been used since 1979 in the U.S. automobile gasoline supply. So, what is so new about MtBE? Hype, after 2 decades?
Answer: MtBE has proven itself to be impossible to control and, therefore, MtBE presents itself as an ever-changing issue which will be with us for a very long time.

## Slide 5: MtBE as an Emerging Pollutant
Initially, MtBE was approved by the U.S. EPA for use as an additive in the U.S. automobile gasoline market early in 1979.
MtBE is widely used today, albeit there are efforts to have it regulated out of the gasoline supply by state actions around the country.
The problem is that MtBE proved to be impossible to keep out of the environment.
Therefore the regulatory philosophy is if MtBE can’t be controlled, don’t allow it to get to the environment in the first place.

## Slide 6: MtBE as an Emerging Pollutant
From a forensic geochemist’s viewpoint, we should ask . . . how is the MtBE problem coming about?
Leaking gasoline storage tanks? Yes
Gasoline spills? Yes
Vapor phase release? Yes
Co-mingled petroleum products? Some, yes
Exhaust releases? Expect it, yes.
Disposal/release of waste oil? Yes

## Slide 7: MtBE as an Emerging Pollutant

## Slide 8: MtBE as an Emerging Pollutant
BTEX
MtBE
UST
The problem is that once released, MtBE is difficult to control. In groundwater, a dissolved plume can look like:

## Slide 9: MtBE as an Emerging Pollutant
Imagine drawing water downstream from such an influence and new results start to show up in your chemical monitoring program:
MtBE at or slightly above method detection limits starts to show up in your well field or in your incoming water more less consistently, and
Common gasoline hydrocarbons at or below method detection limits may or may not be found consistently.

## Slide 10: MtBE as an Emerging Pollutant
Question: How do you assess changes in the chemical composition of incoming waters?
What are your decision making points?
What’s coming next?
Can we identify sources?
Are your monitoring data reliable?

## Slide 11: MtBE as an Emerging Pollutant
In fact, there may be years worth of existing chemical data that constitute a valuable resource. Speaks to source(s).
After all, the USGS reports that MtBE has gotten into the groundwater in areas of the U.S. which don’t even have MtBE-treated gasolines in use.
We have serious funding and important public health issues riding on your answers.

## Slide 12: MtBE as an Emerging Pollutant
Data reliability is the number one issue. In a world replete with both false positives and false negatives, how does one decide if your analytical monies have been well spent? Can we trust our data?
Therefore, logically we start with the data - not a table of data. What do the data show?
How are the data generated?
The tool of choice - gas chromatography - with a variety of detectors - is where we first look . . .

## Slide 13: MtBE as an Emerging Pollutant
The analytical methods of choice where MtBE data are generated include the following standard methods:
  GC/FID U.S. EPA Method 8100/8015
  GC/PID U.S. EPA Method 8021
  GC/MS U.S. EPA Method 8260
Ah, but there’s a catch . . .

## Slide 14: MtBE as an Emerging Pollutant
From the literature, the likely order that one may establish for the elimination of false reports (positive or negative) include:
GC/FID, which is not as good as . . .
GC/PID, which in turn is not as good as . . .
GC/MS, which seems to be held in higher regard than other methods.
But there’s always that catch . . . cost versus reward . . .

## Slide 15: MtBE as an Emerging Pollutant
Like anything else in life, you get what you pay for:
  If total cost was the issue, with a preference for lowest possible price, you received data that may be considered suspect, depending . . .
  If you concentrated on data quality issues, you advance selected a higher order analysis and you received data, more likely than not, you may rely upon, depending . . .
  Depending what constitutes false positives . . .

## Slide 16: MtBE as an Emerging Pollutant
In pump samples - gasoline not released, not weathered - known interfering hydrocarbons (HC) constitute 10% and 12% by volume, respectively.
For early MtBE-treated unleaded gasolines with volume percents at 2-4%, these HC compounds predominate.
For later RFG MtBE-treated gasolines with volume percent of up to 14%, these HC compounds are at least comparable to the volume % of MtBE.

## Slide 17: MtBE as an Emerging Pollutant
Initially, we may be able to conclude that under gas chromatographic conditions where peak interferences are likely, reported MtBE concentrations might be wrong by a factor of from 0.5 to 5.0.
In the extreme, there may be no MtBE in the gasoline samples at all.
Therefore, at first review, one may reasonably conclude that reports of MtBE have a great potential for not being reliable.

## Slide 18: MtBE as an Emerging Pollutant
At first inspection, simply looking at the analytical method should provide us with our first set of decision points about data reliability.
Except . . . that we have changes in the individual components of gasoline over time once it has been released to the environment that change the chances of success of the analyses for MtBE in groundwater.

## Slide 19: MtBE as an Emerging Pollutant
Reviewing the listed interfering compounds we see that they are lighter molecular weight, appreciable octanol/water partition coefficients, not particularly soluble in water and readily degradable by microorganisms.
Therefore, consideration of the interfering hydrocarbons changes over time.
And the properties of MtBE of high water solubility and low octanol/water partition coefficient work to change the likelihood of finding MtBE in samples as well . . .

## Slide 20: MtBE as an Emerging Pollutant
We can construct a decision matrix that will serve as a guide for the evaluation of MtBE data and the likelihood of false readings
What factors do we consider?
  Initial amount of petroleum released
  Soil conditions - permeability
  Groundwater flow regime
  Time since release
  Analytical method used

## Slide 21: MtBE as an Emerging Pollutant
Little degradation Low permeability Low flow Probable | Much degradation Low permeability Low flow Not so probable
Little degradation High permeability High flow Probable | Much degradation High permeability High flow Not so probable
Probability of False Positive MtBE determination

## Slide 22: MtBE as an Emerging Pollutant
So, the likelihood of a false positive for MtBE is dependent upon the nature of the exposure, the site conditions, the length of exposure to the environment, and the quality of the analytical work.
All such factors should be reviewed before deciding if you can trust your data.
Further, the chemical nature of MtBE can change over time as well - weathering.

## Slide 23: MtBE as an Emerging Pollutant
Weathering of MtBE - isotopic changes
Degradation of organic compounds can be modeled by a first order reaction:
dC/dt = -k Co
with first order rate constant k dependent upon molecular weight (among other factors)

## Slide 24: MtBE as an Emerging Pollutant
Therefore, the lower the molecular weight, the easier the compound is to metabolize.
Given the non-radioactive isotopic distribution of carbon (12C and 13C) and hydrocarbon (H and D) atoms, differences in isotopic composition of MtBE can be used to determine MtBE that has been around a while from MtBE that has been recently released.
Age-dating MtBE contamination. Enrichment.
Study design is important here. Duplication to define natural variability is the issue.

## Slide 25: MtBE as an Emerging Pollutant
Stability of MtBE in aqueous solution
Stability of MtBE is a real issue.
Initial investigations concluded that under aerobic conditions, MtBE is not degraded.
Under anaerobic conditions, not initially certain, but MtBE can be degraded.
Initially, under poorly understood laboratory conditions, MtBE can be hydrolyzed during analysis. Bad data.

## Slide 26: MtBE as an Emerging Pollutant
Recently-discovered problems in analytical methods initially due to no/poor methods validation.
Did the MtBE issue catch the laboratory community - both regulatory and regulated - unaware? Yes . . . without a doubt.
First alarm sounded in late 1990s, almost 2 decades after MtBE was first approved as a gasoline additive by the U.S. EPA.

## Slide 27: MtBE as an Emerging Pollutant
Subsequent literature work has confirmed the validity of the analytical problems.
However, be careful in assessing the impact(s) of such analytical artifacts. Remember grams are not moles.
Subsequent published research has confirmed the natural degradation of MtBE by microbial populations.
Finally, a useful property of MtBE!

## Slide 28: MtBE as an Emerging Pollutant
And now, a word about detection limits:
Just because a laboratory analyst rules out a report of MtBE presence because of detection limit considerations, does it really mean that MtBE wasn’t found?
If a finding of low levels of MtBE is consistent among many samples, what is the environment trying to tell us?
What does consistency really mean?

## Slide 29: MtBE as an Emerging Pollutant
Conclusions
The analytical method chosen does not automatically provide the basis for outright rejection of all MtBE monitoring data.
Consideration of the analytical method can be cost-driven IF other factors are also considered.
Site-specific conditions play a major role in the evaluation of MtBE data.

## Slide 30: MtBE as an Emerging Pollutant
Conclusions
Timing of gasoline release(s) important, gives the environment time to work on the released hydrocarbons and MtBE.
Where hydrocarbon peak interferences are likely, reported MtBE concentrations might be off by a factor of from 0.5 to 5.0.
The likelihood of false positives and false negatives is too high to be ignored.

## Slide 31: MtBE as an Emerging Pollutant
Conclusions
Reliability of the laboratory’s work is fundamental to acceptance of MtBE data.
Stability of MtBE in groundwater as well as in laboratory solutions is real. Early quantitative results may be low due to negative laboratory influences.
Detection limits are a regulatory influence, not a natural geochemical law.

## Slide 32: MtBE as an Emerging Pollutant
Conclusions
Ask the question: What do the data show?
Chemists should review chromatograms, look for consistency, examine how the data were generated.
Remember - behind every analytical report is a wealth of information. Make use of it.
Develop a feeling for your data - either acceptance or rejection.

## Slide 33: MtBE as an Emerging Pollutant
Now, just when you thought you were prepared . . .

## Slide 34: MtBE as an Emerging Pollutant
And, if you thought that was clear, how about . . .

## Slide 35: MtBE as an Emerging Pollutant
Technical Contact:
Dr. Michael J. Wade, Principal Scientist
Wade Research, Inc.
110 Holly Road
Marshfield, MA 02050-1724 USA
Telephone: (781) 837-5504
e-mail: mjwade@waderesearch.com
on the web: http://www.waderesearch.com