## Slide 1: Indianapolis Approach to a Use Attainability Analysis
Jodi Perras, Perras & Associates
Presentation to
NACWA & Wet Weather Partnership Workshop
Chicago, IL
June 1, 2006

## Slide 2: Agenda
LTCP Background
Scope of UAA
Timing of UAA
Three Factors Used & Their Supporting Documentation
Next Steps

## Slide 3: Indy LTCP Background
55.5 square-mile combined sewer area; 740 miles of combined sewers
Small receiving streams
More than 130 combined sewer outfall points
LTCP sent to agencies in 2001; Final approval expected soon
Parameters Requiring a UAA:
  Bacteria
N
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Selected LTCP
Level of Control:
  97% capture along Fall Creek & 95% capture along White River & other waterways (expected to achieve 2 CSO events/ typical year on Fall Creek & 4 events/year on other waterways)
Present Worth Cost: $1.76 billion
20-Year Schedule: Completed by Dec. 31, 2025.
Significant increase over plan proposed in 2001: 85% capture and 12 overflow events per year at a cost of $1.1 billion.

## Slide 5: Scope of UAA
City is seeking a CSO Wet Weather Limited Use Subcategory under Indiana’s recreational standards
Application covers:
  What: Recreational designated use & WQS
  Where: CSO-impacted waterways
  When: Storms greater than the chosen LTCP level of control, after full LTCP implementation
  Duration: Up to 4 days following CSO discharge
Not Addressed: WQS exceedances caused by non-CSO sources or outside CSO events

## Slide 6
Data Collection & Analysis
System Modeling Stream Characterization
Stream Use Survey TMDLs Financial Capability
LTCP Development
UAA Development
LTCP Approval
(state)
UAA Approval
(state)
State Rulemaking
to Change WQS
EPA Approval of
Revised WQS
Post-Construction
Monitoring
& Data Analysis
LTCP
Implementation
Periodic
Re-review
Parallel
Processes
First 5 yrs. of
LTCP Implementation

## Slide 7: Indy UAA Approach Included Stream Use Surveys
Surveys examined:
  Types of use
  Frequency of use
  Number of users
  Popularity of location
  Children vs. adult use
  Historic uses
Surveys found limited recreational uses of CSO-impacted waterways
Fishing along White River
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Stream Use Survey

## Slide 9: Stream Use Map
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Three UAA Factors Used
1. Naturally occurring pollutants prevent attainment of the use; or
2. Natural, ephemeral, intermittent, or low flow conditions or water levels prevent the attainment of the uses, or
3. Human-caused conditions or sources of pollution prevent the attainment of the use and cannot be remedied or would cause more damage than to leave in place.; or
4. Dams, diversions, or other types of hydrologic modifications preclude
use attainment; or
5. Physical natural features of the water body, unrelated to water quality,
preclude attainment of aquatic life uses; or
6. Controls necessary to attain the use would cause substantial and widespread economic and social impact.

## Slide 11: Recreational Use is Unattainable During Large Storm Events
During storm events that cause residual CSOs after LTCP implementation:
  Stormwater will create high stream flows, making them unsafe for recreation
  Non-CSO pollution sources will prevent attainment of recreational standards during & after those events -- even if all CSOs were eliminated
  Controls beyond the selected level of control:
    Will not attain more days of recreational use
    Would cause substantial and widespread social and economic impacts

## Slide 12
Natural Intermittent Flow Conditions
Finding: Instream peak flows are unsafe for recreation
Stream Mile
Streamflow (cfs)

## Slide 13
Natural Intermittent Flow Conditions
Finding: Instream peak flows are unsafe for recreation

## Slide 14: Human-caused Conditions or Sources
Finding: Non-CSO sources prevent full attainment of use
95% Capture
84 84 84

## Slide 15: Human-Caused Conditions: % of Instream Flow From CSOs

## Slide 16: Human-Caused Conditions: Combined & Separate Acreage

## Slide 17: Substantial & Widespread Economic & Social Impacts
Indianapolis gathered data on:
EPA Median Household Income (MHI)
  Projected over 20-year implementation period for service area & subpopulations
Economic Trends in last 4-5 Years
  Unemployment, Population, MHI, Property & Income Tax Collections, etc.
Projected Social Impacts:
  Disruption of streets, historic sites, trails and parks if full sewer separation were required

## Slide 18: MHI Indicator 2005-25
Low Burden
High Burden

## Slide 19: Job Losses By Sector 2001-04
Medical
Wholesale
Banking, Insurance
Retail & Other
Manufacturing
Transportation
2001 2002 2003 2004

## Slide 20: Unemployment Trends 1999-05

## Slide 21: Historic Areas in CSO Area

## Slide 22: Likely Next Steps
IDEM & EPA review for completeness
City answers any questions & provides additional information
IDEM approval of UAA
Rulemaking before Indiana Water Pollution Control Board to create subcategory for designated streams
  Public comment
EPA review & approval of revised use and associated WQS