## Slide 1: How to be “Passionate About Pathogens”
Adrienne Nemura, P.E. Limno-Tech, Inc. (LTI) Ann Arbor, MI anemura@limno.com (734) 332-1200
2006 Clean Water Law Seminar Thursday November 16 Sheraton Boston
Notes: Motivational speaker

## Slide 2: Overview
Why do we care?
What water quality criteria apply?
  Now
  Future
How are models applied to determine if the (recreational) water is safe?
  Conceptual
  Fate and transport
  Risk assessment
Notes: Cattle on ranches
Wild pigs

## Slide 3: Why do we care?
Animal Feeding Operations & Producers
Wastewater Treatment Plants (WWTPs)
Municipalities & Utilities with CSOs, SSOs, and stormwater discharges
Fresh Produce Suppliers/Packagers
Water Treatment Plants (WTPs)
Baby Tucker

## Slide 4: Why do we care?
Recreational water-associated outbreaks increased significantly in 2001-2002 [since 1978]
Mostly gastroenteritis from Cryptosporidium, E. coli, and norovirus
Statistics (2001-2002):
  65 WBDOs
  2,536 ill
  61 hospitalizations
  8 deaths!
(Yoder et. al 2004)
CDC Morbidity and Mortality Report

## Slide 5: (What their side leaves out)
18 of the 30 (60%) gastrointestinal outbreaks were associated with swimming or wading pools
Deaths due to individual cases of exposure to Naegleria fowleri
The common element:
  Presence of diaper-aged children
  Diaper-changing on the beach
  Washing of young children
  Infants & children going swimming with diarrhea!
CDC: don’t open your mouth in the swimming pool!

## Slide 6: Summary of EPA Recommended (Indicator) Bacteria Criteria (EPA 2004, 2006a, 2006b)
 | Geometric Mean (cfu/100mL) | Single Sample Maximum (cfu/100mL) |  |  | 
 |  | Designated Beach Area (75% CL) | Moderate FBCR (82% CL) | Lightly Used FBCR (90% CL) | Infrequently Used FBCR (95% CL)
Entero-cocci (Marine) | 35 | 104 | 158 | 276 | 507
Entero-cocci (FW) | 33 | 61 | 89 | 108 | 151
E. coli (FW) | 126 | 235 | 298 | 409 | 575
For beach closure and notification (not an acute criteria!)
Best estimate of illness rates:
8-10 in 1,000 for freshwater
19 in 1,000 for marine

## Slide 7: Future?
Rapid techniques for measuring indicators
  QPCR (Quantitative Polymerase Chain Reaction) (Brenner et al 2006)
New criteria for specific pathogens?
  Cryptosporidia, Giardia
  Bacteroides
  Enteric viruses
  Salmonella …
Requirements for site-specific risk assessments?

## Slide 8: Modeling
Load-duration curves (not covered)
Conceptual models
Fate and transport of indicator bacteria
  Watershed, sewer system, and river (instream) models
  Statistical models
Risk assessment methods

## Slide 9: Conceptual Model: Croton (NY) Watershed Project
Need to assess relative risk for 12 watersheds
Complexity makes deterministic modeling difficult
Relative risk-ranking used to evaluate potential impact

## Slide 10: Ohio River Model (Demonstration) for ORSANCO

## Slide 11: What River Model Output Really Looks Like
24 Hours Later…

## Slide 12: Output can be processed to evaluate exceedances of criteria

## Slide 13: River (Fate and Transport) Models
Accepted method of evaluating bacteria
  Bacteria load introduced
  Bacteria transported downstream
  Concentration diluted by water from cleaner sources
  Concentration increased due to other sources (sometimes resuspension)
  Bacteria “lost” due to:
    Death by UV
    Settling, etc.
E. coli Decay Rate

## Slide 14: E. coli Decay Rate
Specified:
  Based on instream measurements of E. coli
  Literature
Can vary, generally between 1-2/day

## Slide 15: Statistical Models
Primarily developed for understanding and predicting beach closures
  E. coli = a x E. coli (day before)
        + b x Onshore Wind Speed
        + c x Wave height
        + d x Rain….
Need a high quality, robust data set; experts; trust…

## Slide 16: The risk analysis process LTI / EOA (Adam Olivieri) / Drexel (Chuck Haas)
Hazard Identification
Exposure Assessment
Dose Response Analysis
Risk Characterization
Decision Making - Risk Management
NAS, 1983
Risk Assessment

## Slide 17: Recreational risk assessment for pathogens
Hazard is illness from:
Protozoa: Crypto & Giarda
Virus – Norwalk-like & rotavirus
Bacteria- Salmonella spp. & Shigella spp
Dose-response models are:
Exponential (protozoa)
Beta Poisson (virus & bacteria)
Exposure occurs when:
Recreational users ingest water
(Swimmers ingest a lot, boaters ingest less)
Risk characterization determined by:
Calculation of hazard occurrences based on rates of exposure to pathogens
Evaluation of risk reduction from controls

## Slide 19: References / END
Yoder, J.S., et al. Surveillance for Waterborne-Disease Outbreaks Associated with Recreational Water – United States, 2001-2002. In: Surveillance Summaries, October 22, 2004. MMWR 2004; 53 (No. SS-8): 1-22.
EPA. (2001). Protocol for Developing Pathogen TMDLs, First Edition. EPA 841-R-00-002. Office of Water.
EPA. (2004). Water Quality Standards for Coastal and Great Lakes Recreation Waters; Final Rule. 40 CFR Part 131. Federal Register, Vol. 69, No. 220, pages 67218-67243.
EPA. (2006a). Water Quality Standards For Coastal Recreation Waters: Considerations for States as They Select Appropriate Risk Levels. EPA-823-F-06-012, August 2006.
EPA. (2006b). Water Quality Standards for Coastal Recreation Waters: Using Single Sample Maximum Values in State Water Quality Standards. EPA-823-F-06-013, August 2006.
K. Brenner, et al. (2006c). Rapid Health-Based Method For Measuring Microbial Indicators Of Recreational Water Quality. EPA. http://www.epa.gov/nerl/news/forum2006/brenner.pdf
National Research Council. (1983). “Risk Assessment in the Federal Government: Managing the Process,” National Academy Press, Washington, D.C.
AMSA. (2004). Creating Successful Total Maximum Daily Loads.
Chapra, S. (1997). Surface Water-Quality Modeling. The McGraw-Hill Companies, Inc. NY.
Pappenberger, F., K.J. Beven. (2006). Ignorance is Bliss: Or seven reasons not to use uncertainty analysis. Water Resources Research, Vol. 42, W05302, doi:10.1029/2005WR004820, pages 1-8.

## Slide 20: Use of Models in NPDES Permitting

## Slide 21: Model Reliability vs. Complexity
Infinite Resources
Substantial Resources
Limited Resources
Reliability
Complexity
Where we want to be
<footer>

## Slide 22: Reliable, Accurate Model
Observed Value
Modeled
Value
1:1

## Slide 23: Reliable, Less Accurate Model
Observed Value
Modeled
Value
1:1

## Slide 24: Biased Model (Unreliable and not Accurate)
Observed Value
Modeled
Value
1:1