## Slide 1: Indianapolis: Applying the Guidance: A Practical Approach
NACWA Legal Seminar
November 16, 2006
Joseph Ridge, CDM
Jodi Perras, Perras & Associates

## Slide 2: Outline
Applying the Guidance: A Practical Approach
  Review approach used by Indianapolis in developing affordability analysis
  Describe critical issues with the analysis
Negotiations with the Regulators
  Affordability
  Level of control
  Schedule

## Slide 3: Indianapolis Faces a Significant Financial Challenge
Recommended LTCP included $2.5 billion in improvements (in future dollars)
City had identified an additional $3.0 billion in system needs
  Plant upgrades
  Septic system removal
  Increased sanitary capacity to eliminate/ mitigate SSO

## Slide 4: Economic Factors
Unemployment rate trends over time and compared to national unemployment
Poverty rate trends over time and compared to national and state poverty rates
Population shifts outside of service area to surrounding counties
Property tax collections declining after tax reform law passed

## Slide 5: Financial Planning Has to Answer Two Fundamental Questions
How much are customers going to be required to pay?
How are household incomes going to change over time?

## Slide 6: Developed Projections on a Rate Basis Rather than Static EPA Approach
Determined baseline system costs and how likely to change over 20 year period
  Inflation rates
  New facilities and processes to be implemented and changes in operating costs
  Replacement of facilities and systems that will reach end of useful life
Modeled CIP impacts-- timing of expenditures and available funding options
  Debt service timing based on project cash flows
  Interest rates and debt terms
Projected future household bills and resulting burden
Notes: Key assumptions
Costs will inflate at 3 to 4 percent a year
SRF will finance approximately 10 percent of the LTCP at 2 percent rate
Balance fincance dwith revenue bonds on 20 year 6 percent with 125 percent coverage requirement
Both caapital and operating costs inflation will accelerate during a peak period of cosntruction.

## Slide 7: Projected Revenue Requirements
Notes: Increases estimated at 12 % per year

## Slide 8: Impact on Residential Customers

## Slide 9: Static EPA Approach Doesn’t Acknowledge Complexity of Question

## Slide 10: Financial Planning Approach Facilitated Consistent Analysis of Alternatives
 |  |  | MHI Peak |  |  | 
Program Alternative | Uninflated Cash Flow | City | Center Twp | Monthly Bill-Peak Year | Peak Year | 
Recommended Program | $1,700,000 | 1.7% | 2.8% | $103 | 2025 | 
$1.0 Billion program | $1,000,000 | 1.5% | 2.5% | $91 | 2025 | 
$1.4 Billion program | $1,400,000 | 1.7% | 2.7% | $98 | 2025 | 
$2.2 Billion program | $2,200,000 | 1.9% | 3.1% | $112 | 2025 | 
$3.0 Billion program | $3,000,000 | 2.8% | 4.5% | $156 | 2023 | 
$6.2 Billion program | $6,200,000 | 4.6% | 7.5% | $260 | 2023 | 

## Slide 11: Why Do It This Way?
Enables policy makers and regulators to better understand the dilemmas faced by the utility
  How rapidly will rates increase?
  What impact does shifting the schedule really have?
  How is that rate burden going to impact various elements of the population?
  Is the program financially feasible?

## Slide 12: Key Issues
Identifying long term system costs
  Forecast period is 30 years or longer
  Most utilities do 5 year CIP planning
Developing a reasonable financing plan
  Availability of SRF
  Grants
  Long term interest rates
Customer Base Income Distribution
Economic changes/demographic changes
Balancing need to present conservative case with political concern over obtaining local approval

## Slide 13: Negotiations with the Regulators

## Slide 14: Other Economic Factors
Overall financial pressures on community & its fund balances
Population shifts to surrounding counties
Unemployment trends & details
Sanitary sewer flows and revenue
Impacts on significant sub-populations
  Center Township
  People living below poverty

## Slide 15: Job Losses By Sector 2001-04
Medical
Wholesale
Banking, Insurance
Retail & Other
Manufacturing
Transportation
2001 2002 2003 2004

## Slide 16: Since ‘97, Flows Have Remained Flat
Source: Indianapolis Department of Public Works??? NEED SOURCE

## Slide 17: Where Should the Money Go?
EPA: Focused on 2% MHI and what guidance said Indy could “afford”
  Pushed a “3/2” overflows per year solution that would have cost more than $2 billion
City: Counter-proposed 4 overflows/year at cost of $1.7 billion, arguing that further CSO control not a wise investment
EPA: “Tell us where you’d rather spend the money, if not on CSO control”
Not a fair question!

## Slide 18: Knee of Curve v. Affordability
50 40 30 20 10 0
$3.5 B
$3.0 B
$2.5 B
$2.0 B
$1.5 B
$1.0 B
$500 M
$0
93 percent
95 percent
90 percent
97 percent
99 percent
Days E. Coli >10,000 cfu/100 mL

## Slide 19: Not All Curves Have Good Knees
89 90 91 92 93 94 95 96 97 98 99 100
Percent Capture
$3.1 B
$2.9 B
$2.7 B
$2.5 B
$2.3 B
$2.1 B
$1.9 B
$1.7 B
$1.5 B
$1.3 B
?
?!
?

## Slide 20
Incremental Cost per Gallon
Notes: <number>
<footer>
<header>
<date/time>
This chart illustrates another analysis we prepared for EPA.
The bars represent the marginal cost per gallon captured and treated as you move from one level of control to the next.
For example, the bar labeled “12” shows that we would spend 23 cents per gallon to control CSOs at this level of control.
As we move to 6 overflows per year, the cost of capturing and treating those additional gallons increases to 31 cents, then to 46 cents as we move to 4 overflows per year.
Moving to the EPA 3/2 plan, the incremental cost per gallon increases dramatically to $1.23 per gallon – a 165 percent increase from the city’s plan.
We don’t believe this is a wise or fiscally responsible expense, and we cannot accept it.

## Slide 21
“Pleasant Run Falls” during dry weather
“Pleasant Run Falls” following a storm that EPA wanted the city to capture – at added cost of $270 million.
This storm occurs about three times each decade during the summer months.
Flows Unsafe for Recreation
Notes: <number>
<footer>
<header>
<date/time>
The second issue I mentioned is stream flow above the 3-month storm.
Stream flows vary from place to place, but these photographs show the dramatic difference we see in urban streams between dry weather and wet weather.
The photo on the left shows an area known as “Pleasant Run Falls” during dry weather. On the right of this photograph, you can barely see the trickle of water that makes up Pleasant Run in dry weather.
The photo on the right shows Pleasant Run following a 4-month storm. This is the size of storm that you and EPA want us to control with your plan. What is the benefit of capturing CSOs when the stream is so unsafe for recreation? Is that a wise use of ratepayer funds? We don’t think so.

## Slide 22: Length of Schedule Factors
More than 35 diverse and complex CSO projects to manage over a 55-square mile area
Need to coordinate with over 500 wet-weather projects spread over 350+ square miles
Projects located throughout the city and along many major thoroughfares & commuter corridors; need to coordinate with transportation project planning
Logical order and sequencing of projects is required for many watersheds and treatment plant work
Need operational ability to bring capital projects “on-line”
Need to be responsive to citizen concerns during planning, design & construction

## Slide 23: Construction Capacity Concerns
Program schedule needs to account for:
  Availability of materials, suppliers, trucks, contractors & trained labor
  Availability of quality consultants & engineers to design, manage & inspect projects
Need to communicate & listen to the public before and during construction
More than 100 other Indiana communities will be moving forward with LTCPs in same timeframe
Other major mega-capital projects are planned in Indianapolis, controlled by other entities

## Slide 24
Typical Project Schedule

## Slide 25: Did it Help?
End result:
  Compromise on level of control: City agreed to higher control on Fall Creek because of different knee of curve on that waterway
    2 overflows/year on Fall Creek
    4 overflows/year on remaining waterways
  Didn’t commit to spending on other projects (i.e. septics) as part of settlement
  20-year schedule instead of EPA’s 15 or 16

## Slide 26: Contact Information
Joseph Ridge Vice President CDM (617) 452-6258 Ridgejt@cdm.com
Jodi Perras Principal Perras & Associates (317) 407-0148 perrasjodi@comcast.net