## Slide 1
Call to Action Regarding Triclosan and Triclocarban
Catherine O’Connor, Ph.D., P.E.
November, 2006

## Slide 2: Presentation Overview
General Description of Compounds
Uses, Controversies
Concentrations in MWRDGC’s Influent, Effluent, Biosolids
MWRDGC’s Call to Action

## Slide 3
<footer>
<date/time>
Triclosan
Triclocarban

## Slide 4: Triclocarban
also called TCC, Cutisan, Solubacter, and trichlorocarbanilide) is a trivial name for 3-(4-chlorophenyl)- 1-(3,4-dichlorphenyl)urea
Low water solubility (2 - 4.6 mg/L)
High Kow (4.9)
Environmental Half-Life ~ 120 days soil; 540 day sediment

## Slide 5: TCC: EPA’s High Production Volume Chemical Challenge Program
December 2002 - TCC Consortium submitted Data Available Screening Level Assessment reporting “completeness of knowledge” wrt toxicity, safety
May, June 2003 - EDF, EPA submitted comments
EDF - proposed 0.12 μg/l acute WQC, suggest 0.06 μg/l chronic WQS
EPA - concerned about test procedures that reported ready biodegradation
Report of “readily biodegrades” from 1975 testing

## Slide 6: Triclosan: Antimicrobial Mechanism
TSC binds with enoyl-acter carrier protein reductase enzyme (ENR)
Block enzyme’s effectiveness in fatty acid synthesis
Fatty acid essential for reproducing and building cell membranes
E. coli & Staphylococcus aureus have demonstrated mutated ENR
Pseudomonas aeruginosa has innate resistance, “pumps triclosan out of cell”
Humans do not have ENR enzyme

## Slide 7
  Triclosan
Learn of the health effects of triclosan & antibacterial soap products
THERE IS NO ANTIBACTERIAL SOAP IN THE RESTROOMS AT THE COOTIE CLUB Problems with Triclosan and Antibacterial Products
Regardless, we have all those wonderful antibacterial soaps to help keep us safe from germs, right? Well, no. Antibacterial soap is not a panacea; it's not really even a good thing, at least not the way it's used today.
http://www.grinningplanet.com/2005/10-04/triclosan-article.htm

## Slide 8
Testing Antibacterial Soaps
Laboratory & clinical tests evaluate the effectiveness of antibacterial soaps. Laboratory Tests Laboratory tests measure the ability of the antibacterial ingredient, alone or in a formulated product, to kill a wide variety of microorganisms. In a typical test, millions of microorganisms are exposed to the test sample for a period of time, after which the reaction is stopped and the number of surviving organisms determined. Effectiveness is determined by the number of organisms killed. Clinical Tests Controlled studies are also conducted that simulate various handwashing experiences. Studies indicate that the average level of germs found on skin with regular use of an antibacterial soap is significantly lower than when washing with plain soap.
http://www.cleaning101.com/health/health/cleaninghealth9.cfm

## Slide 9: According to the American Medical Association: "Despite their recent proliferation in consumer products, the use of antimicrobial agents such as triclosan in consumer products has not been studied extensively. No data exist to support their efficacy when used in such products or any need for them ... It may be prudent to avoid the use of antimicrobial agents in consumer products ...."

## Slide 10: Occurrence of Triclosan and Triclorcarban In MWRDGC Influent, Effluent and Biosolids
Analysis at Johns Hopkins University
First samples collected in August 2005 (3-year study)
Results to date (Triclocarban)
  Influent 1.5 - 6.7 ug/L
  Effluent 0 - 0.3 ug/L
  Biosolids 17,400 - 35,700 ug/kg

## Slide 11: Concentration of TCC and TSC at MWRDGC Water Reclamation Plants in Winter 2005

## Slide 12: MWRDGC Call to Action
Letter to EPA Administrator
  Site ES&T Article (Heidler et al., 2006)
  75% liquid soaps, 30% bar soaps contain
  Detectable at all Seven MWRDGC Plants
  ~90% in Biosolids
  No Evidence of Public Benefit
  Biosolids Program at Risk?
  “Urges USEPA to explore prudent limitations to the manufacture and use of these compounds”

## Slide 13: MWRDGC Call to Action (Continued)
Letter to Representatives in Washington
  Biosolids Program: 200,000 DT Annually
  TCC, TCS Concentrate in Biosolids
  Concerns: Antibiotic Resistance
  Toxicity of Breakdown Byproducts
  No Evidence of Public Health Benefit
Urge EPA to Explore Prudent Limitations to Use