## Slide 1: Pretreatment Streamlining
What’s required and what optional provisions can help control non-domestic contributions to your treatment plant
September 28, 2006
David J. Knight P.E.
Washington State Dept of Ecology

## Slide 2: Required Provision 1/6 Slug Discharge Control Plans
New criteria for requiring spill plans (spill could violate a pretreatment standard or requirement).
Integrate review of slug discharge potential into the permitting process (add in permit when a plan is needed). Use fact sheets to explain.
Reviewing spill plans part of normal inspection.
Ensure Ordinance uses new definition and gives needed authority

## Slide 3: Required Provisions 2/6 Sampling and Reporting
Same requirements now apply for initial and periodic sampling
Flow based composites not always required.
Samples must be “representative” (document)
Some samples can be field composited.
Update permit applications, shells, fact sheets and POTW inspection and sampling procedures.
Some ordinances might need to be updated.

## Slide 4: Required Provisions 3/6 Definition of SNC
Adds violations of instantaneous limits, best management practices, and/or narrative limits
Only SIUs must meet Chronic & T.R. criteria
All IUs causing Pass Through, Interference, imminent endangerment, or which adversely affect the pretreatment program can be SNC.
(Optional) Reports < 45 days late not SNC.
Change Ordinance, ERP, Permits, Procedures.

## Slide 5: Required Provision 4/6 How Permits Use BMPs
CA’s may develop BMP’s in lieu of conc. limits.
CA’s must ensure permits require IUs subject to BMPs (in Categorical Standards if no local lim.):
  Comply with applicable BMPs.
  Report on applicable BMP’s.
  Keep records showing BMP’s are employed.
Permitting procedures must clarify the process.
Ordinance may need to provide legal authorities.

## Slide 6: Required Provision 5/6 Who Signs Reports
Both POTWs and IU’s must meet updated requirements of 403.12(l) and (m) for who can sign annual and periodic reports.
“Duly” authorized representative term defined.
Local Ordinances should be amended & permit shell and program procedures modified to describe how the program ensures submittals are properly signed.

## Slide 7: Required Provision 6/6 Who Must Do Resampling
A “common sense” clarification, Why?
The POTW must re-sample if they find a violation. This ensures compliance really met.
If a routine sample has already been taken and it shows a return to compliance, no resampling is needed, but POTW can still do.
The POTW can ask the IU to resample for them
Modify the ERP and oversight procedures.

## Slide 8: Optional Provisions 1/6 Sampling Pollutants Not Present
Exempts Categorical Users from requirements to sample for pollutants in categorical standards which they have shown are not present;
Requires specific documentation to be provided, included in the fact sheet, and maintained by the POTW.
Requires periodic certification and new analysis of raw wastewater each permit cycle.

## Slide 9: Optional Provisions 2/6 Using General Permits
POTWs may issue general permits for certain categories of similar users.
The rule preamble provides good background information on how EPA expects this to be done.
Intended for Categorical Users w/ conc. based limits.
Not intended to limit options for control mechanisms for minor users, which could use this approach.
Update ordinance, permit procedures, program manual

## Slide 10: Optional Provisions 3/6 Using BMPs in lieu of Local Limits
Use “Best Management Practices” in lieu of local limits (for all or certain groups of Users).
Use of BMP’s in ADDITION to local limits to control users not meeting SIU status need only meet the requirements to be part of the approved program.
May require modifications to the Local Limits evaluations, Ordinance, Permitting process, Enforcement, and program procedures.

## Slide 11: Optional Provisions 4/6 Mass Based Limits for Water Cons.
Allows Control Authorities to apply equivalent mass based limits where water conservation is employed.
Several fairly rigorous conditions are included:
  The facility must have a baseline of flow data from continuous flow metering device, put in fact sheet
  The CA must determine that dilution not used, establish a production basis, monitor production
Use requires changes to several program areas.

## Slide 12: Optional Provisions 5/6 Non-Significant CIUs
Control Authorities may categorize users which discharge 100gpd or less of categorical wastewater as “Non-Significant CIU’s”
NSCIU’s require only:
  Provide an annual certification (see 403.12(q)).
  Provide a new permit application every five years.
CA’s must change most program areas.

## Slide 13: Optional Provisions 6/6 Middle Tier SIU’s
Allows POTWs to categorize CIU’s with .01% or less of POTW flow or loadings as middle-tier CIU’s with less self monitoring & oversight.
Eligible if IU was not in SNC (2yrs) & has stable enough operation for representative samples.
Permits must be written so that if eligibility is withdrawn, prior requirements are restored.
Changes required to most program areas (-ERP)

## Slide 14: Removal Credits and Net Gross
403.7 - 1/8 of pretreatment regulations address “removal credits”. Not allowed in Washington
No POTWs in Washington use Net-Gross determinations either (403.15) – Requires IU source water = receiving waters, demonstrate that limits would be met but for pollutants in source water.
“Streamlining” may have done well to eliminate rather than expand seldom used provisions.