## Slide 1: Nonylphenol Ethoxylates in Wastewater Treatment Plants
Henryk Melcer – Brown & Caldwell
NACWA National Pretreatment & Pollution Prevention Workshop New Orleans, LA
October 6, 2006

## Slide 2: Outline
Definitions, characteristics of NPEs, NP
Entry to, and levels in environment
Fate in wastewater treatment plants
Summary

## Slide 3: Definitions
Nonylphenol ethoxylates (NPEs)
  High performance, cost-effective surfactants in laundry detergents, cleaning products
  Used widely in consumer, institutional, industrial and agricultural applications
  High volume use for over 50 years
Nonylphenol (NP)
  Starting material in NPE manufacture
  Intermediate in anaerobic biodegradation of NPE surfactants

## Slide 4: Chemistry
C
CH
CH2
CH3
CH2
CH3
CH2
CH3
CH3
OH
C
CH
CH2
CH3
CH2
CH3
CH2
CH3
CH3
O
(CH2CH2O)n H
NP
NPEs
n=1-100, typically 1-20

## Slide 5: Phys-Chem Properties
Water solubility
  Low for low mole NPEs &NP
  High for high mole NPEs
    Use in detergents
Octanol-water partitioning
  High for low mole NPEs & NP
    Adsorption to sludge, land application, mobility in soil
  Lower for high mole NPEs
Vapor pressure
  Low for NPEs and NP
    Limited emissions expected

## Slide 6: Biodegradation
Literature review finds biodegradation pathway is complex
  Aerobic and anaerobic pathways
  Aromatic ring breaks during biodegradation
  NP/NPE degrade in surface waters, sediments, soils
  NP/NPEs & ether carboxylate (NPEC) degradation intermediates not expected to be persistent
Government assessments conclude NP/NPEs not persistent nor bioaccumulative
  Environment Canada, Washington DOE (2006)

## Slide 7: NPE Entry into Environment
NPE

## Slide 8: Levels in the Environment
Alkylphenols & Ethoxylates Research Council (APERC) conducted extensive literature review of NP/NPE monitoring data
  1990-2005
  19 studies, many by USGS
  Authors provided raw data for analysis
  Manuscript submitted for publication

## Slide 9: Percent Rank NP Concs vs. EPA Chronic WQC

## Slide 10: Aggregate NP Equivalent Concentrations in U.S. Fresh Surface Water (includes NPE)

## Slide 11: Environmental Monitoring Conclusions
Results suggest, on nationwide basis, the likelihood of surface water concentrations exceeding EPA WQC for NP is low

## Slide 12: Fate in POTWs
APERC sponsored report on fate of NP/NPEs in POTWs
Review state of science in 40 years of studies
  Environmental fate
  Laboratory, pilot and full scale WWT systems
Strategies for optimizing plant performance for NP/NPE removal
Review by NACWA, WEF
Publication expected by WEF

## Slide 13: Treatment Technologies Reviewed
Primary clarifiers
Secondary processes
  Activated sludge
  Trickling filters (TF/SC)
  Small scale – lagoons, oxidation ditches, SBRs
New technologies: MBRs, MBBRs, BAFs
Sludge treatment

## Slide 14: Treatability of NPEs – 1
Widely found in municipal sewage
Levels lower than 10 years ago: 100-1000 µg/L to <10 µg/L
  Improved WWT practice
  Pretreatment regulations
  Reduced usage
90-95 percent removals of primary compounds

## Slide 15: Treatability of NPEs – 2
NPE1 & NPE2 often remain after treatment
  High mol NPEs break down to NPE1, NPE2
Formation of carboxylated residues – NPECs
No accumulation of NPE residues in biosolids

## Slide 16: Impact of SRT on Effluent Quality
Benefit of high SRT systems
Move to biological nutrient removal (BNR)
Drewes et al. study based on pilot and full-scale plants in the US

## Slide 17: Optimum AS Operating Conditions
Parameter | Value
HRT (hr) | Up to 20
SRT (day) | > 10
pH | 6.5 – 9.0
DO conc (mg/L) | > 2
Temp (oC) | >12

## Slide 18: Summary
NPE levels in municipal plants lower than 10 years ago: 100-1000 µg/L to <10 µg/L
90-95 percent removals of primary compounds
High SRT systems favor NPE removal
Environmental monitoring shows levels below EPA WQC criteria