## Slide 1: To Separate or Not To Separate The Wisconsin Experience
Ralph Erickson
Madison Metropolitan Sewerage District
Presentation to NACWA Pretreatment Coordinators Conference
October 6, 2006
New Orleans, LA

## Slide 2: Our response might best be made in the double negative
We can’t NOT require dental amalgam separators in dental clinics in our service area
Why? We do not believe that the state will approve our Pollutant Minimization Plan for mercury without having a plan to get 100% of the appropriate dental clinics covered

## Slide 3: Mercury Pollutant Minimization Program (PMP)
1.3 ng/L (ppt) surface water quality standard for protection of wildlife
District effluent 2.4 ng/L (2005), among the best in WI
DNR provision in NR 106 to calculate alternative limit for mercury (P-99 limit)
Conditioned on developing and implementing a Hg PMP
Notes: Very low WQS, one example of PPT, floor tile vs State Indiana
We have excellent effluent quality
Not good enough, our variance by rule requires a PMP and future permits will give us a target P-99 derived limit (<6.0 at this time)

## Slide 4: MadMSD Hg PMP
A WPDES permit requirement, is in our permit currently
Must be approved by DNR
  Submittal by 3/31/07
  Implementation by 9/30/07
DNR guidance manual to assist in PMP development
Notes: Prop: very useful guidance manual, especially for POTWs new to this, but one could argue parts of this are bordering on “regulation by guidance”

## Slide 5: POTW PMP Guidance
EPA V Guidance http://www.epa.gov/r5water/npdestek/npdpretreatmentguidance.htm
WDNR Guidance http://www.dnr.state.wi.us/org/water/wm/ww/mercury/mercury.htm
http://www.ci.superior.wi.us/pmp/pmp_manual.htm

## Slide 6: DNR PMP Guidance Manual
4 primary sectors need to be addressed:
  Dental
  Hospitals/clinics
  Schools
  General industries
Guidance identifies BMP goal and commonly accepted BMPs for each sector
Other sectors: Public, HVAC, Auto Switches, Fluorescent Lamps
Notes: Dental: low hanging fruit, must be grabbed first
Hospitals/clinics: limited sampling shows some very good wastewater and some that might need followup; we’ll require a BMP of sorts from them; other issues between medical facilities and wastewater treatment plants willkeep us in contact
Schools: I welcome advice on how to approach potentially dozens of small business equivalents in the Sciences at the UW. Anecdotally, old timers in labs could be resistant to giving up their mercury-containing equipment
General industry: we do not see much in our sampling

## Slide 7: Dental Sector
BMP Goal-maximize capture/recycle of wastewater mercury
BMPs
  Wisconsin Dental Association BMPs
  PLUS
  Install and maintain amalgam separators meeting ISO 11143 standards
Notes: Leaving other sectors for reporting to you later, dental loadings are our concern today
Common sense BMP activities such as (8 common ones endorsed by ADA): eliminate bulk liquid mercury , capture unused amalgam, proper capture at chair-side traps (PROP)
The one controversial BMP, not written as a BMP activity by ADA, is the operation and maintenance of a dental amalgam separator
PROP

## Slide 10: MadMSD Influent Hg sources (2005 estimates)
Notes: Our estimates, using wastewater sample results where available and estimated sector volume data
Work in mass, in gram amounts
>300,000,000 pounds of wastewater to Nine Springs and ~25 g mercury therein
Note: the classic Industrial Sector, is a sliver requiring little work on the mercury issue

## Slide 11
Notes: Sampling is very difficult to perform within or outside the doors of dental clinics
We have used literature values to estimate the the loadings from ~200 general dentists in our service area
This is a HIGH estimation

## Slide 12
Notes: And the low estimate 11 grams per day

## Slide 13: Common Dental Screens
Vacuum Filter
Chairside Trap

## Slide 14
Amalgam separation device
Vacuum pump
Typical Small Clinic Installation

## Slide 15
Amalgam separation device
Vacuum pump
Large clinic installation

## Slide 16: Current status of amalgam use & control in MadMSD Service Area
Amalgam placement/removal generally limited to general and pediatric dentistry
Voluntary separator installation encouraged, many BMPs probably employed at most clinics
≈ 22% (22 out of 99) of clinics have installed amalgam separators
42 clinics are considering installation
Notes: One year ago, I met with local Dane County dental leadership to describe the wastewater problem and to encourage voluntary installation
Current status: survey results from this summer indicate
80/20 Rule …..Pareto's Principle …last 20% could be costly to work with

## Slide 17: Why Must MadMSD Require Separators?
DNR may not accept BMP with voluntary program not reaching 100% coverage
WI Dentists have stated “tell us what and by when” ; reluctance to buy a product that may not be approved under a future regulation
Notes: This is not as big a deal as it seemed 5 years ago. Market is full of devices, this is happening in many places outside of Region 5 and outside of the USA

## Slide 18: MadMSD options for controlling dental sector amalgam
Option 1 Voluntary program
  Follow WDA BMPs plus install separators
  % of clinics complying will be limited
  DNR unlikely to approve PMP without conditions (e.g. sampling to demonstrate that clinics not installing separators are meeting the 0.02 mg/L SUO limit for mercury)
Notes: Option 1 is our current program with the understanding that DNR may expect a 100% coverage in short order and they might expect that we apply ordinance driven industrial permits to any resisting clinics

## Slide 19: MadMSD options for controlling dental sector amalgam
Option 2 Either/Or program
  Install separators and follow BMPs
  OR comply with SUO limit of 0.02 mg/L Hg
  Sampling required in latter case (employs standard industrial pretreatment techniques)
  Dentists won’t be able to meet 0.02 mg/L limit
  Essentially is a mandatory separator program as dentists comply with ordinance
Notes: Option 2 takes those notions about DNR expectations and codifies it here at the District. Either / Or
The problem with sampling is that there WILL BE violations and compliance problems at most/all dental facilities. The resolution of compliance issues would probably be a pretreatment device = an amalgam separator
Zero of 500 San Francisco dental clinics chose this option
1 0f 89 Rhode Island dental clinics chose this
Zero in the Twin Cities program

## Slide 20: MadMSD options for controlling dental sector amalgam
Option 3 Mandatory program
  Install separators and follow BMPs
  Sampling not required, annual reporting and random inspections ensure proper operation and recycling
  Relatively easy for the District to implement
  Most cost-effective option for District and dental community that results in 100% compliance
Notes: Follow the “norm” and do what other communities are doing
It is sensible and it may cost the least for us and for dental clinics
Levels the playing field; the vendors will come
DNR seems to want the Milwaukee program followed by others in Wis

## Slide 21: Recommendation Recently Made to MadMSD Commission
Mandatory separator requirement
Lowest cost to dental clinics and to District
Notes: Ralph to confirm those costs. The ADA report has two high priced units that are not available in the US.

## Slide 22
Typical costs for clinics
    $700 - $1,700 initial cost to purchase/install
    $300 - $500 annual costs for maintenance and disposal
Notes: Ralph to confirm those costs. The ADA report has two high priced units that are not available in the US.

## Slide 23: Issues ahead of MadMSD
May require revisions to SUO
Provisions need to be made for de-minimus contributions
No guarantee that 1.3 ng/L effluent limit will be met; confidence that influent levels will be lowered
Notes: Ordinance language can be added to Article 5 of the SUO (like Milw did)
and/or
we can place generic BMP language in the SUO that allows facilities to comply with need to reduce pollutants that does the job in lieu of sampling and the traditional pretreatment approach
What is the comfort zone for effluent quality violations? We will have P-99 limits above 1.3 ppt that will be reduced each permit cycle. Violations are guaranteed yet no treatment options to achieve consistent compliance
We are among the best in state right now. Preliminary data shows ferric chloride and tertiary plants may have slightly lower mercury values
IT IS ALL ABOUT THE SOLIDS

## Slide 24: Issues ahead of us, cont.
KIS: annual inspection rate, use web reports, build in efficiencies wherever possible
Costs recovery, if desired, difficult
Reasonable PMP steps still required for other mercury sectors
Notes: Administrative and inspection costs to be incurred by District

## Slide 25: National or Statewide versus Local Separator Programs
In WI, 100 POTWs will need to create mercury PMPs if effluent not <1.3 ng/L
MilMSD SUO for separators might be the standard in WI
We (POTW staff) are the local environmental experts; we know our customers
WDA prefers one community at a time, have agreement in place with DNR to help push BMPs locally

## Slide 26: National or Statewide versus Local Separator Programs
Statewide programs may not provide inspection oversight to protect POTWs
Statewide programs may provide a level playing field for the dental clinics
Does a statewide program create more or less of a “paper tiger” than a local one?
National Program: ADA might push back at EPA on issues of costs and significance of dental mercury contributions in the global or national pool

## Slide 27: WI Experience Tips for Working With Your Dentists
Do: Distinguish their expertise in dental care and prevention and your expertise in deciding what are acceptable discharges and preventing problems at the POTW
Do: Use the preventative care accomplishments in dentistry to highlight pollution prevention successes in wastewater treatment
Do Not: The discussion of health concerns for amalgam is not for the wastewater professional; the discussion of mercury in the aquatic food chain and POTW compliance issues is appropriate
Do: Acknowledge that dental contributions of mercury are a small fraction of the anthropogenic releases to the environment; discuss that in the wastewater field, where we measure grams of mercury, dental contributions are significant
Do: Appeal to the interest of many dentists in fishing, hunting, and boating.

## Slide 28: WI Experience Tips for Working With Your Dentists
Do Not: The discussion of dental healthcare costs and salaries is inappropriate when recognizing that employing BMPs and installing separation equipment costs each practice financially
Do: Share your treatment plant mercury data and dental clinic case studies. Dentists like data and need to know that their efforts do or will make a difference
Do: Work with and seek the support of your local dental leadership to foster a mutually agreeable local program
Do: Create a program that is adaptable to various situations such as huge clinics, old offices, and “green” practices
Do: Generate good will by providing local programs for collection and recycling of amalgam waste, lead foil, and X-ray fixer

## Slide 29: Good Enough?
Mercury results of MadMSD September, 2006, grab sample = 1.37 ng/L (LOD = 0.169, LOQ = 0.563)
Not Good Enough, but we wonder if limit might be met, occasionally, some day
Variance: we are projecting a statistically based “P-99 limitation” under 6 ng/L mercury to be put in next WPDES permit