## Slide 1: Washington D.C.’s CSO Plan: Development to Implementation
Presented to: Wet Weather Partnership
and
National Association of Clean Water Agencies
April 26, 2007
Presented by: Avis Marie Russell, Esq., General Counsel
District of Columbia
Water and Sewer Authority

## Slide 2: What is WASA?
Independent Authority formed in 1996
Formerly Water and Sewer Utility Administration (WASUA) under Dept. of Public Utilities
Services Provided
  Water Distribution
  Wastewater Collection and Treatment
  Storm water Collection and Conveyance
Serves
  District
  Parts of Maryland & Virginia
Wastewater capital program
  Blue Plains $ 1.2 B
  Collection System $ 160 M
  CSOs $ 2.2 B
        Total $ 3.6 B

## Slide 3: The District’s Combined Sewer System
Typically located in older areas of the District
Combined sewer area is about 12,478 acreas or 33% of District
53 CSO outfalls listed in NPDES permit issued by EPA
Combined
Sewer Area
Maryland
Maryland
Maryland
District of Columbia
District of Columbia
District of Columbia
Potomac
River
Anacostia River
Rock
Creek
Potomac River
N
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Blue Plains Wastewater Treatment Plant
Largest advanced wastewater treatment plant in the world
Capacity:
  370 mgd annual average
  1076 mgd wet weather
    740 mgd full treatment
    336 mgd excess flow treatment
Current average annual flow is 330 mgd
Serves about 2 million people
Blue Plains Wastewater Treatment Plant

## Slide 5: Development of LTCP
Started 1998
Draft LTCP June 2001
Comment Period
Re-evaluation based on comments
Final LTCP
2002
Agreement on data set, modeling and approach
Substantial Public Involvement
4 Public meetings
11 Stakeholder mtgs

## Slide 6
Final LTCP: Overview
Combined Sewer Area
Maryland
D.C
Potomac River
Rock Creek
Anacostia
River
Maryland
D.C.
F
F
Piney Branch Storage Tunnel
P
Tunnel Dewatering P.S.
Replace Poplar Point P.S.
P
P
P
Potomac Storage Tunnel
Ft. Stanton CSO Pipeline
Abandon Northeast Boundary Swirl
Rehab Potomac Pumping Station
Rock Creek Regulator Improvements
P
Improvements to Excess Flow at Blue Plains
Low Impact Development-Retrofit at WASA facilities
Separate Luzon Valley
Storage Tunnel
Rehab Main & O Pumping Stations
Rehab Eastside Pumping Station
Tunnels Storage
Anacostia 126 mg Rock Creek 10 mg Potomac 58 mg Total 194 mg

## Slide 7
Consolidation
Combined Sewer Area
Maryland
D.C
Potomac River
Rock Creek
Anacostia
River
Maryland
D.C.
Anacostia Marinas: CSO 006, 016, 017, 018
Georgetown Waterfront CSO 023-028
Separate Rock Creek: CSO 031, 037, 053, 058
Separation
Receiving Water | # Outfalls Eliminated | Cost ($M)
Anacostia | 4 | $30.3
Potomac | 5 | $20
Rock Creek | 4 | $4.6
TOTAL | 13 | ~$55
Final LTCP: Outfall Elimination

## Slide 8: Predicted CSO Overflow Reduction Under LTCP
Item | Anacostia River | Potomac River | Rock Creek | Total System
CSO Overflow Volume (mg/yr) No Phase I Controls Recommended Plan % Reduction | 2,142 54 98% | 1,063 79 93% | 49 5 90% | 3,254 138 96%
# of Overflows/Average Year No Phase I Controls Recommended Plan | 82 2 | 74 4 | 30 1 / 41 | - -
Notes:
1. One overflow/avg. yr at Piney Branch (major CSO), 4 overflows/avg. yr at other small Rock Creek CSOs

## Slide 9: Regulatory Requirements: Overview
LTCP Decree (2 yr negotiation)
Facilities to be constructed
20 yr schedule (subject to modification for changes to financial, technical, and institutional assumptions)
Phase II NPDES Permit & Fact Sheet
LTCP permit compliance:
Divert, capture treat flow rates
Report flows
Overflows allowed for flows beyond LTCP capacity
Post construction monitoring requirements and performance evaluation
EPA/DOH determined LTCP meets WQS and protects designated uses
Issued Together
Provides flexibility to address changing times

## Slide 10: Diagram of LTCP NPDES Permit Flow Based Compliance
Existing CSO Regulator
Exist. CSO Outfall
“A”
Receiving Water
Interceptor
Existing Combined Sewer
New CSO Diversion Structure
New Meter (Typ)
M
“E” MGD Max Rate
Existing Dry Weather
Pumping Station
De-waters Storage in “D” hrs
CSO Storage on Anacostia, Potomac & Rock Creek
M
“B”
“C”
S
Blue Plains AWWTP
“F” MGD, Max Rate
“G” MGD, Max Rate
Excess Flow Treatment
Complete Treatment
002
001
Also flow thru meter at A must be zero in dry weather to preclude DWO
No overflows unless:
Diversions to tunnels at max rate,
Tunnels filled and;
Blue Plains treating at max rates
CSO Storage Facility (Tunnel)
Notes: Permit compliance is not based on achieving 2 overflows/average year or reducing overflow volume to a specified level.
2. Instead, it’s based on flow. We measure the flow captured by the tunnel and demonstrate that we have captured the flow rates required and that overflows don’t happen unless the tunnel is full.
For the permit, overflows are OK if the tunnel is full or if nature produces flow rates that exceed the flow rates that must be captured as listed in the permit.
4. Post construction monitoring will demonstrate whether the plan is performing sufficiently to meet WQS.

## Slide 11: Estimated CSO Reduction over 20-Year LTCP Implementation Period
Inflatable Dams
P.S. Rehab
Early Action Projects
Remainder of LTCP
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: Paying for CSO Control
WASA is seeking Federal funding

## Slide 13: Current Challenges Demonstrate Need for Flexibility in LTCP and Consent Decree Planning and Process
Current Challenges:
  TMDL litigation – “Daily Means Daily”
  New total nitrogen effluent limit for Blue Plains
  Finding alignments for tunnels in urban area

## Slide 14: D.C.- MD - EPA Response to TMDL Decision
Current TMDLs are annual loads for average year in 1988-1990 climate period
Remaining overflows under LTCP meet TMDLs
Permit compliance based on 1988-1990 results
New TMDLs are for TSS and BOD (TMDLs litigated)
TSS TMDL out for Public comment
  Uses 1995-1997 climate period
  Expressed as daily
BOD TMDL due June 2008
No plans to address other TMDLs (e.g. bacteria)

## Slide 15: TMDL Impacts and Uncertainties
LTCP and Permit impacts
  Both annual and daily loads
  Different climate periods for different TMDLs
  Does “daily in a climate period” meet Court’s ruling of “daily means daily”
Uncertainties
  Will “daily in a climate period” be upheld
  Can TMDL compliance work with different bases
  Until TMDLs are settled, how can LTCP proceed
WASA’s current response
  Scaled back LTCP facility planning (but continue to meet consent decree)
  Reviewing LTCP and Permit impacts

## Slide 16: Balancing Nitrogen Removal and Wet Weather Flows
Blue Plains
Complete Treatment ENR
Excess Flow Treatment - Plain Settling
Outfall 001
Outfall 002
336 mgd
740 mgd
1076 mgd
Add TN to Current WW Flow Treatment
Blue Plains
Complete Treatment ENR
Excess Flow Treatment - Enhanced Clarification Technology
Outfall 001
Outfall 002
521 mgd
555 mgd
1076 mgd
Reducing peak flow to ENR reduces cost
High cost to provide ENR for this flow rate
Transfer more wet weather flow to new technology
Peak wet weather flows
Modify WW Flow Treatment, Add Storage & New Excess Flow Treatment Technology
$800 M
Modified approach provides equal or better effluent performance compared to LTCP
Draft plan to modify LTCP/Consent Decree
Balances TN removal and wet weather treatment
Additional Tunnel Storage
555 mgd
225 mgd
$1,287 M

## Slide 17: Impacts of Nitrogen Control Overlaid on LTCP on D.C. Ratepayers Sewer Bill
 |  | 2016 Typical Residential Sewer Bill ($/yr) | Residential Bill as % of Household Income (3) |  | Avg % Increase in Residential Bill 2008-2017
No. | Nitrogen |  | Median Incomes (3) | Lower 20th Percentile Income (4) | 
1 | No additional nitrogen control | $698 | 1.7% | 3.8% | 8.2%
2 | Add TN to current wet weather flow treatment ($1,287 million plan) | $903 | 1.9% | 4.2% | 10.9%
3 | Modify Wet weather flow treatment, add storage & new excess flow treatment technology ($800 million plan) | $832 | 1.8% | 4.0% | 10.2%
Notes:
All based on 2007 CIP (including LTCP)
Cost allocation based on current IMA:
  Nitrogen: DC @ 40%, suburbs @ 60%
  LTCP : DC @ 100%, suburbs @ 0%
Year 2005 median household income = $44,993 per U.S. Census, inflated @ 3% per year
Year 2001 lower 20th percentile household income = $18,000 per U.S. Census, inflated @ 3% per year

## Slide 18: Tunnels Alignments in an Urban Area
Areas of Concern
  Existing residential/commercial development
  Crossing under D.C. subway (WMATA)
  New riverfront development
  Construction areas
Issues to resolve
  Protection of existing facilities
  Public acceptance of permanent CSO facilities
  Lost opportunity (CSO displacing development)
  Land acquisition
  Underground easements
Use best balance of avoidance and technology

## Slide 19: Summary: D.C.’s LTCP Scorecard
Item | WASA’s Target | Formalized
Implementation Schedule | 25 years, locally funded | Consent Decree-20 years, modification for changes, locally funded
WQS and Designated Uses | Watershed/climate period approach; CSOs comply at LTCP control level. Other sources regulated. | LTCP meets WQS and uses in average year based on capacity of Plan
NPDES Permit Compliance | Zero overflows up to capacity of LTCP | Permit requires flow measurement: * Diversion rates * Storage use * Treatment rates Overflows allowed for rates and volumes above capacity of plan
Look ahead issues: Total nitrogen, TMDLs and tunnel siting | Apply flexibility in CSO Policy and Consent Decree to achieve environmentally responsive and economically balanced program | Making good progress, requires continued vigilance