## Slide 1: CSO LTCP Hot Topics
NACWA/Wet Weather Partnership 2007 CSO Workshop Chicago, IL April 28, 2007

## Slide 2: Overview
Dan Markowitz, Malcolm Pirnie
LTCP was never intended to be perfect.
Limitations often ignored during wet weather negotiations.
SSOs should be prioritized with, or in advance of, CSOs.

## Slide 3: Overview (cont.)
Fred Andes, Barnes & Thornburg LLP
Definition of “existing use” may be critical for CSO decisions.
Compliance schedules can be incorporated into CSO permits.
Design storm approach may pose challenges for WQ standards compliance.

## Slide 4: Overview (cont.)
Adrienne Nemura, LimnoTech
Current criteria not well suited for cost-effective CSO decisions.
Decision-makers need to be cognizant of new information.
Post-construction monitoring programs (PCMPs) will be challenging.

## Slide 5: Overview (cont.)
How can we forecast the post-implementation world?
Fred Andes
fandes@btlaw.com
(312) 214-8310
Dan Markowitz
dmarkowitz@pirnie.com
(330) 375-1464
Adrienne Nemura
anemura@limno.com
(734) 332-1200

## Slide 6: 1) LTCP was never intended to be perfect.
Guidance and policy written as iterative process.
Presumptive controls written as a way to get started and see how things work.
Planning process does not require demonstration that water quality will be met at the end of a 20-year planning window.
Consent Orders only one of several implementation methods proposed in guidance.

## Slide 7: 2) Limitations often ignored during wet weather negotiations.
CSO-related water quality impairment assumed.
Benefits assumed achieved by CSO control alone.
Highly variable and statistically weak data.
Economically achievable language in CWA.
Political and development pressures on municipalities.

## Slide 8: 3) SSOs should be prioritized with, or in advance of, CSOs.
Defined in CMOM policy (withdrawn)
  Included basement flooding
  Defined by aging infrastructure and addressable by O&M
Is wet weather SSO different from CSO?
In systems with both combined and separate sewers difference is not clear, discernable, or defined in guidance or rules.
  Lots of arbitrary definitions used
  Water quality contributions ignored since SSO should be “eliminated”
  What is the elimination threshold?

## Slide 9: 4) Definition of “existing use” may be critical for CSO decisions.
In UAA process, can change designated use UNLESS that would remove an “existing use”.
Existing use is defined in EPA rules as a use actually attained after 11/28/75, even if not designated in WQ standards.
  It’s not entirely clear what that means.
  If existing use is defined as “swimming,” and the swimming has to be in waters attaining standards to protect the existing use, then no UAA can be done that would ever allow any remaining CSO discharges.

## Slide 10: 4) Definition of “existing use” may be critical for CSO decisions (cont.).
But why would you define the existing use that way in a CSO situation?
  Don’t need to – instead, should define it more carefully, to include bacterial levels that exist when you swim after CSO events.
If existing use is “swimming in waters with high bacteria levels,” then a CSO LTCP will only improve the situation.
THEREFORE – LTCP with UAA should not have problem showing that existing uses will not be removed.

## Slide 11: 5) Compliance schedules can be incorporated into CSO permits.
Enforcement option for CSOs is based on assumption that if LTCP will take longer than 5 years to implement, cannot be done by permit.
BUT that is not always true.
Compliance schedules are not allowed for WQ-based limits based on WQ standards that are pre-1977, but can be issued for post-1977 standards.

## Slide 12: 5) Compliance schedules can be incorporated into CSO permits (cont.).
Some states have changed from fecal coliform to E. coli since 1977, or are considering making that change.
State has ability, under EPA Star-Kist decision, to provide compliance schedules – CAN be more than 5 years.
Indiana has recently adopted statute providing for long-term compliance schedules – can also be done by rule.

## Slide 13: 6) Design storm approach may pose challenges for WQ standards compliance.
Michigan DEQ developed approach for CSO LTCPs that avoids need for UAA.
Similar approach now being used by Indiana DEM.
Key concepts:
  Retention, and treatment at WWTP, of flows from 1-year, 1-hour storm
  Primary treatment and disinfection of flows from 10-year, 1-hour storm
  Flows in excess of 10-year, 1-hour storm receive treatment that is “feasible” given capacity limits
  NO untreated overflows – but treatment may be less than 30 minutes detention

## Slide 14: 6) Design storm approach may pose challenges for WQ standards compliance (cont.).
Not entirely clear how agency can allow discharges in high-flow events that do not meet WQ standards without need for UAA, so some legal uncertainty.
Indiana DEM tried putting force majeure language in permits to address those discharges, but EPA has not agreed – so agency now using language stating enforcement discretion.
Cost of ensuring that there are no untreated overflows – probably through changes to collection system – can make this option infeasible for communities with more than a few CSO discharge points.

## Slide 15: 7) Current criteria not well suited for cost-effective CSO decisions.
Huge success for WWTP decisions
Imperfect, unclear for wet weather decisions
  Epidemiological studies based on steady-state conditions
    Do not address runoff events
  “Single sample maximum”
    Different interpretations about how to apply
    Interpretation could drive significant expenditures resulting in little to no increase in actual recreational use

## Slide 16: 7) Current criteria not well suited for cost-effective CSO decisions (cont.).
Source: www.nkyviews.com (Campbell County, Beaches)
Tiered uses, and wet weather exemptions, need to be considered.
Notes: Picture is from 1928 of Dayton Beach on the Ohio River near Cincinnati. The water was often crystal clear, there were bath houses, and some of the issues of the day were:
people suing insurance companies because they would get hurt diving in the shallow water
nude swimming during daylight hours ($1.00 fine for first offense, maximum $5.00 fine), and
dogs running loose (penalty- your dog could get shot and you would be billed for carcass removal).
In the 1940s and 50s, the beach was polluted enough with sewage that the US Public Health Service selected it for one of the first epidemiological studies to relate illnesses from swimming to bacteria in the water.
Swimming at this bathing beach, however, soon became moot because the beach disappeared when the Corps dammed the river.
Today, the entire Ohio River is designated for primary contact recreation. CSO communities along the Ohio may not be able to develop affordable LTCPs without designated use reviews.

## Slide 17: 8) Decision-makers need to be cognizant of new information.
WQ standards review & revisions
  Guidance minimal regarding successful recreational UAAs
  “Safety” defined mostly by “acceptable” illness rates based on 1950s data
Chicago study to provide data on secondary contact recreation (SCR)
  Agreement needed over SCR uses (kayaking)
  Acceptable geomean and SSmax?

## Slide 18: 8) Decision-makers need to be cognizant of new information (cont.).
New criteria to be developed after additional research (2012)
  Method 1600 = viable indicators; QPCR = nonviable bacteria (indicative of viruses)?
  Specific pathogens to be evaluated if significant risk
Pellston experts say…
  Animal waste should not be discounted
  Children should not be considered separately
Economics/competitiveness to play a larger role?
Notes: The first two bullets reflect unofficial recommendations from a workshop EPA held in March with experts from all over the world about research questions surrounding development of new criteria. The official report on the workshop is due to be released within the next few months.
On economics/competitiveness, big concern for beaches. What if beach closures continue due to animal waste? What then?

## Slide 19: 9) Post-construction monitoring programs (PCMPs) will be challenging.
Limited experience
Conditions may vary significantly between events and years
Can be difficult to do this right
Performance-based, water quality-based, or both?
Model or data-based or both?
Notes: People think this will be easy but probably most complex.
How to apply with CSO Policy using presumption approach. How to measure? US/DS doesn’t get at continuing presumption approach. CSO communities may jump into RW monitoring without focusing on presumption approach.
Permittees don’t have experience in this.
Guidance only has a few pages on this.
Operate system way you described/designed (capture 85%, limit 4 OFs/yr). Emphasis should be on this.
Receiving water impacts (more difficult, different standards, US/DS, before/after). Knee jerk reaction by EPA that US/DS for bacteria needed to be done (impairment was PCB). Lot of burden for community to do this.
People get hung up on meet WQS. WWTPs don’t do this type of monitoring.
Small discharge to large river. Where should they monitor? Plume hugs bank. Monitor transect? Where you have bridges?
Idea that once you sample a few times, you are done? Do it forever?
RPE- worst case scenario will be off the charts
Permittees have no responsibility over what goes on in stream.
If you go for demonstration approach, what should it be?

## Slide 20: 10) How can we forecast the post-implementation world?
Will different endpoints be acceptable?
  “Swimming in Sewage”
  Emerging contaminants
  Universal health care
Will we ever get rid of Consent Decrees?
What do we tell the public when water bodies remain impaired?
What can we / should we do about global warming?