## Slide 1: Watershed Planning and LTCP Where Are We and How Did We Get Here
Michele M Pla
MPLA Cleanwater Consulting
Wet Weather Conference
Chicago, IL
April 27, 2007

## Slide 2: CSO Policy and Watershed
1989 CSO Policy
1994 National CSO Policy
LTCP
Why Watersheds

## Slide 3: 1989 Policy
Six Controls
Permits Required
Compliance with WQS
Notes: No Road Map – the requirement to meet water quality standards and the lack of a phased and affordable approach made it difficult for agencies to proceed. No Road Map

## Slide 4
Climate which led to the CSO Negotiations in July 1992
Notes: <number>
<footer>
<header>
<date/time>
1989 CSO Policy – An Attempt to break paralysis and gridlock and to move the program forward
Summer of 1990 Syringes on east coast beaches - Front page photos in Time and Newsweek – and outrage across the country – the beginning of the Beaches approach which we have seen since then
Language to eliminate CSOs – In the Senate Bill as a response to what was
Things were bleak – much like what we saw a few years ago on blending.

## Slide 5: SB 1081 Eliminate CSO
Notes: Well the only way to eliminate CSO is to stop the wet weather – many of us, including the CSO Partnership worked with Baucus on this to try and bring some sense to this idea. Jeff Peterson – later of EPA, was the chief of staff and he was pushing this bill – there should be no untreated discharges – no CSO at all – his term – eliminate.

## Slide 6: National Stakeholder Group Purpose
“ To develop a consistent set of criteria with an adequate degree of specificity to be used to determine long term CSO control to be implemented through NPDES permits.”
Notes: Real purpose – stop the paralysis get things moving and make sure that the requirements could be met
Develop an approach that was going to work and get things moving again.

## Slide 7
CSO Problems are
site specific in nature and
solutions should
be site-specific
Notes: <number>
<footer>
<header>
<date/time>
This was an important point that we made during the development of the Policy and it carried over into the preamble of the Policy itself. This is an important point and it impact both the development of a LTCP and the application of a watershed approach.

## Slide 8
Pieces of the CSO Policy
Sensitive
Uses
Nine Minimum
Control
Technologies
Evaluation of a
range of
alternatives to
meet water
quality standards
Long Term Control Plan
Public
Participation
Coordination with
State on WQS
Phased
Implementation
depending on $
Monitoring to
determine
compliance
Characterization
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: CSO Policy Is a Whole Approach
LTCP Cannot be without
Characterization
Sensitive Uses
WQO
Phased Approach
Affordability
Watershed
Notes: What we have partioning the policy – it is meant to work as a holistic approach to CSO control and the intent is to make progress
The NMTs are intended to be implemented and continued – these are not only the technology requirements of the act, but were intended to be implemented quickly to make progress quickly – then the LTCP process would follow.
In fact I would say that many of us had not heard the term “adaptive management” clearly this policy is founded on that principal.

## Slide 10: Not Every Water Body Has the Sensitive Uses
Notes: Our Working group was looking specificically at: Bathing beaches, drinking water intakes, endangered species habitat and shellfish beds – we were considering where these were really present – not as part of the 303(b) designated uses. So – what we are now seeing is that entire rivers and lakes are considered drinking water or bathing. Well – we missed that. Thought that the Bacteria issue would be taken care of at Sensitive Uses. Did not anticipate that meeting the bacteria standard in the waterbody would become the responsibility of an individual CSO community – expect where real sensitive uses exist.

## Slide 11: Long-Term Control Plan
Notes: Experience in CSO Control had already taught us that it takes years and a lot of money to control CSO. We concluded that this control is a journey; we know generally what the destination is still need a plan and then the idea is to follow that plan – the point of the LTCP – was to develop an approach, a schedule and vision – make sure it is affordable and BEGIN – Do not expect that the journey would be completed over night – that every step of the journey would be completely mapped out – improvements and enhancement could be made along the way. Get started as it is a long journey and it is costly.

## Slide 12: Presumption A High Level of Control
Notes: Presumption Approach - presumes compliance with WQ standards.

## Slide 13: Make Your Own Determination with Demonstration Approach
Notes: Demonstration Approach - make your own determination about level of control to meet WQ standards
  allows for site-specific and watershed approach to CSO control
  The demonstration approach was assumed to be more analytical work that would result in less capital and overall more protection – why – because it was assumed to be focused on watersheds and establishing priorities.

## Slide 14: Phasing and Affordability
Notes: Two sides of the same coin – Yes it is about money and time- and the idea that this is a long term plan means that it cannot be implemented all at once – there has to be a recognition of this. – seems obvious but it was groundbreaking at the time.

## Slide 15: What About Water Quality
Water Quality Is Site Specific
Notes: Policy is Clear that WQO should be formulated AT the SAME Time as CSO LTCP – the iterative or adaptive approach is what was intended by the Presumption alternative – do some thing – big and major – check out if you can meet WQS – if not do more – but WQS should not stop us dead – but as we have been saying and as we know – they have stopped us
This means taking into account both the sensitive uses and the beneficial uses – all have a site specific nature to them
Never expected that control of CSO would bring the Boston Harbor, the Pugent Sound, or the San Francisco Bay into compliance with all WQS – so – this is where the watershed approach comes into play

## Slide 16: Watersheds Approach
“The permittee may need to consider information on the contributions and important of other pollution sources in order to develop a final plan designed to meet water quality standards”
CSO Policy, 1994
Characterization Section II C 1
Notes: Always part of the CSO Policy – always intended to be an approach to WQ Compliance.
This one sentence is not a throw away – this was intentionally inserted into the section on Characterization so that we established a watershed context – Nancy said – the upstream stormwater and urban runoff will carry with it bacteria
We were thinking –TMDL approach of a wasteload allocation so that CSO discharges were not totally required to bring a water body into Compliance

## Slide 17
“ …WQS…are not met in part because of natural background conditions or pollution sources other than CSO…”
CSO Policy, 1994
Demonstration Section II 4 b
Notes: Under the demonstration approach – the watershed was intended to determine if you would need a high level of control

## Slide 18: Why Watersheds
Notes: There is a misconception that with capital intensive controls for CSO we can do this make the water clean – just like these two graphics show. Lets talk about reality – a majority of the CSO Communities and CSO discharges are in highly urban areas along urban watershed. These water bodies are valuable to all of us – We want to see restoration of these rivers, estuaries, lakes and stream are what we all desire. The CSO discharges the only discharge.

## Slide 19: Why Watersheds
Notes: This is what we really think will be effective – what will result in real benefits for the water body, which will change some behavior and will be more cost effective and will really focus on long term and adaptive management. – Less costly – lost of other reasons
Is it practical; does it work; can it be done given the NPDES permit regulations and the other requirement of the Clean Water Act

## Slide 20: Approach, Obstacles and Rewards
Paul Freedman – LimnoTech
  21st Century Approaches
LaJuana Wilcher
  Stumbling Blocks or Stepping Stones?
Q/A with Panel and Participants