## Slide 2
Notes: <number>

## Slide 3
EPA Bacteria Standards and Implications for
CSO/Storm Water Sources
TMDLs for Wet Weather Receiving Waters

## Slide 4
Bacteria Criteria

## Slide 5: 1956 Fecal Coliform
Monthly average of 200 counts with no more than 10 percent of all samples over 400
  Most states implemented as a geometric mean/monthly average only
  Some states monthly/weekly (200/400)
  A few monthly/daily max
  Implementation issues all vetted after 50 years of use

## Slide 6: EPA’s New (1986) Bacteria Criteria
However, fecal coliform is a poor indicator of health risk – EPA found NEGATIVE correlation between fecal levels and swimmer illness….
EPA’s 1986 criteria
  Replaces 1956 fecal coliform criteria
  Entero & E.coli found to be better indicators of illness

## Slide 7: EPA’s New (1986) Bacteria Criteria
  1986 Criteria:
    Geometric mean (recreational season) and
    Single sample maximum/upper percentile value
      Enterococcus (ex: 35 geomean; 104 SSM)
      E. Coli (125 geomean 235 SSM)

## Slide 8: Key Implementation Issues
Are criteria scientifically valid?
Is adoption of the criteria required for all states?
Level of protection in terms of swimmer illness
Intended Use of the Single Sample Maximum values
Implications for CSO/Storm Water Control

## Slide 9
Are EPA’s Criteria Valid?

## Slide 10: Are Criteria Scientifically Valid?
Vigorous disagreement between states and EPA over technical merit.
  Really unprecedented State opposition to a new EPA WQS in the past 15 years
Academic community, public health community and research community are split as well.
Epidemiology studies are few and inconsistent about which indicators are best

## Slide 11: Are the Criteria Valid?
Beach states very upset (on written record)
Florida; California; Maryland
Do not want to close beaches based on one sample
Surf zone yields occasional hits for no reason
  EPA all tied up on this
  Geometric mean and SSM values inherently inconsistent (addressed below)

## Slide 12: Are Criteria Scientifically Valid?
Beach Act (Congress) forces EPA to lean on beach/coastal recreation waters (incl. Great Lakes) states to adopt.
2005 EPA promulgates criteria for those states which did not promulgate on their own
State concerns persist but EPA agrees to develop implementation guidance to address concerns and provide state flexibility

## Slide 13: EPA Backing off of State Adoption
EPA finalized implementation guidance in 2006
EPA has initiated new bacterial criteria studies
Pendency of new criteria – including moving away from indicator organisms to actual pathogens – has caused EPA to relax earlier demands that all states adopt the 1986 criteria
If new criteria emerge in the pipeline, states may not have to adopt the 1986 criteria; otherwise EPA will push for adoption as an interim measure

## Slide 14
What About Level of Illness Protection

## Slide 15: Level of Protection – Swimmer Illness
Criteria include range of monthly geometric mean values based upon State views on acceptable number of swimmer illnesses.
EPA Guidance gives states greater discretion in setting levels of swimmer illness protection

## Slide 16
How Should the SSM Values be Adopted and Used?

## Slide 17: Intended Use of the SSM Value
EPA:
“[F]or making beach notification and closure decisions.”
Beach managers may only have one sample….

## Slide 18: EPA’s New (1986) Bacteria Criteria
Science used to develop the Geo Mean
SSM merely a statistical construct
EPA: “the SSMs were not designed to provide any more protection of health than provided by the geometric mean criterion.”

## Slide 19: 1986 Criteria
Imposing SSM value as a daily maximum NPDES permit limit is an approach
“the Agency had not envisioned when it published the 1986 bacteria criteria document….”

## Slide 20: 1986 Criteria
If states decide to impose weekly/daily max limits, they should be calculated in accordance with EPA’s TSD for Water Quality-Based Toxics Control.
EPA: don’t copy SSM as a daily maximum value; instead a proper daily limit must “be based on 30-day average conditions and an understanding of effluent variability.”

## Slide 21: How to Adopt Criteria
Most States simply copied EPA’s criteria and adopted BOTH the Monthly geometric mean and the single sample maximum value
Most did not include implementation language in the regulation

## Slide 22: How to Adopt Criteria
Some addressed implementation:
  Some said the SSM would only be used for Beach notification purposes (DC)
  Others said both would be used
  Others said the Geometric mean would be used unless fewer than five samples were collected in which case the SSM must be met
  Others followed fecal and allowed a percent of monitoring results to exceed the SSM

## Slide 23: How to Adopt Criteria
Others addressed implementation in Guidance or simply through the permits

## Slide 24: How to Adopt the Criteria
Ok to adopt both Geomean and SSM
However, imperative to include implementation language
  Best approach is to use GEO MEAN ONLY for NPDES purposes
Narrative criteria remain to fill any gaps in level of control that State agencies may feel exist in a particular case using the Geometric mean only

## Slide 25: How to Adopt Criteria
This is good advice for all future EPA bacteria criteria….

## Slide 26
Implications for CSO/Storm water

## Slide 27: SSM Does Not Work for CSO/Stormwater
Intermittent wet weather discharges are not consistent with “never-to-exceed” values
The CSO Policy is not consistent with never-to-exceed bacteria values
  Consider the presumptive approach criteria
Impairment decisions should not be based on one sample
  Fecal standard included 10% allowance

## Slide 28: States Struggling with SSM
Indiana adopted e.coli early on and has implemented the SSM as a daily maximum in NPDES permits
  This has led to numerous permit appeals
IN also uses the SSM for making ambient impairment decisions
  This has led to impaired waters listings for bacteria that are overbroad.

## Slide 29: IN Changing its Approach
http://www.in.gov/legislative/register/20061220-IR-327060573FNA.xml.pdf
Specifically, IDEM notes in its proposed Rule:
“For a variety of reasons, many NPDES permits are appealed due to the expected inability to meet the single sample maximum limits for e.coli.”

## Slide 30: IN Changing its Approach
“Due to the nature and limitations of bacterial sampling and analysis, it is not possible for operators of wastewater treatment facilities to ensure compliance with a single sample maximum at all times.”

## Slide 31: Indiana Experience
“[T]he testing methods may produce falsely high values that could place facilities in noncompliance even when the wastewater treatment plant is being operated properly.”

## Slide 32: Indiana Experience
“[M]ost states determine a wastewater facility’s NPDES permit compliance based upon the geometric mean of a minimum number of effluent samples, 7-day averages of samples or by excluding a percent of the data due to testing method variability. Each of these approaches allows wastewater treatment operators to function within acceptable and protective permit parameters without being subject to noncompliance due to the variability inherent in E. coli testing results.”

## Slide 33: Indiana Experience
“[F]ederal guidance related to bacterial water quality criteria does not require or support the use of a single sample maximum for determining compliance with NPDES permits….”
“Specifically, the rulemaking will address compliance with the E. coli limits from wastewater effluent. Sample variability as well as the lack of precision of the current test method can make meeting the [daily maximum] limit difficult.”

## Slide 34: Indiana Experience
IDEM is likely to allow a percent excursion of the daily max value (i.e., no more than 20 percent can exceed….) or a weekly average for e.coli.

## Slide 35: Implications for CSO/Storm Water
Make sure SSM is not applicable for NPDES purposes
If SSM is applicable, this will force numerous standards revisions
  Due to CSO/Storm water
  Natural background
  Otherwise, TMDLs will not be attainable
Using geometric mean plus narratives will MINIMIZE WQS revisions while still yielding high level of CSO control

## Slide 36
TMDL Issues for Wet Weather Discharges
Notes: <number>

## Slide 37: EPA TMDL Requirements
CWA says EPA must develop TMDLs for all pollutants suitable for daily load calculation
  EPA required to publish list of suitable pollutants
EPA never did
1977 EPA was sued in DC District Court; ordered to publish the list
Notes: <number>

## Slide 38: EPA Said the Following
"all pollutants, under the proper
technical conditions, are suitable for the
calculation of total maximum daily
loads."
43 Fed. Reg. At 60,665 1978
Notes: <number>

## Slide 39: What does this mean?
EPA regs reserve to EPA opportunity to make case-by-case determination of suitability for daily loads
  This makes perfect sense given variability of pollutants, receiving waters and sources
  EPA refuses to embrace this argument
Notes: <number>

## Slide 40: Anacostia River TMDL Appeal
Early challenges to non-daily TMDLs resulted in Courts saying “daily” does not mean “daily”
DC Court of Appeals:
  Rejects annual/seasonal TMDL for Anacostia
    “Daily” in TMDL in CWA means “daily”
    See “daily bread” – Cite (incorrectly) to God
    Daily Dr. Rounds
Notes: <number>

## Slide 41: Anacostia River TMDL
  Court wrote that EPA found that
  “all pollutants … are suitable for TMDL development”
  Court held that CWA requires daily loads unless EPA revises regs to say pollutants not suitable
  Law clerk wanted to get to CWA issue of “daily”
  Court should have decided whether the proper conditions existed or remanded for such a determination
Notes: <number>

## Slide 42: Why “Daily” Matters
Critical for CSO
Storm water
POTW flexibility:
  Nutrients (Ches Bay)
NB: Charleston fecal annual load TMDL….
Notes: <number>

## Slide 43: Anacostia TMDL
EPA response:
  We concede
  We will issue guidance that says develop all TMDLs showing DAILY loads
    But then ignore them for permitting purposes in favor of other frequencies (such as annual)
DC WASA files for certiorari before the U.S. Supreme Court
Notes: <number>

## Slide 44: Anacostia TMDL
Wet Weather Partnership and NACWA file amicus brief in support
Court declines to review the case
Did we all miss something along the way?
Notes: <number>

## Slide 45: EPA Should not Abandon Flexibility to Find Technical Conditions Lacking
Case should have been about whether EPA determination that technical conditions were lacking for daily loads was arbitrary and capricious
  Very favorable standard for EPA
  Should have been a winner for EPA
  Would not have reached question of whether “daily” means “daily”

## Slide 46: What does this mean?
WWP/NACWA meeting with EPA (Grumbles et al) March 16 to pressure EPA to revise guidance to allow case-by-case finding that annual loads are not suitable
Calamita:
  EPA 1978 Rule (Under proper conditions) – “Brilliant”
  EPA staff: words are “meaningless”
  EPA staff do not want discretion to avoid daily loads
    EPA usually loves discretion (see bears and honey)
Notes: <number>

## Slide 47: What does this mean?
After beating around the bush, EPA staff are concerned they can’t do TMLs if they say pollutants are not suitable in particular waters/situations
  Discussion with Grumbles that this is not the case
  They did wasteload allocations for multiple dischargers long before TMDLs
  They can do TMDLs for non-impaired waters
  They don’t have non-point source authority so what’s the big deal there?
Either EPA finds a way to do non-daily TMLs or POTWs will likely petition to remove PCBs, Nutrients, bacteria from TMDL program….
Notes: <number>

## Slide 48: What does this mean?
Regardless of ultimate EPA HQ approach, CSO communities and your state NPDES permit agencies should fully memorialize the lack of technical suitability in any TMDL which is not suitable for daily loads
  Make sure the TMDL cites to the 1978 regulation
    Which was cited by the DC Court of Appeals in its decision!
    This remains GOOD LAW
Notes: <number>

## Slide 49: What does this mean?
This will provide a separate legal basis for implementing non-daily permit requirements.
Consistent with EPA 1986 guidance about non-daily TMDLs
WWP/NACWA approach prevents legal limbo for prior non-daily TMDLs
  There are reasons they were done on a non-daily basis
  These affect many of your communities, POTWs and CSO discharges
Notes: <number>