## Slide 1
Presented By:
Clyde Wilber
301 817 3723
Cwilber@greeley-hansen.com
Greeley and Hansen LLC
October, 2004
Simplified UAA’s
Do they exist?

## Slide 2: How Complicated does a UAA need to be?
EPA – WQS Workshop TM 4
  Pennsylvania
New York State
Kansas
Missouri

## Slide 3
EPA WQS Workshop TM4
Guiding Principle
REACH AGREEMENT on the data to be collected, analyses to be conducted and the bases on which to interpret the information BEFORE initiating the analyses and keep everyone informed throughout the process.
Notes: Show Slide 18: Guiding Principle
We will now cover the types of data for evaluating aquatic life and recreational UAAs.

## Slide 4
EPA WQS Workshop TM4
Factors To Consider In Recreation UAA
WATER QUALITY - e.g., bacteria, nutrients
(phosphorus, nitrogen, secchi disc and chlorophyll a),
BOD, total and suspended solids and narrative free
froms (floatables and objectionable deposits).
HOW PEOPLE USE THE WATERBODY
  What type of recreation, how frequently, seasonally or year-round?
SAFETY AND ACCESS
  Do other uses endanger swimmers?
  Do signs or fences restrict or prohibit access?
Notes: RECREATION UAA
Show Slide 19: Recreational UAA
Excessive bacteria and nutrients can make the water unsuitable for recreation as well as aesthetically unpleasant. These are the numeric water quality criteria most likely to be applicable in addition to any narrative criteria.
Primary contact recreation designations and secondary contact recreation designations with bacteriological criteria to protect primary contact recreation, meet the section 101(a)(2) goal use of recreation in and on the water. Primary contact recreation and the applicable criteria should be adopted for any water body where people engage in or are likely to engage in activities that could result in ingestion of the water or immersion. These activities may include swimming, water skiing, kayaking, etc. Some authorized Tribes have adopted a ceremonial use and apply the primary contact bacteria criteria to protection that use.
When evaluating whether a primary contact recreation use is attainable for a particular water body, some States and EPA Regional Offices have developed “protocols” or worksheets for evaluating recreational uses. The worksheet used by two Regional Offices is in Handout 4-5 on page 4-29 of your manual.
Section 131.10(f) specifically allows States to adopt a “seasonal” recreation use and allows less stringent criteria during certain seasons to reflect the lack of use, as long as the less stringent criteria would not preclude its use for recreation in another season. Because there are less stringent criteria for at least part of the year, the WQS regulation requires some defensible justification to show that the use throughout the year is not an existing use, e.g., the water and ambient temperature in International Falls, MN during the winter provides sufficient justification that swimming does not occur.
Some States adopt primary contact recreational uses for all State waters or waters in urban areas or parks, where recreation is likely. Others evaluate site-specific factors such as access, nearby recreation facilities, safety considerations and physical attributes of the water body, such as depth, width, flow, substrate.

## Slide 5: “We have approved 100’s of UAAs in Pennsylvania
This is a rumor
Most are actually Upgrades
Cold to Warm Water Fisheries
  “Get a bit more scrutiny”
  We rejected – but not because it was a downgrade…

## Slide 6: New York State
Urban Tidal Creeks NYC
Secondary Contact
10,000 Total Coliform GM
Letter to the file in last Triennial Review?

## Slide 7: Kansas Department of Health and Environment Bureau of Environmental Field Services
USE ATTAINABILITY ANALYSIS (UAA) FOR PRIMARY AND SECONDARY CONTACT RECREATION

## Slide 8: KDHE
A checklist approach
Water Presumed for WBC

## Slide 10: Existing Use Definition?
Actual Use?
By the Criteria?

## Slide 11: Kansas Primary Contact Existing Use Checklist
Primary contact recreation use shall be considered existing in streams in which indications of the following uses are evident:
swimming
skin diving
boating
waterskiing
mussel harvesting
windsurfing
or which were used for this purpose on or after November 28, 1975 (based on interviews with streamside landowners or other knowledgeable individuals or other dated documentation).

## Slide 12: Kansas Secondary Contact Existing Use Checklist
wading
trapping
Fishing
hunting
or which were used for this purpose on or after November 28, 1975 (based on interviews with streamside landowners or other knowledgeable individuals or other dated documentation).

## Slide 13: Kansas Primary Contact Flow Criteria
An average depth of at least 0.5 meter or a maximum depth of at least 1.0 meter at base flow conditions is considered minimal for primary contact recreation.
Base = Fair Weather Flow

## Slide 14: Kansas Economic Considerations
What activities are apparent along the stream that might impact the water quality of the stream segment, i.e. discharges, cropland, grazing activities,

## Slide 15: KDHE Over 3 years…
Over 600 Waterbodies examined – about 1/3 classified for Secondary Contact

## Slide 16: Missouri Department of Natural Resources Water Protection Program
Recreational Use Attainability Analysis Protocol
Many waters not designated for WBC
UAA before designation?

## Slide 17: Stated Purpose of MDNR UAA WBC Protocol
Comply with federal requirements for the designation of recreational uses,
Assist in identifying waters of the State which support recreational uses,
Respond to the changes in capacity of surface waters to support recreational uses, and/or
Review and modify, as appropriate, the recreational designation of surface waters

## Slide 18: MDNR
Checklists very similar to KDHE - but…

## Slide 19: .
Any interested person may conduct a
Use Attainability Analysis (UAA) and submit the
resulting report to the Department of Natural
Resources (the department). An internal UAA
review committee will meet periodically, as
needed, to review completed UAAs for
accuracy, completeness, and adequacy
MDNR – HELP US!

## Slide 20: MDNR WBC Protocol for the 6
Uses the Federal Register Language – but adds to Natural and Low Flow Criteria

## Slide 21: MDNR – WBC Natural Conditions
When watersheds contain both natural and anthropogenic sources of bacteria, the UAA must separately quantify the bacterial contributions from natural sources and show through science that the natural contribution alone is the cause for the water quality to exceed the bacterial standard.

## Slide 22: Low-Flow Conditions
a maximum depth of at least one (1.0) meter (3.28 feet) in the deepest pool or an average depth of at least one-half (0.5) meter (1.64 feet) must be maintained during base flow

## Slide 23: Observation Checklist similar to Kansas
□ Swimming
□ Skin diving
□ SCUBA diving
□ Tubing
□ Water skiing
□ Wind surfing
□ Kayaking
□ Boating
□ Wading
□ Rafting
□ Hunting
□ Trapping
□ Fishing
□ None of the above
□ Other:
Describe: (include number of individuals recreating, frequency of use, photo-documentation of evidence of recreational uses, etc.)

## Slide 24: But….*
This information is not to be used solely for removal of whole body contact recreation but rather is to provide a more comprehensive understanding of water conditions. Consequently, this information is not intended to directly influence a decision on the recreation use analysis but may point to conditions that need further analysis or that effect another use.

## Slide 25: Are these drive by?
On-site data collection of stream character – intended to be less than a day –
  But may require repeating
Presence of incompatible conditions (Agriculture, discharges) taken into consideration
Depth and Flow alone can preclude the use
Existing Use definition unresolved

## Slide 26: QUESTIONS ?