## Slide 1: City of New York Department of Environmental Protection
October 18-19, 2004
New York City’s Approach and Issues on
Wet Weather Water Quality Assessments,
CSO Long Term Control Plans and the UAA
AMSA / CSOP / EPA Workshop
Chicago, Illinois

## Slide 2: Watersheds Draining to New York Harbor and Adjacent Waters
Watershed for the New York Harbor Estuary Is Large and Includes Portions of Six States
Total Drainage Area: 34,663 sq.mi.
Major Tributaries: 11
Wastewater Treatment Plants: 325
Combined Sewer Overflows: 750
Stormwater Drains: Multiple Thousands
Large Catchment Area for Atmospheric Deposition

## Slide 3: New York City’s Water Pollution Control Infrastructure
NYC’s Wastewater Infrastructure Characteristics:
14 Water Pollution Control Plants (1,300 MGD)
Over 90 Pumping Stations
Majority of Sewers Are Combined
  60% of NYC’s sewered area is serviced by combined sewers
Notes: <number>
<footer>
<header>
<date/time>
NYC’s wastewater infrastructure spans over 6000 miles of sewers and 90 pump stations that distribute on average 1.2 billion gallons per day of sanitary flow to 14 Water Pollution Control Plants (WPCPs). At the WPCPs the sanitary flow receives secondary treatment (85%removal of biochemical oxygen demand (BOD) and suspended solids plus disinfection) and in some instances tertiary treatment for nitrogen removal. Approximately 60% of the sewer system is classified as a combined system, which will be explained on the next slide, with approximately 460 outfalls throughout the City.

## Slide 4: NYC’s CSO Abatement Program
Constructed Spring Creek CSO Retention Tank in 1972 (18 MG)
Nine Minimum Controls Implemented
Reduced Sewer System Bypasses by 99%
Increased Wet Weather Capture from 18% to 72%
City-Wide Floatables Control Program
  Inventory, cleaning & re-hooding of 130,000 catch basins
  End-of-pipe floatables containment of 64% of the CSO area
  4 tributary and 1 open water skimmer vessels
Ongoing CSO Facility Planning
  Three CSO Retention Tanks Under Construction (98 MG total capacity - $757M)
  Three additional CSO retention tanks are being planned
  Other controls – additional wet weather capture, in-line storage, SCADA and regulator automation, plant and pump station expansion, additional floatables control, in-stream aeration, dredging

## Slide 5: Harbor Water Quality Has Benefited From New York City’s Programs
Harbor-Wide Coliform Bacteria Improvements
  No Local Beach Closings in 2004
Harbor-Wide Dissolved Oxygen Improvements
Significant Improvements - Some DO Problems Remain
  Nitrogen and carbon related
  CSO is not a significant contributor
Major CSO Controls Are Not Needed in the Open Waters to Meet Current Standards
2003 New York Harbor Water Quality Report

## Slide 6: Priority CSO Impacts Are in Urban Tributaries
Key Characteristics
  Large highly developed/impervious watersheds
  Minimal dilution in highly modified, confined waters
Impacts and Use Impairments Are Significant
  Aquatic life - hypoxia
  Primary contact - high bacteria
  Aesthetics – floatables/odor
  Sedimentation
Fishable/Swimmable Uses Can Not Be Attained at All Times
  Need to determine the “appropriate” beneficial uses
Knee-of-the-Curve Approach Is Applicable To Determine Appropriate Level of Use
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: NYC’s Approach to CSO Planning
Focus Most Capital Intensive Projects (Retention Tanks) on Tributaries with Real Water Use Problems
Apply Mathematical Models and Good Engineering for the Demonstration Approach to CSO Control
Use the Knee-of-the-Curve Approach To Define Cost-Effective Solutions and Reasonably Attainable Water Uses
Seek To Obtain Public / Regulator Buy-In
Commit Large Capital Resources in the Capital Plan to CSOs
Use the UAA Process to Reconcile Attainable Water Quality with Uses / Goals and Engineering/Economic Realities

## Slide 8: Features of NYC’s USA and LTCP Projects
Significant Resources Committed ($40 M)
  Comprehensive, coordinated effort
  Multi-year planning
Waterbody / Watershed Assessments
  17 urban tributaries
  9 open water areas
Steering Committee Includes EPA Region 2 and NYSDEC
Applies EPA’s Guidance To Coordinate CSO LTCP Planning with WQSRR Process
Data Collection, Modeling and Engineering Evaluations in Each Area
Project Goals
  Identify current and desired water-based and shoreline uses
  Identify appropriate attainable uses with public/community involvement
  Reconcile water quality standards to highest reasonably attainable uses
  Provide basis for potential UAA
  Develop Long Term Control Plans

## Slide 9: Planning End Points Are Still Uncertain
Regional TMDL Analysis Is in Progress for New York Harbor
EPA Recreational Use Criteria (enterococci, possibly others) Are Still Being Promulgated and Developed (BEACH Act)
New York State Water Quality Standards and Criteria Revisions Are In Progress, Not Completed
  Dissolved oxygen marine criteria
  Un-ionized ammonia criteria
  Nutrient criteria
  Enterococci
  Potential local waterbody classification revisions
Water Quality Standards Review and Revision Process Should Be Completed To Define Attainable Uses Before TMDLs Are Completed – This Is Unlikely
Notes: <number>
<footer>
<header>
<date/time>
Even with a more extensive program it is not anticipated that water quality standards will be met at all times in the confined tributaries of NY Harbor. Regulatory alternatives are being pursued such as Use Attainability Analyses (Auras) that may redefine water uses and classifications for certain tributaries to bring NYC in compliance with the Clean Water Act. There may be an opportunity to pursue upgrades in current classifications once planned engineering controls are in place.

## Slide 10: CSO Planning Issues in USA / LTCP Projects
Unattainable Criteria for CSO Receiving Waters
  Dissolved Oxygen – “never less than”
  Enterococci Bacteria – “single sample maximum”
  Floatables/Solids – “no” and “none”
NYC’s Most Expensive Alternative Would Not Assure Attainment of These Criteria
  Extensive tunnel construction in all boroughs
  Massive upgrades to WPCPs where there is no available space
  $8-10 billion in capital cost
  Community disruption impacts / environmental justice issues
  Benefits undefined and probably inappropriate
Need To Understand There Is a Frequency of Occurrence in all Criteria
If Tunnels Were Required, NYC Would Not Be Proceeding with Current Strategy of Retention Tanks and Other Controls

## Slide 11: What Is Needed in New York Harbor To Attain the “Fishable” Goal?
Impacted Tributaries Represent a Small Fraction of the Total Ecosystem by Volume Within New York Harbor:
  Open Waters: 96%
  Tributaries: 4%
New York Harbor Is Adjacent to Other Productive Ecosystems
  Hudson River
  Atlantic Ocean
  Long Island Sound
Atlantic Ocean
Long Island Sound
Hudson River

## Slide 12: Attainability and Costs for Marine Dissolved Oxygen Criteria
Dissolved Oxygen < 2.3 mg/L
Dissolved Oxygen > 4.8 mg/L
2.3 mg/L < Dissolved Oxygen < 4.8 mg/L
DEP Is Nearing a Point of Diminishing Returns on Water Quality Investment and Measurable Benefits
Notes: <number>
<footer>
<header>
<date/time>
While CSO Abatement Planning Continued as part of the 1992 consent order, NY Harbor Water Quality has Improved Drastically over the Past 30 Years. This has mainly been due to NYC Treatment Plants coming on-line (North River and Red Hook), track down and abatement of dry weather overflows and increases in the wet weather flow processed through the WPCPs.
The above slide illustrates the improvements in dissolved oxygen (DO) from 1970 to 2000. As you can see, the area of NY Harbor that is above 4.8 mg/l of DO has drastically improved while most areas in the open water never go below 2.3 mg/l.

## Slide 13: Is Bathing Water Quality Needed Everywhere To Attain the “Swimmable” Goal of the CWA
Primary Contact Water Use Is Attained in Open Waters with Current State Criteria
Access to the Water Is Limited on Much of the Shoreline
New York City Supports Designated Bathing Beaches at Multiple Locations
  No local beach closings in 2004
Coney Island Beach
Designated Bathing Beaches in New York Harbor
Staten Island
Brooklyn
Queens
Manhattan
Bronx
New Jersey

## Slide 14: Significance of Criteria Application Enterococci Bacteria for Primary Contact Recreation
Geometric Mean – Almost
Complete Compliance in NYC Waters
Single Sample Maximum of 104 –
Almost No Compliance in NYC Waters

## Slide 15: Regulatory and Public Water Quality Expectations Should Be Realistic
?
?
Newtown Creek

## Slide 16: Clarify the Knee-of-the-Curve Approach in the CSO Control Policy
KOTC Approach in the CSO Policy Needs To Be Accepted as a Justification for Use Designation if Fishable/Swimmable WQS Can Not Be Attained
Economic Capability Should Not Define the Endpoint Uses; It Is Inconsistent with the KOTC Approach

## Slide 17: New York City’s Needs
New York City Needs as Much Certainty as Possible
  Water quality criteria that are realistically attainable
  Clearly defined targets
  Practical application of fishable / swimmable goals
  UAA criteria / guidance for densely urbanized coastal estuaries
  Clarification of the knee-of-the-curve approach as criterion to define attainable uses
The UAA Process Should Define the Planning Endpoint and the “Final” LTCP Plan Should Be Final