## Slide 2: Put it In the Plan: City of Wilmington Links CSO Controls and Designated Use Reviews
Greeley and Hansen, LLC

## Slide 3: City of Wilmington, Delaware
72,000 residents - largest city in Delaware and in the Christina Basin
1 of 2 CSO communities in Delaware
Bottom of a diverse watershed (agriculture, rural, suburban/urban)

## Slide 4: Wilmington CSS at a Glance
CSS comprises:
  5,700 acres
  190 miles combined sewers
  40 CSOs
Comprehensive NMC program
Recent expansion of WWTP
Calibrated XP-SWMM
Current performance - 75% capture

## Slide 5: Wilmington’s Plan Guided By the CSO Task Force
Statewide stakeholder group recommends an LTCP that:
  Addresses priority CSOs
  Provides 85% capture
  Complies with TMDLs
  Addresses upstream pollution sources

## Slide 6: Evolution of CSO Planning
Early planning focused on 85% capture
  Wet weather exclusion for primary contact use in Delaware WQS
Current planning addresses water quality
  WQS revision removed wet weather exclusion
  “High-flow” TMDL for bacteria

## Slide 7: Wilmington’s Enhanced LTCP Links Projects to WQ Objectives
Build key CSO projects now
Concurrent UAA and WQS Review
  Watershed-wide
  Integrated with TMDLs
Evaluate additional CSO controls and other projects based on outcome of UAA and TMDLs

## Slide 8: Key CSO Projects
Projects that make sense
Address Task Force’s priority CSOs
Provide > 85% capture
$27 million
Build by 2010

## Slide 9: Integrated UAA and TMDL
Coordination Team of key stakeholders
  DE Department of Natural Resources and Environmental Control (DNREC)
  EPA Region 3
  New Castle County, DE
  DelDOT
  City of Wilmington

## Slide 10: Getting Stakeholders Onboard: Not Just “A CSO Thing”
WQS for Enterococcus - 100 geometric mean
Data for CSO waters
  GM range 74 - 255
  90th % range 580 -1900
Data for non-CSO waters
  GM range 55 - 390
  90th % range 400 - 2000

## Slide 11: New Castle County and DelDOT: Stormwater NPDES’s Onboard
“ … TMDL will treat New Castle County as one big point source…”
- EPA Region 3, 2003
Bacteria load reductions in TMDLs for other urbanized areas:
  Culpeper, VA 95% reduction
  Fairfax Co., VA 92% - 98% reduction
  Arlington Co., VA 95% - 98% reduction
  Suburban Boston 72% - 99% reduction

## Slide 12: Getting the State Onboard
99% of river and stream miles don’t support primary contact use
State doing TMDLs
Stormwater NPDES requirements
DNREC looking for model to apply to other watersheds

## Slide 13: Getting EPA Region 3 Onboard
Ideal Case Study:
  Watershed-wide issues
  Multiple sources - multiple impacts
    CSOs, agriculture, suburban/urban stormwater
    - bacteria, nutrients, sediment, habitat
Need to support key leg of CSO Policy - WQS reviews and LTCP planning
Good science for UAA leads to better TMDL and leverages resources

## Slide 14: Intgrated UAA and TMDL: Phase 1
Objective - consensus workplan for scientifically-based UAA and TMDL based on appropriate wet weather water quality objectives
Broad stakeholder effort
  Coordination team - regulators and regulated
  Stakeholder Advisory Group - citizen, special interest groups

## Slide 15: Intgrated UAA and TMDL: Phase 1 Scope
Data assessment and gap analysis - data needs to support:
  UAA based on good science
  Level of attainment of current uses
  Highest feasible, appropriate uses
  TMDL based on good science
Data collection plan for UAA and TMDL

## Slide 16: Intgrated UAA and TMDL: Phase 1 Scope
Stakeholder Advisory Group - establish issues and priorities across watershed
  Where do people want to spend their money
  Puts CSOs in perspective with other watershed issues

## Slide 17: Intgrated UAA and TMDL: Phase 1 Scope
Integrating UAA with TMDL
  Data and analyses for UAA will be improvement over many TMDLs to date
  Ideal - do UAA, revise WQS, do TMDL
  Time sensitive option - phased TMDL implementation with completion of UAA, WQS revision and non-point BMPs first

## Slide 18: Intgrated UAA and TMDL: Phase 1 Scope
Public outreach:
  Develop outreach materials
  UAA/TMDL website
Case Study Report